## Slide 1
Camera Culture
Ramesh Raskar
Camera Culture
MIT Media Lab
Ramesh Raskar
http://raskar.info

## Slide 2
Every Photon has a Story

## Slide 3
What is around the corner ?

## Slide 4
Can you look around the corner ?

## Slide 5
2nd Bounce
Multi-path Analysis
1st Bounce
3rd Bounce
Notes: My idea is to use the multiple bounces of light i.e. echoes of light.
Echoes of sound -> Echoes of light
We all know about echoes of sound.
But sounds travels slow and we can actually hear the echoes
Light travels fast so we need specialized hardware to ‘listen’ to these echoes.
So we end up using light sources and cameras that run at a trillion frames per second (not a million and not a billion, but trillion)

## Slide 6: Femto-Photography (Transient Imaging)
FemtoFlash
UltraFast Detector
Computational Optics
Serious Sync
2011: CVPR (Pandharkar, Velten, Bardagjy, Bawendi, Raskar)
2010: Darpa Young Faculty Award
2010: Lincoln Labs, Campus Collaboration Award
2009: Marr Prize Honorable Mention (Kirmani, Hutchinson, Davis, Raskar, ICCV’2009)
2008: Transient Light Transport (Raskar, Davis, March 2008)
With M Bawendi, MIT Chemistry
Notes: Trillion fps camera (which was previously used only for specialized biochemistry expt)
This new form of imaging is possible by fusion of dissimilar .. A specialized camera previously used only in biochemistry labs and a new computational method that analyzes multiple bounces of light.
I started the project just before I joined MIT in summer 2008.
The hardware we use is borrowed and is in the lab of Prof Bawendi, MIT Chemistry, who is now a collaborator

## Slide 7: Time-Image
Time Profile
for a single pixel
R

## Slide 8
Third Bounce (First bounce not shown)
Space, 640 pixels
Time, ~2ns each row
Time Image of a single point

## Slide 9
Steady State 4D
Impulse Response, 5D

## Slide 10
Streak Photo
L
x
z
s
S
Streak-camera
Laser beam
Occluder
C
B
Echoes of Light
3rd bounce
R

## Slide 11
Capture Setup
Photos from Streak Camera
Hidden Scene
Notes: The reconstruction is very low right now, about 80x80 pixels. So these are just baby steps.
Top: synthetic results based on physically realistic simulations
Bottom: real world results

## Slide 12
Capture Setup
Photos from Streak Camera
Hidden Scene
Overlay
Reconstruction
Notes: The reconstruction is very low right now, about 80x80 pixels. So these are just baby steps.
Top: synthetic results based on physically realistic simulations
Bottom: real world results

## Slide 13
Motion beyond line of sight
Pandharkar, Velten, Bardagjy, Lawson, Bawendi, Raskar, CVPR 2011

## Slide 14
…, bronchoscopies, …
Participating Media

## Slide 15
…, colonoscopies, …

## Slide 16
…, cardioscopies, …

## Slide 18
Each frame = ~2ps = 0.6 mm of Light Travel

## Slide 19
Ripples of Waves

## Slide 21: Femto Photography Time Resolved Multi-path Imaging
Scene with
hidden elements
Raw
Time profiles
t
®
Signal
Proc.
Novel light transport models and inference
algorithms
Photo, geometry, reflectance, beyond line of sight
3D Time images
Ultra fast illumination and camera
5D Capture
Tasks: Non-line of sight, Motion estimation, Material sensing, Volumetric
Inversion: Sparsity, Rank, Bounded Approx, Scene Priors, Transforms
Signal Processing: Compressive, SNR, Bandwidth, Noise models
Illumination: Coding space/time/wavelength, Semicondctr lasers, nonlinear optics
FormFactors: Endoscopy, OCT, Bench-top, Room size, Outdoors
Applications: ComputerVision, MedicalImaging, Biochemistry, Rescue/Planning, IndustrialInspection, Robotics, Spectroscopy
Art/Education
Collaborations Welcome
http://raskar.info
Notes: Here is a road map for this ambitious research project based on time-resolved imaging .. Non line of sight Looking around corner (LaC) is just one example ..
Such Time resolved imaging requires one to develop a completely new set of tool for understanding our world.

## Slide 22
Camera Culture
Ramesh Raskar
Current Team
Moungi G. Bawendi, Professor, Dept of Chemistry, MIT James Davis, UC Santa Cruz Andreas Velten, Postdoctoral Associate, MIT Media Lab Rohit Pandharkar, RA, MIT Media Lab
Otkrist Gupta, RA, MIT Media Lab Andrew Bardagjy, RA, MIT Media Lab
Nikhil Naik, RA, MIT Media Lab Everett Lawson, MIT Media Lab
Ramesh Raskar, Asso. Prof., MIT Media Lab

## Slide 23
Bits
Photons
Computer Vision
Optics
Sensors
Signal Processing
Displays
Machine Learning
Computational Light Transport
Computational Photography
Co-designing Optical and Digital Processing
Notes: My work involves creative new ways to play with light by co-designing optical and digital processing.
My work lies at the INTERSECTION of processing of photons and processing of bits.
At MERL, I transformed the field of computational photography, with key papers and impact on products
At Media Lab, I invented a new field ‘computational light transport’

## Slide 26: Medical Diagnostic Devices
Notes: How many of you own a high end diagnostic instrument
That is not surprising ..
Show multiple complicated electronic medical diagnostic devices

## Slide 27
Notes: Bulky, expensive , trained professionals
Here is a cataract exam with a slit lamp .. A device that hasn’t really changed for decades

## Slide 28
Slit Lamp Exam
Retinal Scan
Notes: And here getting a retinal scan .. But checkout the user interface .. It is a quarter million dollar device but the nurse has to shove my head into the eyepiece

## Slide 29: Reading Charts
Phoropter
Notes: And here to get eyeglasses, I am lost in a phoropter.
This diagnostics while a fine solution in developed countries is not going to scale in developing countries lack of diagnostics .. Millions worldwide are suffering from conditions that have proven treatments
Reading charts appear to be an easy solution, this method has too many problems. Sharpness of legible text is very subjective. The brightness of the chart has to be very carefully chosen otherwise the pupil size will change, increasing depth of field, and allowing user to recognize even lower rows.
The trial lenses + the lens frame the doctor will use also cost over $150
% Reading chart tests involve using a frame or a phoropter. The doctor will swing a sequence of lenses in front of your eye and ask for which lens allows you to see the lower rows on the reading chart.

## Slide 30
Vitor Pamplona, Ankit Mohan, Manuel Oliveira, Ramesh Raskar SIGGRAPH 2010
NETRA Near Eye Tool for Refractive Assessment
Notes: Imagine
We call our tool NETRA: a one dollar clip on eye piece that goes on top a cellphone
near eye tool for refractive assessment
such as nearsightedness/far/astigmatism

## Slide 31
6.5 Billion
people
4.5B
cell phones
2B
refractive errors
0.6B without glasses
NETRA at LVP Eye Institute
Notes: 2 billion people have refractive errors
And half a billion mostly in developing countries worldwide have uncorrected vision that affects their daily livelihood.
Blurry vision leads to illiteracy, unemployement and poverty
More phones that toothbrushes and people who make less than a dollar
They don’t have access to an optometrist or it simply too expensive.
While making and distributing of lenses has become quite easy now, surprisingly there is still no easy solution for measuring eyesight.
Can we use a fraction of the 4.5B cellphone displays to address this problem?

## Slide 32
Diagnostics
Dispensing Glasses
Bulky Equipment , Trained Professionals
Increasingly cheap and easy
Notes: There are two pieces to the puzzle of providing eyeglasses
Diagnostics and dispensing. Over time, the cost of providing eyeglasses has come down dramatically and this shop here in Mumbai can sell distant vision glasses for under $3 and still make profits. But there is still no easy solution for diagnosis ..
Country like India only 10K optometrists for 1B people, and many smaller countries no optometrists at all
While making and distributing of lenses has become quite easy now, surprisingly there is still no easy solution for measuring eyesight.
Can we use a fraction of the 4.5B cellphone displays to address this problem?

## Slide 33: Shack-Hartmann WS
Wavefront aberrometer
Refraction Map using Wavefront Sensor
Notes: The most accurate method is based on a so called SH WS that you would use to get a refraction map before a Lasik surgery. I love this kind of stuff.
My group at MIT Media Lab invents crazy cameras and displays: a camera that can look around corners beyond the line of sight that costs a million dollars, a portable CAT scan machine, glasses free 3D displays ..
But every once a while I like to boil down all the mathematics, optics and theory into something really modest that costs just a dollar
Netra is actually exactly opposite of this complicated laser based sensor
============
It involves shining a laser at the back of the retina and observing the wavefront using a sophisticated sensor.
We ask user to generate a spot diagram. But navigating in a high dimensional space is
challenging so we come up with a strikingly simple approach to let the user interactively create the spot
diagram.
We are first to make connection between Shack Hartmann and Lightfields (and it goes well with recent
work in computational photography about ALF and Zhang/Levoy). Connection to Adaptive optics/
Astronomy.
The way that this device works is that, it shines a lasers in the eye, the laser is reflected in the retina and comes out of the eye being distorted by the cornea. These light rays reaches an array of lenses that focus them to dots in a sensor. The device measures how much this dots deviate from the ideal case. Since it uses lasers, the device is expensive and requires trained professionals

## Slide 34
Shack-Hartmann Wavefront Sensor
Laser
Sensor
Microlens Array
Planar Wavefront
Shack & Platt 1971
Liang et al 1994
David Williams et al, Rochester
Spot Diagram
Notes: For a normal eye, the light coming out of the eye forms a parallel wavefront. The sensor has a lenslet array and we get a spot diagram of uniform dots.
This lenslet should remind you of a lightfield camera, and in fact Levoy and others showed last year that there is a close relationship between the two.
In addition, Zhang and Levoy, plus our grp has shown the relationship between wavefront sensing and lightfield sensing.

## Slide 35
Laser
Sensor
Displacement = Local Slope of the Wavefront
Spot Diagram
Shack-Hartmann Wavefront Sensor
Shack-Hartmann ~ Lightfields
Levoy et al 2009
Zhang and Levoy 2009: Observable Light Field
Oh, Raskar, Barbastathis 2009: Augmented Light Field
Notes: When the eye has a distortion, the spot diagram is not uniform.
And the displacement of the spots from the center indicates the local slope of the wavefront. From the slope one can integrate and recover the wave shape.

## Slide 36
NETRA = Inverse of Shack-Hartmann
Spot Diagram on LCD
Cell Phone Display
Eye Piece
Notes: NETRA uses an exact inverse of this sensor. We get rid of the laser and we instead show the same spot diagram in a cellphone display. For normal eye, it will appear as a dot to the user.
And then we replace the sensor for a light field display. If the user sees a single red dot, he does not need glasses, but if he sees more than one, he interacts with this display.

## Slide 37
NETRA = Inverse of Shack-Hartmann
Spot Diagram on LCD
Cell Phone Display
Eye Piece
Notes: NETRA uses an exact inverse of this sensor. We get rid of the laser and we instead show the same spot diagram in a cellphone display. For normal eye, it will appear as a dot to the user.
And then we replace the sensor for a light field display. If the user sees a single red dot, he does not need glasses, but if he sees more than one, he interacts with this display.

## Slide 38
Spot Diagram on LCD
Inverse of Shack-Hartmann
User interactively creates the Spot Diagram
Displace 25 points
Notes: For eye with distortion, the user will interactively displace the 25 points so that he will see a single spot. Of course changing 25 spot locations is cumbersome, but we realize that there are only 3 parameters for eye-prescription and we help the user navigate thru this space efficiently.
But if you think about these theory, you will realize that we have the dual of the shack-hartmann. First we though out the laser.

## Slide 39
Spot Diagram on LCD
Inverse of Shack-Hartmann
User interactively creates the Spot Diagram
Displace 25 points but 3 parameters
Notes: For eye with distortion, the user will interactively displace the 25 points so that he will see a single spot. Of course changing 25 spot locations is cumbersome, but we realize that there are only 3 parameters for eye-prescription and we help the user navigate thru this space efficiently.
But if you think about these theory, you will realize that we have the dual of the shack-hartmann. First we though out the laser.

## Slide 40
Spot Diagram on LCD
NETRA = Inverse of Shack-Hartmann wavefront sensor
User interactively creates the Spot Diagram
1. Displace 25 spots with smart UI
CellPhone LCD
EyePiece
2. Displace spots till single dot perceived
Notes: Netra is based on a light wavefront sensor but acting in reverse.
A traditional wavefront sensor, called Shack Hartmann sensor involves shining lasers into the eye and using a high quality detector to record reflected light.
Netra is basically the inverse of such wavefront sensor. We ask the user to manipulate patterns on the LCD screen so that the user perceives only a single dot at the end.
For eye with distortion, the user will interactively displace the 25 points so that he will see a single spot. Of course changing 25 spot locations is cumbersome, but we realize that there are only 3 parameters for eye-prescription and we help the user navigate thru this space efficiently.
But if you think about these theory, you will realize that we have the dual of the shack-hartmann. First we though out the laser.

## Slide 41
Spot Diagram on LCD
NETRA = Inverse of Shack-Hartmann wavefront sensor
User interactively creates the Spot Diagram
1. Displace 25 spots with smart UI
CellPhone LCD
EyePiece
2. Displace spots till single dot perceived
Notes: We ask the user to manipulate patterns on the LCD screen so that the user perceives only a single dot at the end.
The number of clicks it takes to align in each directions gives us your complete spherical and cylindrical parameters
==============
Netra is based on a light wavefront sensor but acting in reverse.
A traditional wavefront sensor, called Shack Hartmann sensor involves shining lasers into the eye and using a high quality detector to record reflected light.
Netra is basically the inverse of such wavefront sensor. We ask the user to manipulate patterns on the LCD screen so that the user perceives only a single dot at the end.
For eye with distortion, the user will interactively displace the 25 points so that he will see a single spot. Of course changing 25 spot locations is cumbersome, but we realize that there are only 3 parameters for eye-prescription and we help the user navigate thru this space efficiently.
But if you think about these theory, you will realize that we have the dual of the shack-hartmann. First we though out the laser.

## Slide 42
300+ DPI LCDs
Notes: This is mobile phones today but was not possible even 3 years ago
The reason is phone makers are rapidly increasing the resolution of the screens
Why because we all want to watch out favorite episodes of lost and desp housewife in HD
The pixel pitch is now down to about 25 micrometers, half the width of a human hair
At that resolution we can cleverly exploit the phone as a scientific instrument
So pl go and watch more HD content and play HD games and help build the next mobile diagnostic device

## Slide 43: NETRA Worldwide
Notes: Thanks to the portable, no mechanically moving parts, and low cost, we have received a tremendous response in a very short time. Netra is working with NGOs in more than a dozen countries, collaborating with eyeclinics, research centers and glasses-makers. Plus multiple IRB approved trials.
And as a professor what delights me is that my students are writing a
series of prestigious academic papers in the geekiest of journals

## Slide 44
Kenya
Thermometer for Eye
Notes: Blurry vision is not life threatening but often gets overlooked
We can give children a shot at decent education with early diagnostics
In that sense, Netra is a thermometer for the eye, and one can check regularly as the child is growing up
Video game

## Slide 45
India
Notes: Vision is important for day labor for his employment

## Slide 46
Brazil
Notes: And sometimes its just that important to be able to watch Ronaldinho kick that soccer goal

## Slide 47
Clinical Testing Partners

## Slide 48
Awards and Selection
VodafoneFoundationWinner$300K prize
NASA/USAID Launch Top 10 Innovators
World Bank 3 selected global health inv
Google Innovation
Deshpande Ignition Grant
MIT IDEAS (#2 award)
MIT 100K (dev finalist)
International Space Station evaluation
Validation
0.09 D : objective precision
~ 0.5 D: subjective trials
0.3 D: IRB approved wet-studies (Prelim data)
Academic Scientific Papers
SIGGRAPH 2010
Frontiers in Optics
Am Acad of Optometry (AAO)
Netra in dozen+ countries
India
Kenya
Selection for Global Health Events
Notes: Netra is a beautiful match of deep theory, simplifed down to a $1 device and a very important global health problem.
It has received several awards (prestigious Vodafona Challenge award #1 for $300K)
It has been validated with IRB approved studies. Picture on top right is trials in LV Prasad eye institure in India.
Netra algorithms and research has been published in major journals of the field after academic peer review.

## Slide 49: Hardware App Store
Notes: We all know about software app store, but now we are entering an era of hardware app store where a dollar or two clip on created by developers will be useful for health, productivity, entertainment and education.
Not just a communication or computer device

## Slide 50: Mobile Mates for Health
Notes: Mobile mates: cheap device on a phone that allows diagnostics in remote
parts of the world, bring them to doorstep/portable
You may have seen devices attached to the phone to provide service but here the phone is just data collector and computer.
(Show example of devices where medical device is simply connected to phone)
My aim is to convert the myriod of sensors embedded in mobile phones into a scientific instrument

## Slide 51
Notes: I am excited about creating mobile mates for health, where the phone is not just a comm device or computer but is actually a scientific instrument.
Exploiting all the great I/O components that are being crammed into the phone.
http://www.i-micronews.com/lectureArticle.asp?id=5147

## Slide 52
Slit Lamp Exam
Cataract
Notes: When we talk to our NGO partners, they wanted us to solve cataract screening as that is the leading cause of preventable blindness.
But seems quite challenging to compete with a slit lamp exam.
Cataract leads to blindness and often lazy eye
Because there is no automated way to find cloudiness, doctors use subject analysis. But we think individuals are best suited.
Power for user intelligence can overcome very cumbersome and expensive devices.
But unlike other condition eye screening is quite challenging.
Modern solutions may provide students a fighting chance is a very rewarding.

## Slide 53
CATRA: Cataract Screening Tool
Vitor Pamplona Erick Passos Jan Zizka Manuel M. Oliveira
Everett Lawson Esteban Clua Ramesh Raskar
Notes: Well we have another mobile mate called CATRA that looks very similar but used very different optics and algorthms
Like a radar for the eye

## Slide 54
CATRA: Radar for Cloud Cover
Moving
patterns
on Screen
Cell Phone Display
Pinhole
Lens
Notes: Catra is like a radar for your lens, scanning to find cloud cover
NETRA uses an exact inverse of this sensor. We get rid of the laser and we instead show the same spot diagram in a cellphone display. For normal eye, it will appear as a dot to the user.
And then we replace the sensor for a light field display. If the user sees a single red dot, he does not need glasses, but if he sees more than one, he interacts with this display.

## Slide 55
Notes: And we can not only screen but give you a full map of the blocking and scattering in the lens, here performed by LVP in India

## Slide 56: Mobile Mates for Health
Notes: Refraction .. Cataract .. Mobile mates for health ..
If you get the right mobile mate, how many of you will have a high end medical instrument ..
Now .. That is not surprising either ..

## Slide 57: Eye is a Mirror of Health
Notes: Why start with the eye?
Eye is a mirror of general health.
Ocular manifestation of systemic diseases such as diabetes, hypertension, infections and metabolic disorders is well known.
Like a thermometert, people are in charge of their own health although it does not give prescription

## Slide 58: NETRA: Eye Test on a Mobile Phone
Device without moving parts or lasers
Inverse of Shack-Hartmann wavefront aberrometer
IRB approved trials: good accuracy
  Myopia, Hyperopia, Astigmatism (2009)
  Cataract (2010)
  Retinal Scans (2011-)
  600 Million without corrective glasses
  250 Million with undiagnosed cataracts
  Huge impact on literacy, employment, poverty
  $1 cost, easy to deploy
  http://EyeNetra.com
http://EyeNetra.com
Notes: Summarize:
Netra provides a unique solution with no mechanically moving parts.
Netra is possible because the pixel pitch (resolution) of mobile phone LCDs is now down to 25 micrometer. Which means the LCD on mobile phones can be used to build scientific instruments.
In the future, we are going to puruse a range of activities in unsual low-cost and portable solution for eye-care.

## Slide 59
Notes: Just think about it, over 4 billion people will soon be carrying a high end medical instrument if we can just create the right mobile mate.
Join us as designers technologists biologists social entrepreneurs .. To take affordable diagnostics everywhere with next generation of mobile mates.
Netra is the beginning.
====================
Using a thermometer as an inspiration, the NETRA team aims to empower hundreds of millions with portable devices.

## Slide 60
After X, what is neXt
How to Invent?
Ramesh Raskar, MIT Media Lab
Full Presentation at
http://www.slideshare.net/cameraculture/raskar-ideahexagonapr2010
Notes: Six ways of coming up with new ideas based on an idea ‘X’.
Ramesh Raskar Associate Professor
MIT Media Lab
http://raskar.info
http://cameraculture.info
Full Presentation at
http://www.slideshare.net/cameraculture/raskar-ideahexagonapr2010
http://raskar.info
http://cameraculture.info

## Slide 61
Xd
X++
X
X+Y
X
X
neXt
Ramesh Raskar, http://raskar.info
Full Presentation at
http://www.slideshare.net/cameraculture/raskar-ideahexagonapr2010
Notes: Full Presentation at
http://www.slideshare.net/cameraculture/raskar-ideahexagonapr2010

## Slide 62: Heilmeier's Questions
What
  What are you trying to do? Articulate your objectives using absolutely no jargon.
Related work
  How is it done today, and what are the limits of current practice?
Contribution
  What's new in your approach and why do you think it will be successful?
Motivation
  Who cares?
  If you're successful, what difference will it make?
Challenges
  What are the risks and the payoffs?
  How much will it cost?
  How long will it take?
Evaluation
  What are the midterm and final "exams" to check for success?
Why now? (why not before, what’s new that makes possible)
Why us? (wrong answers: I am smart, I can work harder than others)
http://en.wikipedia.org/wiki/George_H._Heilmeier#Heilmeier.27s_Catechism
Notes: http://en.wikipedia.org/wiki/George_H._Heilmeier#Heilmeier.27s_Catechism

## Slide 63: Great Research: Strive for Five
Before Five teams
  Be first, often let others do details
Beyond Five years
  What no one is thinking about
Within Five layers of ‘Human’ Impact
  Relevance
Beyond Five minutes of description
  Deep, iterative, participatory
Fusing Five+ Expertise
  Multi-disciplinary, proactive
Notes: = If more than five teams in the world are doing the same research, don’t do it.
= If you disappear for five years, will someone do it anyway? Then your idea is not that great anyway.
= Can you explain your work in five sentences how it will impact human life?

## Slide 64: The Full MIT Innovation Ecology
Basic+Applied Research
Commercial Promise & Viability
University Spin-Off
Emerging Growth
Established Company
Support / Alum Offices:
Academic / Research Offices
Student / Informal Organizations

## Slide 65: Action Labs @ MIT Both For-Credit Curricular & Non-Credit Extracurricular Offerings
Basic+Applied Research
Commercial Promise & Viability
University Spin-Off
Emerging Growth
Established Company
Tiger Teams
S-Lab
D-Lab Energy, ICT, Health, Cycles, Design…
MarketLabs
New Enterprises
Media Ventures
D-Lab Development Ventures, Dissemination
Imaging Ventures
VentureSIGs
Africa Health Delivery Lab
India Lab
China Lab
Tech Testbeds
Leadership Lab
T h e M I T I n n o v a t I o n P I p e l I n e
Neuro Ventures

## Slide 66
Phone = Scientific Instrument
Theory of Rays / Waves
LCD Display = Camera
Looking around corners
Notes: Goal is to create super-human vision: super-human abilities to visually interact with the world via cameras that can see the unseen and displays that can alter the sense of reality. But I build fundamental theories and tools rather than focusing on a single goal or application.
Teaser slide: (overview of research) cameras, displays, medical devices and theory of light
How can we create cameras that can look around corners
How can we build displays that also act like large lensless cameras
Can we bridge the ray versus wave nature of light
And how can be provide care in remote parts of the world by converting mobile phones into scientific instruments

## Slide 67
Cameras, Medical Tools, Future Devices
  Theory, Modeling, Optical+Mathematical insight
New Fields
  Femto-photography
    Sparsity, rank, priors
New Purpose
  Disruptive mass-use tech for social impact
  Netra, Cataract, Retinal scans
  $1M -> $1
New Insights
  Idea Hexagon
  Strive for Five
Ramesh Raskar http://raskar.info fb.com/rraskar
Bits
Photons
Computer Vision
Optics
Sensors
Signal Processing
Displays
Machine Learning
Computational Light Transport
Computational Photography
Notes: My new field Computational Light Transport is for creating super-human visual abilities: camera that can see around corners, devices that can see inside our bodies (Netra), 3D displays that are hyperrealistic, barcodes that shrink to a dot but still readable etc.
The empirical nature of the research means I must go and explore multiple directions rather than one narrow application or technique.
Lot of my work is about the fusion of dissimilar.
I have invented new fields, provided new insights in existing fields and provided new purpose to widely deployed mass-market devices.
My projects range from $1 million projects (looking around corners) to $1 projects (Netra)
They are long term and short term
They have commercial impact as well as social impact
Going forward, I am highly motivated to puruse an agenda that will spawn new fields, applications and commercial opportunities.
I have a plan to create a research trajectory, motivate students and important social, commercial and educational impact.

## Slide 68: Exploring Cameras, Displays & Visual Computing Innovations
Spring 20xx
Tue 4-6p
Media Lab e14-525
Professor Ramesh Raskar
&
Joost Bonsen
http://imagingventures.media.mit.edu
Imaging Ventures
MAS.533

## Slide 69: Organizer Intros
Ramesh Raskar
  Assistant Professor, MIT Media Lab
  Leader, Camera Culture Group
  http://raskar.info & http://cameraculture.media.mit.edu/
  PhD, UNC Chapel Hill 2002
  Formerly Research Scientist, MERL
Joost Bonsen
  Visiting Scientist & Lecturer, MIT Media Lab
  http://alum.mit.edu/www/jpbonsen & jpbonsen@alum.mit.edu
  SB, MIT, EECS 1990
  SM, MIT Sloan, MOT 2006

## Slide 70: Why Imaging? Why Now?
<Ramesh’s slides>

## Slide 71: End Goals of our Seminar
Quality Connections with Fellow Classmates, Course Advisors, & Guest Speakers
Survey-Level Awareness of Imaging Technology Business Challenges & Opportunities
Lessons-Learned from Live-Cases
A Specific Venture Proposal written up as a Business Plan Executive Summary
Increased Skills for Analyzing, Communicating, and Synthesizing Information towards Imaging Venture Creation
Global Perspective on Imaging Innovations

## Slide 72: What this Class is Not…
In-Depth
Packaged Lecture-Style
A Replacement for Core Classes, Advanced Electives
A class on How to Write a Business Plan
A Solo-Exercise
A Place for “Just Listening”

## Slide 73: Invention + Entrepreneurship  Innovations
It’s not enough to just do research, discover knowledge, or invent solutions
Good ideas must be deployed in the world to have impact
Entrepreneurship is about identifying worthwhile ideas and building the organizations to spread / sell the idea everywhere
  Both For Profit or Non-Profit
Founding tradition of MIT
http://mit-libraries.net/blog/wp-images/rogers1869sm.jpg

## Slide 74: MIT Alum Venture Legacy
~ US$ Hundreds of Billions in Market Valuation
Joost Bonsen © 2010 ~ jpbonsen@alum.mit.edu ~ Please email if you use or re-distribute this PPT

## Slide 75: The MIT $100K Entrepreneurship & IDEAS Competitions
Elevator Pitch Competition -- October
  1 minute, $1000 (October)
Executive Summary Competition -- November
  2 pages, $1000
  Announced next week Thurs 2/11 7:30pm 10-250
Business Plan Competition -- Spring
  2 page executive summary + business plan DUE 3/4!
  $100k Grand Prize + Track Prizes
http://www.mit100k.org/
IDEAS Competition
  Mid-Month Rolling Submission; Grant Funds
http://web.mit.edu/ideas

## Slide 76: MIT $100K Alumni Companies

## Slide 77: The Full MIT Innovation Ecology
Basic+Applied Research
Commercial Promise & Viability
University Spin-Off
Emerging Growth
Established Company
Support / Alum Offices:
Academic / Research Offices
Student / Informal Organizations

## Slide 78: Action Labs @ MIT Both For-Credit Curricular & Non-Credit Extracurricular Offerings
Basic+Applied Research
Commercial Promise & Viability
University Spin-Off
Emerging Growth
Established Company
Tiger Teams
S-Lab
D-Lab Energy, ICT, Health, Cycles, Design…
MarketLabs
New Enterprises
Media Ventures
D-Lab Development Ventures, Dissemination
Imaging Ventures
VentureSIGs
Africa Health Delivery Lab
India Lab
China Lab
Tech Testbeds
Leadership Lab
T h e M I T I n n o v a t I o n P I p e l I n e
Neuro Ventures

## Slide 79
Computational Light Transport
  Super-human visual abilities
  Empirical, Multi-directional rather than one narrow field
  Fusion of dissimilar
New Fields
  Femto-photography
New Insights
  Challenge the status quo
  BiDi Screen, CAT-scan, Augmented LF
  Sparsity, rank, priors
New Purpose
  Disruptive mass-use tech for social impact
  Netra, Cataract, Retinal scans
  $1M -> $1
Cameras, Displays, Medical Tools, Future Devices
  Theory, Modeling, Optical+Mathematical insight
Ramesh Raskar http://raskar.info
Bits
Photons
Computer Vision
Optics
Sensors
Signal Processing
Displays
Machine Learning
Computational Light Transport
Computational Photography
`
=
Notes: My new field Computational Light Transport is for creating super-human visual abilities: camera that can see around corners, devices that can see inside our bodies (Netra), 3D displays that are hyperrealistic, barcodes that shrink to a dot but still readable etc.
The empirical nature of the research means I must go and explore multiple directions rather than one narrow application or technique.
Lot of my work is about the fusion of dissimilar.
I have invented new fields, provided new insights in existing fields and provided new purpose to widely deployed mass-market devices.
My projects range from $1 million projects (looking around corners) to $1 projects (Netra)
They are long term and short term
They have commercial impact as well as social impact
Going forward, I am highly motivated to puruse an agenda that will spawn new fields, applications and commercial opportunities.
I have a plan to create a research trajectory, motivate students and important social, commercial and educational impact.