## Slide 1
AstroSat –
India’s First Astronomy Satellite
for simultaneous observations in multi-wave bands
PSLV-XL C-30 carrying AstroSat: 28th Sep 2015
Notes: 1

## Slide 2: Multi-wave Bands: Visible + NUV, FUV and X-rays
Each X-ray photon is >1000 times more powerful than a visible light photon !
Soft X-rays: 100 – 1000 eV; Hard X-rays: 1000 – 1,00,000 eV
X-ray Band: 0.1 – 100 keV (120 to 0.12 Angstroms) : 10 octaves
(compare with Visible light band of 4000-8000 Angstroms): 1 octave

## Slide 3
NUV, FUV and X-rays require space borne instruments

## Slide 4
AstroSat in a clean room before Launch
Mass of 1513 kg. (750 kg. Payloads) + 6 more small satellites
Power = 2200 watts by solar panels + 2 x 36AH Li-ion batteries

## Slide 5
Orbital period : ~98 minutes;
Eclipse period : 35 minutes; Sunlit period : 62 minutes
Heaters and sensors for thermal control of all the payloads and subsystems as specified.
Three-axis stabilization.
Orientation by 4 reaction wheels and 3 magnetic torquers (capacity: 60 A m2) + inputs from 3 dual gimbal gyros, 2 star sensors and 2 magnetometers.
Target acquisition capability of 0.05° (Moon Dia. = 0.5o)
Pointing accuracy of ~1 arcsec with star sensors.
Drift rate is expected to be 0.2 arcsec/s.
Maximum slew rate will be 0.6o/s.
AstroSat
Launched into a nearly circular orbit with Altitude: 640 - 650 km;
Inclination : 6 deg.

## Slide 6
Solid-state recorder with 200 Gb storage (4 orbits).
A satellite positioning system for time reference of 200 ns.
A Bus Management Unit with interface standard of 1553 for Attitude and Orbit control system, Command Processing, House keeping Telemetry, Sensor Processing, RCS interface, Thermal Management etc.
Data transmission by two X-band (8 – 12 GHz) carriers via two phased array antennas, once in all the visible orbits, at a rate of 210 (2 x 105 Mb/s) Mb/s.
House keeping data transmission in S-band (2 -4 GHz) via quadrifilar helix antennas.
The spacecraft control, payload data acquisition, data processing from ground stations in Bengaluru viz., ISTRAC TTC Network, TTC - Bangalore station.
Indian Space Science Data Centre (ISSDC) for payload data.
Operational life of >5 years
AstroSat

## Slide 7
LAXPC (TIFR)
SXT
(TIFR+UoL+ISAC+VSSC)
UVIT (IIA+ISAC+CSA+IUCAA+TIFR)
SSM (ISAC+VSSC)
Cold Side with
Radiator plates
For CCD and
CZTI
CZTI (TIFR + IUCAA +VSSC)
Star Sensors (ISAC)
AstroSat: Co-aligned multi-wave instruments
Website : astrosat.iucaa.in

## Slide 8
AstroSat
Expected Performance Parameters of the scientific Instruments

## Slide 9: Why build all the X-ray instruments? What Science
Physics of regions with strong gravity
Accretion – White Dwarfs (CVs), Neutron Star Binaries and Black Holes (galactic, extragalactic – AGN).
Physics of highly accelerated streams of particles astronomical jets (Blazars)
Strong Magnetic fields (Cyclotron lines) etc.
Physics of very hot coronal plasmas and their Hard X-ray components and flares

## Slide 10: AstroSat: Its Main Strengths
Simultaneous Opt- NUV –FUV- soft X-ray - hard X-ray measurements
Large X-ray bandwidth, better hard X-ray sensitivity than RXTE
Low background X-ray detectors : near Equatorial Launch
Bright source capability in soft X-rays
UV imaging capability better than GALEX

## Slide 11: Charge Particle Monitor (TIFR) detects SAA (Oct. 1, 2015)
To monitor the SAA entry & exit to lower voltages of the LAXPC, CZTI
CsI + Si-pin photodiode;
LLD of 1 MeV & can be reset

## Slide 12: SAA: The Bermuda Triangle of Space

## Slide 13: AstroSat:CZT-Imager(TIFR): Coded Aperture Mask-CAM
Side joining plates
Collimator
CZT top hsg.
CZT bottom hsg.
Radiator
Heat pipes
Optical cube
Alpha tag source
Handling brackets
CFRP support
CAM (Tantalum)255 pseudo-random Hadamard
Weight - 50 kg
976 cm 2 (64 CZT modules x 15.25 cm2
in 4 quadrants);
No. of pixels: 16384; 2.4 mm X 2.4 mm
(5 mm thick) ; ASIC based
(128 chips of 128 channels)
Collimator fov: 6o x 6o

## Slide 14: CZTI: Calibration & Veto
An X-ray source (Am241) mounted in a gap of 8 cm between the base of the collimator slats and detector plane in each quadrant for calibration.
VETO Detector: CsI (Tl) 20 mm thick x 165 mm x 165 mm detector viewed by two photomultipliers in a flat geometry. Just under the CZT modules.
  LLD: 50 keV. Variable by command: 256 steps of ~ 10 keV.
  Uniformity: ~ 10%,
  Response time: 5 ms
  Typical dead-time: 20 ms; A few hundred ms for saturated peaks
NIM:A (2010), 616, 55

## Slide 15: CZTI: First Light from Crab (Oct. 6, 2015)
X-rays > 25 keV
Resolution: 10 arcmin
(Moon Dia: 30 arcmin)
Image (blue) in Soft X-rays: ~2 arcmin
Power of 100,000 suns.
33 ms Pulsar
(29.65 Hz)

## Slide 16: CZTI: Detects a GRB 2015-10-06A lasting ~ 45 s
Thousands detected but origin is still debated.

## Slide 17
Scanning Sky Monitor (SSM)- ISAC
Three rotating Units: PSPC + coded mask

## Slide 18: SSM: First Light GRS1915+105: A black-hole in our backyard

## Slide 19
X-ray timing (10 μsec) low spectral resolution studies
A broad energy band (3 - 80 keV) with high detection efficiency
Three co-aligned identical Counters
Each with a multi-wire-multi-layer configuration filled with 90%Xe +10% Methane gas at 1520 torr. Energy resolution (13%@22 keV)
A 50 micron thick aluminized Mylar window for X-ray entrance
Mylar film support -- by a honeycomb shaped window support collimator with 5 x 5 degs field of view
A narrow field of view of 1x1 degs provided by mechanical collimators made of a sandwich of 50µ Sn + 25µ Cu + 100µ Al co-aligned with the window support collimator and sitting above it.
Blocking shield on sides and bottom : 1mm Sn + 0.2 mm Cu
LAXPC: Large Area Xenon Proportional Counters

## Slide 20
LAXPC
60 anode cells 3 cm x 3 cm x 100 cm in 5 layers each 15 cm deep (12 anodes/layer).
Mutual & layer by layer anticoincidence + Veto layers of 46 anodes cells (1.5x1.5 cm)
1600 wires – tension 80 gm per wire

## Slide 21: LAXPC unit (~125 Kg)

## Slide 22: LAXPC: First observations – Crab, GRS1915, 4U0115, Cas A etc
Transient X-ray pulsar (3.6 seconds) 4U0115+63.
High Mass X-ray Binary with a neutron star (high magnetic field) companion that accretes mass

## Slide 23: SXT: Optics + CCD Camera (~65 Kg)

## Slide 24: SXT: Optics – Replicated Thin foil mirrors made in TIFR (following Suzaku)
2 m focal length;
~2 arcmin HPD;
40 shells (130 – 260 mm dia);
Only 12 Kg !
Mirror roughness 7 – 10 Angstroms : Exp. Ast. (2011), 28,11

## Slide 25
Four Fe-55 calibration (corner) sources
One Fe 55 calibration door source
Thin Optical Blocking Filter
CCD Assy. including TEC
PCB with front-end electronics
Modified from Swift; Using
spare MOS CCD22 from XMM:
600 x 600 pix, 40 microns

## Slide 26: SXT FM: Electronics: NIM:A (2009), 604,747; Energy Calibration spectrum measured using internal sources: Single Pix events, all types of events. CCD @ -80 C (Superior resolution!)
4.5 keV
(Ti-F)
4.15, 4.75 keV Mn-K Esc
2.6 keV
(CL-F)
1.74 keV
(Si-K)
1.48 keV
(Al-F)

## Slide 27
SXT CCD – Switch On: Camera venting – Daily Oct 1st - 26th
TEC ON for CCD - Oct 9th and the following images taken after launch in the first week of Oct. 2015
Door and Corner X-ray Calibration Sources
Optical LED Image

## Slide 28: SXT Switch ON continued …. and FIRST LIGHT
Telescope (Optics) Door opening - Oct 15th
Camera Door Opening - Oct 26th @ 06:30 UT
First Light – Oct 26th
Pointed at and observed- PKS2155-304 (Quasar) at redshift of 0.116
(1.6 Billion LY away)

## Slide 29: SXT X-ray Light Curve of PKS2155-305
At 0.9 mCrab level !!
1100 times weaker than Crab:
We can go hundred times fainter in 10000s

## Slide 30: SXT X-ray Spectrum of PKS2155-305
Red-shifted absorption lines due to Oxygen?
WHIM?

## Slide 31: UVIT
Doors
Main-baffles
Secondary Mirror
Sec. Baffle
Primary Baffle
TiCone (interface
With S/C)
Primary mirror (375 mm)
Thermal cover (this encloses
Detectors and filter-wheels)
~3100 mm

## Slide 32: UVIT:J. Hutchngs PASP (2011), 123, 833 Effective Apertures (estimates)

## Slide 33: UVIT Simulations
M51 galaxy
GALEX (spatial scale reduced to put it at 3 times its distance)
vs
Astrosat FUV Image
From stacking of several short exposure images to correct for drift
PASP (2009), 121, 621

## Slide 34: AstroSat – Post launch Mission Plan
1st year
  First 6 months – PV Phase (4 X-ray; 2 UV)
  Next 6 months – GT Phase ( 4 X-ray; 2 UV)
2nd year
  5% Canada, 3% UK, 5% TOO, 2% Cal, 35% Open for GO (India), 50% Instruments’ GT
3rd year
  5% Canada, 3% UK, 5% TOO, 2% Cal, 45% Open for GO (India), 30% Instruments’ GT, 10% Open for International GO
4th year
  5% Canada, 3% UK, 5% TOO, 2% Cal, 65% India (GO), 20% International GO

## Slide 35: SCIENCE: Still to come --
Simulations XRB,
Cyclotron lines
from neutron stars in X-ray binaries.
Simulation
MCV

## Slide 36: Clusters of galaxies: illusive non-thermal emission in X-rays

## Slide 37: More Science to come from …
Stars and Stellar Flares in UV and X-rays
Supernova and Supernova Remnants
Novae
Cataclysmic Variables
White dwarfs in UV and soft X-rays
Star Formation
Low energy absorbers in soft X-rays
Transient X-ray Sources

## Slide 38
Thanks !
Several colleagues at TIFR, Mumbai; IIA, Bangalore, IUCAA), Pune
Canadian Space Agency, University of Leicester, UK
ISRO Satellite Centre (ISAC), Bangalore,
Raman Research Institute, Bangalore
Vikram Sarabhai Space Centre, Trivandrum,
Space Applications Centre, Ahmedabad & Physical Research Laboratory, Ahmedabad

## Slide 39: AstroSat: A comparison with other X-ray Satellites
Energy (keV)

## Slide 40: CZTI: Modes
Normal mode 1s 0-9 packets/quadrant
SAA mode 100s 1 packet/quadrant
Shadow mode 100s 1 packet/quadrant
Reduced data mode
  Fixed no. of events 1s 0-9 packets/quadrant
  Block veto spectrum 1s 0-9 packets/quadrant
  2 word event report 1s 0-9 packets/quadrant
Secondary spectral 100s 2 packets/quadrant

## Slide 41: Readout Modes of the CCD
Photon Counting Mode (PC), [The Default Mode - includes the calibration sources]
Photon Counting Window Mode (PCW),
Fast/Timing Mode (FM),
Bias Map Mode (BM), and
Calibration Mode (CM).
X-ray spectral information available in all the modes.
Time resolution in the PC, PCW, CM modes is 2.4 s, and 0.278 s in the FM mode.
FM reads only the central 150x 150 pixels of the CCD.
For observing very strong cosmic sources, the PCW mode should be used to avoid pile-up followed by the Calibration mode where four small windows (each of size=80 x 80 pixels) covering only the corners are used for the corner radioactive sources in the CM. ( A central 100x100 window is also used in the CM).