## Slide 1: Torsion Balance Motion Control System & Autocollimator Calibration System
DHEP Annual Meeting
7th & 8th April, 2016
Simon Pereira
Gravitation Group.

## Slide 2: Motion Control System for Torsion Balance
Torsion Balance
THE NEED FOR ADJUSTMENTS
i) The initial amplitude of torsional oscillation is often quite large (tens of degrees to several full rotations).
ii) The angular orientation of the axis of the optical
lever (OL) may be offset from the direction of the normal
to the mirror. (by an angle going anywhere upto 100)
Clearly, we need to be able to reorient the angular
setting of the torsion balance
BUT, the full measurement range of our Optical
Lever (OL) is about 5 micro-radian, and the p-p
amplitude of the torsional oscillation should be less
than this! (Note that the OL resolution is about 3 x
10-10 radians, for a total dynamic range of > 104!)

## Slide 3: Motion Control Technique (Mechanical, for Large Angle Osc.)
Oscillations of Very Large Amplitude are damped down to a few milli-radians by our “patented” mechanical technique. (“Sudden Shifting of Potential Wells”)
The Rotary Motion Drive at the top of the UHV system is used to damp the initial large oscillation amplitude (several radians) of torsion balance.
A set of precisely-timed rotary motions of the top feed-through using the stepper motor, with appropriate drive parameters allows the rapid damping of very large amplitude of oscillations.
The drive parameters for stepper motor are determined through careful and accurately timed measurements of the optical signal of torsion balance motion.

## Slide 4: Motion Control Technique (Electrical, for small Amplitude Osc.)
Damping below ~ 10 m-rad amplitude of oscillations to micro-radians is done by our home-built Magnetic Induction Drive (MID) System
Two sets of orthogonally oriented current–carrying coils, external to the UHV chamber are driven with AC signals in quadrature, to generate a rotating magnetic field at the location of the mass-bob of the torsion balance.
In effect, the coil then functions like the stator, and the mass-bob as the rotor of an induction motor. The resulting torque on the rotor is proportional to (Drive Voltage)2 and to Drive Frequency. We can change the direction of the torque by changing the direction of rotation of the magnetic field.
This gives us a very powerful tool for the control of the Torsion Balance, and we can generate drive torques that can be:
Proportional to the angular displacement of the Balance.
OR
Proportional to the angular velocity of the Balance.

## Slide 5: Automated Calibration System for Optical Lever
Optical Lever is used to monitor the motion of Torsion Balance.
  The sensitivity of the optical lever is 3x10-10 rad./(Hz1/2) and has linear range of +/- 2.5x10-6 rad.
The system has a very precise in-built mechanical simulator of angular movement for calibration. (This is what we call the “Compensating Plate”.)
Any system has “drifts”.
While we may spend a great deal of effort in reducing these drifts at source, it is necessary to calibrate the system periodically and the calibration has to be obtained even while the torsion balance is executing oscillation.
Optical Lever

## Slide 6: Prototype setup at Mumbai Lab

## Slide 7: Prototype setup at Mumbai Lab cont..

## Slide 8: Block Diagram of State Machine Lab VIEW Program (only a small part of the full system!)

## Slide 9: Front Panel of Lab-VIEW State Machine Program

## Slide 10
Chart: This graph displays all the applications of the program sequentially
Performance of the system at a Glance

## Slide 11: Precise Amplitude measurement
Chart: Torsion Balance Signal @ 0.1sec. scan rate
Chart: Torsion Balance Signal @ 3 sec. scan rate
Chart: 
Chart: 

## Slide 12: Precise Amplitude measurement
Chart: Torsion Balance Signal @ 2.3 sec. scan rate
Chart: 
Chart: Torsion Balance Signal @ 2.3 sec scan rate with 10-points averaging @ 20 msec rate
Chart: 

## Slide 13: Motion Monitoring, Driving & Damping Application
A
B
C
Chart: Time (day)
C
Chart: 
Chart: Time(day)
Chart: 
A
Chart: 
B

## Slide 14: Reset Signal , Calibrate OL & Recover Signal Application
Chart: Time (day)
Chart: Time (day)
Chart: 
Chart: 

## Slide 15: Optical Lever Calibration Data
Chart: Lin. Pot. Output (volts)
| 5.6553000000000004 | 5.6814 | 5.7168000000000001 | 5.7530999999999999 | 5.7851999999999997 | 5.82 | 5.8575999999999997 | 5.8944999999999999 | 5.9287999999999998 | 5.9619 | 5.9973000000000001 | 6.032 | 6.0701999999999998 | 6.1066000000000003 | 6.1398000000000001 | 6.1764999999999999 | 6.2103999999999999 | 6.2474999999999996 | 6.2826000000000004 | 6.3197999999999999 | 6.3540999999999999 | 6.3879000000000001 | 6.4279999999999999 | 6.4627999999999997
PSD Output | -10.138 | -9.3629 | -8.4976 | -7.655 | -6.7879 | -5.9291 | -5.0564 | -4.2162 | -3.327 | -2.4518 | -1.5759 | -0.66652 | 0.22979 | 1.1345 | 2.0537 | 2.9836 | 3.9006 | 4.8644 | 5.7952 | 6.7216 | 7.6421 | 8.615 | 9.5995 | 10.528
Chart: Lin. Pot. Output (volts)
| 5.5982000000000003 | 5.6288 | 5.6642999999999999 | 5.6969000000000003 | 5.7359999999999998 | 5.7695999999999996 | 5.8025000000000002 | 5.8403 | 5.8715999999999999 | 5.9084000000000003 | 5.9459 | 5.9798 | 6.0172999999999996 | 6.0522 | 6.0890000000000004 | 6.1245000000000003 | 6.1588000000000003 | 6.1863999999999999 | 6.2310999999999996 | 6.2670000000000003 | 6.3005000000000004 | 6.3367000000000004 | 6.3712999999999997 | 6.4035000000000002
PSD Output | -9.8774 | -9.1928 | -8.451 | -7.6634 | -6.8729 | -6.0712 | -5.2579 | -4.4302 | -3.6062 | -2.7433 | -1.8916 | -1.0333 | -0.16214 | 0.70931 | 1.5992 | 2.4808 | 3.4046 | 4.3158 | 5.2222 | 6.1476 | 7.0536 | 8.0037 | 8.9524 | 9.946

## Slide 16: Torsion Balance Data recorded at Mumbai Lab
Chart: This data is acquired from Torsion Balance on 26 June 2014 from 11:06:14 onwards
Chart: This data is acquired from Torsion Balance on 27 June 2014 from 10:54:44 onwards

## Slide 17
Home Made Encoder Mike Controller

## Slide 18
Encoder Mike Controller Circuit Boards

## Slide 19
EM
PWR
RESET
DIRECTION
FORWARD
REVERSE
MOTOR
RUN
HALT
SPEED
Basic version of EMC
1
1
1
1
1
1
EM1
EM2
PWR
LOAD
RESET
SELECT EM
MIRROR EM
CP EM
OP MODE
AUTO
MANUAL
DIRECTION
FORWARD
REVERSE
MOTOR
RUN
HALT
THUMBWHEEL SWITCH
MEMORY
TWS
COUNTER
REGISTER
DATA IN
DATA OUT
SPEED
AUTO RUN
SW7
SW2
SW3
SW4
SW5
SW6
SW8
SW9
SW10
Advanced version of EMC

## Slide 20
Thank you for your attention!