## Slide 1: Neutrino oscillation & INO
Angles (mixing) are very much different than in quark sector
For neutrinos weak Eigen states may be different from mass eigen states.
In a weak decay one produces a definite weak eigen state
Then at a later time t,
Pontecorvo-Maki-Nakagawa-Sakata
Cabibbo-Kobayashi-Maskawa

## Slide 2: First atmospheric neutrino was reported from Kolar Gold Field (KGF) at a depth of 2.3km way back in 1965 by the TIFR-Osaka-Durham group.
TIFR had a long tradition of carrying out experiments deep underground.
KGF laboratory was the deepest underground laboratory during the period 1951-1992.
KGF by TIFR-Osaka collaboration to look for proton decay.
KGF mines closed its operation in 1992.
~30 muon /year/m2/sr at KGF, increased by a factor of ~100 at INO

## Slide 3: India based neutrino observatory (INO)
Create experimental facility in the country where we can carry out front ranking experiments in the field of particle & astroparticle physics.
Underground laboratory with ~1 km all-round rock cover accessed through a 2 km long tunnel. A large and several smaller caverns to facilitate many experimental programmes.
Frontline neutrino issues e.g., mass parameters and other properties, will be explored in a manner complementary to ongoing efforts worldwide.
The ICAL detector, with its charge identification ability, will be able to address questions about the neutrino mass ordering.
Will support several other experiments when operational. Neutrino-less Double Beta Decay and Dark Matter Search experiments foreseen in the immediate future.
Open to International participation

## Slide 4: INO-ICAL detector
Total number of RPCs in the ICAL = 3  150  64 = 28,800
Total gas volume = 28,800  190cm  190cm  0.2cm ~ 200 m3
Total surface area = 28,800 × 1.9m × 1.9m ~ 105 m2
Standard gas composition for the avalanche mode:
  Freon, R134a(C2H2F4):Isobutane(i-C4H10):Sulphur Hexafluoride(SF6)::95.5:4.3:0.2
Float Glass
Float Glass
Fast and precise timing information to identify up-down ambiguity of muon: RPC is a the best choice to have <1ns precision with low cost
3cm strip pitch & strip multiplicity : ~5mm position resolution (along with ~1.3T magnetic filed) to identify bending of +ve and ve muon, very crucial for the determination of neutrino mass hierarchy

## Slide 5: INO-ICAL Detector
Parameter | ICAL | ICAL-Engineering module
No. of modules | 3 | 1
Module dimensions | 16.2m × 16m × 14.5m | 8m × 8m × 2m
Detector dimensions | 49m × 16m × 14.5m | 8m × 8m × 2m
No. of layers | 150 | 20
Iron plate thickness | 56mm | 56mm
Gap for RPC trays | 40mm | 40mm
Magnetic field | 1.3Tesla | 1.3Tesla
RPC dimensions | 1950mm × 1910mm × 30mm | 1950mm × 1910mm × 30mm
Readout strip pitch | 30mm | 30mm
No. of RPCs/Road/Layer | 8 | 4
No. of Roads/Layer/Module | 8 | 4
No. of RPC units/Layer | 192 | 16
No. of RPC units | 28,800 (107,266m2) | 320 (1,192m2)
No. of readout strips | 3,686,400 | 40,960

## Slide 6: A journey through RPC road
10 cm  30 cm
30 cm  30 cm
100 cm  100 cm
200 cm  200 cm
Started with 10 cm × 30 cm Glass RPC in Streamer mode
Now with 200 cm × 200 cm Glass RPC in Avalanche mode

## Slide 7: Running Prototype RPC Stack at TIFR
General muon flux distribution
n=2.15 ± 0.01
I0 = (6.217 ± 0.005)×10-3 cm-2 s-1 str-1
Distinction of up/down Muon
Zenith angle of muon, measurement of cosmic muon flux as well as it angular dependency
Mis-identification
Inefficiency due to button, dead strip, but edge effect also present
Multiplicity and position
Input to detector simulation and digitisation
Notes: 7

## Slide 8: Sub-ns Time resolution in Large area single gap RPC
Existing/used RPC in HEP : ATLAS, L3, BELLE, BABAR : t ~1.5 to 3.0ns
First time trying to obtain sub-ns time resolution

## Slide 9: Improvement of RPC timing
Looking for the understanding of this kind of sources to improve the time resolution
in RPC in RPC
Variation in RPC timing as a function of position in strip and also multiplicity
Faster and also slower arrival time near the button spacer

## Slide 10: Heat Strengthening & Tempered Glass
HS ~twice hard than normal glass (Surface test : 40 Mpascal)
Performance of RPC with HS glass is comparable with Normal Glass, though the dark current is larger, which is under study
Eventually want to look on Tempered glass (Six times harder than normal glass)

## Slide 11: Multigap RPC
Motivation:We want to use Multigap Resisitve Plate Chamber (MRPC) for TOF for possible application in the medical imaging. MRPCs offer σt = 60 - 100 ps.
Plan: We will read both X and Y coordinates with orthogonal pickup panels. We also plan to use two detectors on each side with layers of converter plates. Both space and timing information will be used to locate the source position. ΔL[mm]≈σt [ps]/2, ΔL=FWHM in the position accuracy.

## Slide 12
Detector simulation and event reconstruction
GENIE : modified
3D neutrino flux,
Weighted evt
GEANT
Neutrino Event Generation
νa+ X -> A + B + ...
Generates particles that result from a random interaction of a neutrino with matter using theoretical models .
Output:
i) Reaction Channel
ii) Vertex Information
iii) Energy & Momentum of all Particles
Event Simulation
A + B + ... through RPCs + Mag.Field
Simulate propagation of particles through the detector (RPCs + Magnetic Field)
Output:
i) x,y,z,t of the particles at their interaction point in detector
ii) Energy deposited
iii) Momentum information
Event Digitisation
(x,y,z,t) of A + B + ... + noise + detector efficiency
+ time resolution from operational RPC in Mumbai
Output:
i) Digitised output of the previous stage (simulation)
Event Reconstruction
(E,p) of ν + X = (E,p) of A + B + ...
Fit the tracks of A + B + ... to get their energy and
momentum.
Output:
i) Energy & Momentum of the
initial neutrino

## Slide 13: Determination of neutrino mass hierarchy
Hadronic information is added separately
Larger value of sin213, more confidence level/less year to have same CL

## Slide 14: INO Graduate Training Program
8th batch of 3 students have started their course work at TIFR.
Several students from 1st and 2nd batch ( 2008-9) submitted their theses.
Has designed the RPC trigger and before completion of 5th year, was hired (Post. Doc.) by CMS L1 trigger upgrade group
Post. Doc@Berkeley : for development of the novel bolometric detectors for CUORE neutrinoless double–beta decay experiment and as well as R&D towards a next-generation double-beta decay experiment.
@ Rutherford Appleton Lab : Setting up an experiment (starting from making detector to DAQ system and then analysis) for muon tomography.
INO Graduate Training School will move to IICHEP, Madurai in near future.
Expect those will return back with more experience and will design & build expt.

## Slide 15: Other R&D
Close loop Gas recirculation system
Indigenous design of gas monitoring and purifier system
RPC leak testing technique
Industrial interface and Assembly of RPC………………
Electronics, DAQ, Trigger………………..