## Slide 1: ASSISTECH Technology Solutions for the Mobility & Education of the Visually Impaired
M Balakrishnan
CSE Department, IIT Delhi

## Slide 2: Key Challenges
Census 2011 Data
    Disabled population: 21 Million
    Visual disability: 48.6 %
Societal Inclusion
Independent Mobility
Education

## Slide 3: White Cane – A Reliable Companion

## Slide 4: Independent Mobility

## Slide 5: SmartCaneTM
Ultrasonic ranging – 3 meters
Warning through intuitive vibratory patterns
Complements white cane functionality
Detachable handle
Suitable for all grips
Low power & chargeable
Knee-above + non-contact
obstacle detection

## Slide 6: Product- Resources & Accessories

## Slide 7: SmartCaneTM Journey

## Slide 8: Mobility Continued Public Bus Access

## Slide 9: Public Bus Access Challenges
Route No ?
Where is the entry door ?

## Slide 10: Bus Access: Challenges not the Same

## Slide 11: OnBoardTM

## Slide 12: Working Principle (Query Stage)
  User presses the Query button (user module)
    RF query sent to all buses in the vicinity.
  Buses respond with their route numbers
    User module reads out all the route numbers

## Slide 13: Working Principle (Selection Stage)
In case a route number is of user interest
  User presses the Select button (user module)
This triggers a voice output from the speaker (bus module fixed near the door)
  Acts as auditory cue for locating the door

## Slide 14: Deployment of Bus Module
Under-the-Seat Module comprising of the battery, amplifier and control circuits.
Speaker and Antenna module installed on the railings next to the door

## Slide 15: OnBoard Video

## Slide 16: Education
How do the visually impaired read and write?
Using Braille – a script used by almost all languages of the world!
Ever thought of how do they access pictures?

## Slide 17: Tactile Diagrams – Diagrams for the Visually Impaired
Diagrams created using raised lines or textures that can provide meaningful information to a visually impaired person
Examples are many
  Maps
  Bar graphs
  Economics diagrams
  Science diagrams
  Yoga posture diagrams

## Slide 18: Tactile Diagrams
A Tactile Book from American Printing House

## Slide 19: Tactile Diagrams from Centre of Excellence in Tactile Graphics IIT Delhi
Developed end to end technology to reduce the cost from nearly Rs 130 per page to Rs 15 per page
First open source software for production of tactile diagrams to be launched soon
Produced numerous books for NCERT – IX Grade NCERT Maths & Science, Maps, Economics, Introductory Mathematics …..
Pilot studies under way for testing their effectiveness

## Slide 20: Education Continued
How do the visually impaired access e-text?
Using Audio – screen readers
JAWS and NVDA are popular screen readers
Based on TTS
Reading & Writing
Refreshable Braille Display

## Slide 21: Refreshable Braille Displays
Many such devices are available
@ USD 2500 to USD 5000 hardly any penetration in India and other low income countries

## Slide 22: IIT Delhi RBD Prototype

## Slide 23: Key Collaborators
Mr. Dipendra Manocha
Prof. P V M Rao
Dr. Rohan Paul
Mr. Piyush Chanana

## Slide 24: ASSISTECH Research Group
Interdisciplinary: Comp Sci, Elec Engg, Mech Engg, Design
20 Staff (incl. two visually impaired) and nearly 25 students each semester
Recently PhD and MS(R) enrolled

## Slide 25: Recognitions yes – Impact ?

## Slide 26: Scaling Challenges
No easy way to reach the potential users
All NGOs serve only a very small user group
  40+ channel partners across the country
Incubation very hard as Govt is the main customer

## Slide 27: Status – 31st Dec 2016
SmartCaneTM
17997 devices sold
400 devices in 10 countries
OnBoardTM
Pilot on 25 BEST buses with 21 users, 350 unsupervised boardings
Waiting funding for BEST installation
Tactile Diagrams
Many NCERT books
IX Science & Maths books under pilot testing
Refreshable Braille Displays
Pilot trials due in May ‘17

## Slide 28: To touch a million lives by 2020

## Slide 29
Thank you
Notes: Secondly, the detection range of the cane is restricted to 1-2 feet from the user.
In situations like walking on the roadside, a moving obstacle like a car cannot be detected until it is dangerously close to the person.