## Slide 1
Krithi Ramamritham
IIT Bombay
Building Smart Things
Managing Energy, Computationally
Center
for
Urban Sc. & Engg.

## Slide 2
Krithi Ramamritham
IIT Bombay
Solving Real-World Problems
Using Computational Thinking
Center
for
Urban Sc. & Engg.

## Slide 3
Krithi Ramamritham
IIT Bombay
Harnessing Big Data for Building Smart Things
Solving Real-World Problems
Using Computational Thinking
Managing Energy, Computationally
Center
for
Urban Sc. & Engg.

## Slide 4: Being Smart
clever, bright, intelligent, able, analytical
shrewd, astute, perceptive, savvy
brisk, energetic, vigorous
fast, rapid, swift, lively
sharp-witted, quick-witted
quick on the uptake

## Slide 5: SMART phone

## Slide 6: Smart Door
Spotlight
Smart
Door
Reduce unnecessary consumption
Notes: (First image) This is an example of a smart door knob. The locked door unlocks in the presence of your phone which you would have had to synchronize with your lock earlier. It senses the presence of the device, analyzes if it is a recognized device and if it is unlock the door.
(Second image) The smart knob here makes life easier by making your entry keyless. Your phone or a card etc can be used to unlock. These items make the lock more difficult to break open by force and makes life easier as your don't have to carry a key.
(Third image)
Here the door knob is itself a security system. If you try to break in, unless you have the key or an authentication of some kind the door will set off the alarm.

## Slide 7
Use Smart door to
Sense
  Height and weight
Analyze
  Identify User
Respond
  Store Identity info
  Turn their appliances ON
Smarter Door
Height
+
Weight
Identity
Lasers
LDRs
Ultrasonic Sensor
Machine Learning
Weight mat

## Slide 8: Accuracies obtained with different features and classifiers
Accuracies with different features and classifiers

## Slide 9
  Winning combination:
  Height + Weight
Smart Door $100
(Prototype)
(Active RFID $1500)

## Slide 10: Who is entering/leaving the lab?
From height + weight based (hard sensor) information
IDENTIFY the set of possible occupants given
occupants list
-- {A,B,C}
PRUNE set using
soft sensors (people’s/rooms’ schedules/occupancy, etc.)
-- C has a meeting elsewhere,
-- B usually comes after lunch
=> A is entering
ACM e-Energy 2015
Demonstration of Using Sensor Fusion for Constructing a Cost-Effective Smart-Door.

## Slide 11: Being Smart
clever, bright, intelligent, able, analytical
shrewd, astute, perceptive, savvy
brisk, energetic, vigorous
fast, rapid, swift, lively
sharp-witted, quick-witted
quick on the uptake

## Slide 12
The Smart Classroom Complex
Energy Consumed
ONLYIF
Occupied
Spotlight:
Smart
Classroom
Occ - Occupied
HD - Human Detected
HND - Human Not Detected
L- Lights
F - Fans
AC - Air Conditioners

## Slide 13
The Smart Classroom Complex
Consumption => Occupied
OCC -- Occupied
HD – Human Detected
HND – Human Not Detected
L- Lights
F - Fans
AC – Air Conditioners
Spotlight:
Smart Classroom

## Slide 15
Sense | Temperature & Humidity
Analyze | Temperature & Humidity > Threshold of Fan
Respond | Turn ON Fans

## Slide 16
Sense | Temperature & Humidity
Analyze | Temperature > Upper Threshold of AC
Respond | Turn ON AC

## Slide 17
Sense | Temperature & Humidity
Analyze | Temperature > Upper Threshold of AC Temperature & Humidity < Threshold of Fan
Respond | Turn OFF Fans

## Slide 18
Zero Occupancy
Zero
Consumption

## Slide 19
The Smart Classroom Complex
Energy Consumed
ONLYIF
Occupied
Spotlight:
Smart
Classroom

## Slide 20
Sensing Occupancy
Alternatives | Correctness | Prompt-ness | Data | Resilience to Network Problems | Cost Efficiency
PIR | 5 | 2 | 1 | 1 | 1
PIR Array | 4 | 3 | 2 | 2 | 2
Camera | 3 | 1 | 5 | 5 | 3
+ PIR | 2 | 5 | 4 | 4 | 4
+ PIR Array | 1 | 4 | 3 | 3 | 5
Alternatives | False Positive | False Negative | Network Usage | Zonal Occupancy
PIR | High | High | None | No
PIR Array | High | Low | None | Yes
Camera | Medium | Medium | High | No
+ PIR | Low | Low | High | No
+ PIR Array | Low | Low | Low | Yes
Properties
Ranking

## Slide 21: Energy savings
Energy Savings: 32 to 43%
Payback period: 12 to 18 academic months

## Slide 22
Old Schedule
New Schedule
Room Scheduling to Reduce Consumption
During gap hour, sometimes it is better not to turn off the ACs,
Instead maintain space at > desired temp,
Just prior to usage, decrease temperature.
Scheduling based on
Precooling
Scheduling based on Room Size
large classrooms

## Slide 23
Appliances switched on for all 9 slots
Chart: Energy(KWh)
| Baseline | Better Baseline | SMART | SMART + Given Schedule | SMART + Clever Schedule
Lights & Fans | -36000 | -27000 | -15425.5 | -14800 | -9950
HVAC | 40664.8 | 34614.6 | 27015.5 | 21475.55 | 15835.3
Appliances switched on for 7 slots, excluding 2 slots of Lunch hour. (-19.63%)
Appliances are actuated based on Occupancy. (-31.11%)
Appliances are actuated based on current schedule and smart
IDU scheduling. (-41.2%)
Appliances are actuated based on energy aware schedule and smart IDU scheduling policy. (-58.15%)
Energy Savings: 58%
Payback period: 6 academic months

## Slide 24: Smart Academic Environment
ML
Scheduling based on
Precooling
Scheduling based on Room Size
OLD SCHEDULE
NEW SCHEDULE
SENSE
MEANINGFULLY
ANALYZE
RESPOND
TIMELY
SMART
SYSTEMs
EMEMBER

## Slide 25: Demo – Smart Door and Smart Classroom

## Slide 26
Reduce unnecessary consumption
Increase reliance on sustainable energy sources
Exploit renewables
Flatten peaks in consumption
Reduce need for unsustainable energy sources
Store excess energy
Towards Sustainable Energy

## Slide 27: Thermostatically Controlled Electrical Devices
Maintain
Temp within [L, H]
Exhibit Periodic ON-OFF Operation
Spotlight
Co-ordinated Scheduling

## Slide 28
Behavior of a Cooling Unit
Sense Temp
If Temp > H Cooler_ON
If Temp < L Cooler_OFF
Run Time
H
L

## Slide 29: Feedback
Analyze and Control
Have to learn from the past

## Slide 30: Smart Scheduling: Peak Demand Reduction
AC2
AC2
AC2
AC1
AC1
AC1
Time
Power
AC1
AC1
AC1
AC2
AC2
AC2
Time
Power

## Slide 31: Thermal Comfort Band Maintenance Algorithm
Temperature
Time
BU
BL
Peak energy constraint:
At most m out of n devices can be on
L
H
n=3, m=2
Sense Ambient Temp, Available Peak Power
Analyze Schedulability
Respond Set m, Temp Band

## Slide 32: Feasibility Analysis
Can the given band [L, H] to be maintained
by running at most‘m’ ACs at a time
-- using the characteristics of each of the ACs.
Analysis:
Is Aggregate cooling
greater than
aggregate warming
Sf - slope of cooling curve
Sr - slope of warming curve

## Slide 33: Improved Schedulability by shifting comfort-band (5 ACs)
Reinitialization Time
Comfort band | m | Feasible?
23-25 | 3 | Yes
23-25 | 2 | No
24-26 | 2 | Yes
 |  | Ambient 270C |  |  | Ambient 300C |  | 
Comfort- band | m | Σ Sf | Σ Sr | Feasibility | Σ Sf | Σ Sr | Feasibility
23 – 25 | 2 | 0.149 | 0.140 | Yes | 0.35 | 0.53 | No
24 – 26 | 2 | 0.218 | 0.098 | Yes | 0.46 | 0.35 | Yes
Demand-Response Management

## Slide 34
Sense
Analyze
Response
Sense
Analyze
Remember
Meaningfully
Timely

## Slide 35: SMART Design Philosophy
It is a continuous feedback-driven process
Sense
Analyze
Remember Response
Meaningfully
Timely
What?
When (How Often)?
How?
Where?
Which (Hard, Soft, Aggregating,….)?
Archival Data
Real-Time Data
(Dis)aggregated data
Who?
When?
Where?

## Slide 36: Types of Analysis
Sense
Analyze
Respond
Temperature of different zones
Using Schedulab-ility analysis
Actuate minimum number of AC’s
Analysis:
Model-based reasoning
Exploiting correlated phenomena
Regression
Sense
Analyze
Machine Learning
Logical Reasoning
Schedule
Time of Day
Response
Number of Occupants & ID’s
Sense
Analyze
Machine Learning (ANN)
Temperature
Time of Day
Response
Power Consumption

## Slide 37
Reduce unnecessary consumption
Increase reliance on sustainable energy sources
Exploit renewables
Flatten peaks in consumption
Reduce need for unsustainable energy sources
Store excess energy
Towards Sustainable Energy
  Need
  SMART
  Approaches

## Slide 38: If there is a need to save energy don’t depend on the consumers
What do users know about their energy consumption?
What is the potential renewable energy available?
How can we optimally use energy?

## Slide 39: User Energy Awareness Study
To know whether consumers understand their energy consumption behavior
  Time of the day at which they consume highest energy
  Overall energy consumption pattern on a weekend or a weekday
Do consumers remember their electricity bills over period of time?

## Slide 40: Study Building
Residential building on campus
  13 floor building, 4 apartments on each floor
  Separate smart meter for each apartment, sampling rate is 5 seconds
Consumer distribution
Family size | # of apartments
1 | 2
2 | 3
3 | 18
4 | 10
5 | 7
6 | 1
Study Building

## Slide 41: Buildings Energy Usage Behavior
Prominent energy consumption patterns found in different apartments
Aggregate building energy consumption over 4 consecutive days

## Slide 42: Survey Questionnaire

## Slide 43: Study Findings
Question | No. of correct responses | No. of wrong responses | Correct Percentage
Bill Awareness | 16 | 25 | 39
Peak Awareness | 9 | 32 | 22
Profile Awareness | 7 | 34 | 17
Number of correct and incorrect responses to three different survey questions

## Slide 44: Reasons for Low Awareness
Apartments are instrumented with smart meters, but consumers do not have interface to visualize their daily energy usage
Bills get automatically deducted from salary, so consumers don’t remember their bills
Electricity bill forms just a small percentage of one’s expenses.

## Slide 45: Automation is essential

## Slide 46: Smart Lecture Hall
If people in the back moved to the front rows,
during this talk,
we will save
30% energy
600
2.5 trees

## Slide 47: What info is needed?
How many people are there?
Where are they seated?
What are the temperature variations across this space?
What is the outside temperature?
What is the power consumption profile of this space?
How much energy will be consumed for different seating configurations?
Is there a limit on the max power available?
What is the power price structure?
….

## Slide 48
Sensing -- Facets
Obtaining different perspectives
about the building
Power consumption
occupancy
Air quality
(temperature, humidity)
#ON Appliances

## Slide 49
ACHIEVE OBSERVABILITY
of different facets
USING FEWER SENSORS
GOAL

## Slide 50: SMART Energy Improving QoS: Lowering Energy Cost & Enabling Consumer Participation
Energy Cost
Costly & Inefficient Peak Reserve
Usage Charge
TOD Charge
Demand Charge
Investment & Utilization
Consumption
Flattening Peak Demand
Limiting Peak Demand
Reducing Consumption
Dynamic Adaptation of
Comfort Band (CB)
Partitioning Power & TCBM
<<Reduces>>
<<Reduces>>
<<Reduces>>
<<Reduces>>

## Slide 51: Soft Sensing
Using soft sensing to
achieve observability
with fewer sensors
G
Infer facets from soft information.
Ex: people/room schedules, location information.
Analysis:
Inference Logic
Deep Learning
Formula
Replace hard/physical sensors with soft sensors

## Slide 52: Tree representation of Smart Classroom Complex
Power Consumption – SUM
Occupancy Status – OR
Vacancy Status – AND
Temperature – Weighted AVG
Small Classroom
Big Classroom
Zone of Big Classroom
VS = f(VCR1, VCR2, VCR3, VCR4, ODU)
Use building structure to reduce the number of sensors:

## Slide 53: Facet-Sensor Relationship Graph

## Slide 54: Facet-Sensor Relationship Graph

## Slide 55
Facet | Hard Sensors | Soft Sensors
Power | Smartmeter (ODU) | Inffrm
Occupancy Status | PIR, Camera | -
Number of ON Appliances | - | Infapp
Temperature | Temperature Sensor | -
Use soft sensors to reduce the
number of physical sensors
Only 1 (NOT 10) Smart Meter Required
Use correlation between different facets to reduce number of sensors
Facet-Sensor Relationship Graph

## Slide 56
Achieved through
Sensor Fusion:
Hard + Soft Sensing
Structure of building
Facet-Sensor relationship graph
In spite of their possible inaccuracy,
soft sensors can lead to
accurate query results:
Using multiple (hard and soft) sensors can improve reliability and accuracy.
Observability of facets of a building
SenSys'16 Demo, ACM BuildSys '16 (best paper candidate) :
Observability: A Principled Approach to Provisioning Sensors in Buildings

## Slide 57: drastic minimization of the number of sensors deployed
Replace hard/physical sensors (PS) with soft sensors (SS):
    e.g., Power consumption of a lab can be inferred from the number of ON desktop machines
    no need for smart meters (SMs).
    SSs are free from capital costs and hence are preferred over PS, but are inherently inaccurate because they are based on inferences.
Use building structure to reduce the number of sensors:
We can represent a building as a graph, with each node representing a logical zone of the building (for example, rooms, floors, wings, etc.) and edges representing the flow of information.
Use correlation between different facets observed and sensors available:
A facet value obtained from a sensor can serve as an input for observing another facet.
Observability:
A Principled Approach to Deploying Sensors

## Slide 58: Applications of Big Data Analytics
Estimating whether the immediate demand can be fulfilled in the near future
Detecting peak consumption
Is the consumption more than usual
Detecting anomalous or abnormal appliance consumption.
Estimating the number and type of appliances operating at any instant.
Identifying a change in consumption pattern over the last few days or hours.

## Slide 59
  Reduce unnecessary consumption
Increase reliance on sustainable energy sources
  Exploit renewables
  Flatten peaks in consumption
Reduce need for unsustainable energy sources
  Store excess energy during off-peak – avoid blackouts
SMART Energy Management

## Slide 60: Using Stored/Renewable Energy
batteries in home settings:
peak flattening, reduced costs,
smoothed intermittent sources,
surviving grid outages

## Slide 61
Chart: 
| Transport | Offices | Educational | Hospitals | Industrial | Commercial | Residential
Potential in kW and respected share | 29.9 | 20 | 72 | 15 | 223 | 56 | 1300
Category-wise Potential & Share
Mumbai’s peak power demand 3.35GW
Rooftop PV
potential
is enormous
1.55GW - 1.89GW
46% to 56%
Need policies
to harness it
Notes: The Degree of Difficulty explains here,
Residential Inadequate space, for domestic use (dry cloth lines), Lack of control over rooftop space, High Upfront investment for individuals, Lack of awareness, incentivize with attractive Govt. policies
Commercial Recreational Activities, Rood Garden, affect the aesthetics, Dome shaped roof (Malls, Hotels, Restaurants), cooling
towers, ventilating shafts, water heating systems and tanks
Industrial mostly occupies by cooling towers, ventilating shafts, water heating systems and tanks so less area
Hospitals Most Hospitals are having Solar water heater system
Educational want Easy financing options, affects Aesthetics
Transport & Offices Possible immediately to imply since only controlled by Govt. body (Policy Implication)
Key drivers for Solar Rooftop PV systems in Residential segment are,
Ease of Installation
Minimum maintenance
Generate revenue for using rooftop
Should run all loads at home

## Slide 62: SMART Design Philosophy
Applicable at
Design
Deployment
Initialization
Run Time
SENSE
MEANINGFULLY
ANALYZE
TIMELY
RESPOND
EMEMBER
What
When (how often)
How
Where
Which (hard, soft, aggregating…)
Archival data
Real-Time data
(Dis)aggregated data
Who
When
Where

## Slide 63
SENSE
RESPOND
ANALYZE
Any time
we answer a question
or make a decision, we
It is a continuous feedback-driven process

## Slide 64: Responsive Systems
SENSE
RESPOND

## Slide 65: Real Time Systems
SENSE
RESPOND
TIMELY

## Slide 66
SENSE
ANALYZE
RESPOND
TIMELY
RT Systems +

## Slide 67
SENSE
MEANINGFULLY
ANALYZE
RESPOND
TIMELY
RT Systems ++

## Slide 68
SENSE
MEANINGFULLY
ANALYZE
RESPOND
TIMELY
EMEMBER
RT Systems +++

## Slide 69: SM A RT Systems
SENSE
MEANINGFULLY
ANALYZE
RESPOND
TIMELY
EMEMBER

## Slide 70: SMART Systems
SENSE
MEANINGFULLY
ANALYZE
RESPOND
TIMELY
EMEMBER

## Slide 71
SENSE
MEANINGFULLY
ANALYZE
RESPOND
TIMELY
EMEMBER
SMART Design Philosophy
What
When (how often)
How
Where
Which (hard, soft, aggregating…)
Archival data
Real-Time data
(Dis)aggregated data
Who
When
Where
Applicable at
Design
Deployment
Initialization
Run Time

## Slide 72: Smartness at all “TIMES”
Design Time
Deployment Time
Initialization Time
Run-Time
+

## Slide 73
Smart buildings
Smart campuses
Smart cities
Smart Auditorium/ Classroom
Smart Door
Smart Chair
Smart HVAC
Smart Office

## Slide 74
Towards Sustainable Energy
Reduce unnecessary consumption
Increase reliance on sustainable energy sources
Exploit renewables
Flatten peaks
Reduce need for unsustainable energy sources
Store excess energy during off-peak – avoid blackouts
Use energy efficient
appliances
Turn off devices
when not needed
Set comfort levels
smartly
Exploit elasticity
of appliance operations
Store excess energy

## Slide 75: Towards Sustainability
Reduce
  Consumption
  Peaks
  Reliance on unsustainable energy sources
Reuse resources
Recycle resources
The 3 R’s

## Slide 76: Some examples of SMART things Smart phone Smart entrance/doorSmart Lab/office/classroom What does it mean to be smart ---- ‘SMART’ PRINCIPLE Computational Thinking needed to build Smart Things User studies -- Automation / analytics is Key Sensing Framework Goal: Need for smart, minimal sensing Notion of observability of facets Sensors Occupancy -- binary/count, Occupant -- Identification Environmental Conditions -- Temperature, Humidity, CO2 Smart Energy -- Algorithms for matching Demand with Availability Smart HVAC Management Collecting Big Data – User Studies Automation + analytics is Key Smart Energy Management -- Integration Smart Integration with Energy Storage Smart Integration with Renewables + Solar potential Smart Electric Grid Smart city Challenges Data Challenges in a Smart World

## Slide 77: How does a computer scientist think? What are the concepts/approaches used in CS?
Algorithms -- Step-by-step approaches
Enables use of computer and other tools to help solve them; Automating solutions
Abstractions -- Focus on the key aspects, remove unnecessary detail Use models/simulations
Generalizing and applying a solution to a wide variety of problems.
Decomposition -- Divide and conquer
Simplifies solution development
Patterns -- Look for and exploit similarities
Reuse existing solutions
Logic — reasoning according to strict principles of validity
Logically organizing and analyzing the problem/data eases correct problem solving
Evaluation — Adopt after checking out performance
Identifying, analyzing, and implementing possible solutions with the goal of achieving the most efficient and effective combination of steps and resources

## Slide 78
Planning your day
Responding to messages
Organizing your backpack
Managing your todo-list
Reorganizing your office
Preparing dinner
Planning your next day
Simple Everyday
Activities
Scheduling
Prioritization
Deadline cognizance
Checking feasibility
Pipelining
Caching
Prefetching
Partial computations
Parallel processing
Optimization
CS Systems
Tricks

## Slide 79: Useful CS concepts/approaches
Algorithms -- for coordinated AC on/off
Enables use of computer and other tools
to help solve problems
Abstractions -- Use physics-based models
Decomposition – pre-runtime feasibility checking,
runtime control
Patterns – spot and exploit the periodic execution patterns
Reuse existing solutions
Logic — If someone is entering, they can’t be inside the lab!
Logically organizing and analyzing the problem/data eases
Evaluation — Adopt after checking out performance benefits and payback periods
Identifying, analyzing, and implementing possible solutions with the goal of achieving the most efficient and effective combination of steps and resources
Scheduling
Caching
Prefetching
Partial computations
Parallel processing
Checking feasibility
Optimization
Compiling
`

## Slide 80: Lowering Energy Cost & Consumers’ Participation in Improving QoS
Energy Cost
Costly & Inefficient Peak Reserve
Usage Charge
TOD Charge
Demand Charge
Investment & Utilization
Consumption
Flattening Peak Demand
Limiting Peak Demand
Reducing Consumption
Dynamic Adaptation of
Comfort Band (CB)
Partitioning Power & TCBM
<<Reduces>>
<<Reduces>>
<<Reduces>>
<<Reduces>>

## Slide 81: Thanks a lot Thanks to my collaborators

## Slide 82
Thanks to my students and members of SEIL: Smart Energy Informatics Lab, IIT Bombay