## Slide 1: Indian Participation in ITER - Technology Challenges and Industry Response
U K Baruah, Project Director

## Slide 2: Foreword
2005 Dec: India became a member of ITER,
  Mixed bag of In-Kind procurements
    Heavy and Precision engineering
    R&D intensive, with technology yet to be proved
    Site specific in cases
2006-2008: Geared up for ITER roles,
  Domestic Agency created
  Industry engagements
  Country wide engagement if Academics/ R&D under National Fusion Program
2009 onward: Procurements initiated
  R&D, where necessary
  QA-QC organization established
  Industry on board

## Slide 3: Outline
Indian procurements for ITER
Technology Challenges
  Key issues
    R&D and Mock-ups
    Lessons learnt
Broader Perspective of India in ITER
Summary

## Slide 4: Indian Procurements for ITER
Nine Procurement Packages

## Slide 5: Schedule

## Slide 6: Technology Challenges
Cryostat
  ~29 m across, ~29 m tall Vacuum Vessel and 2nd Confinement Barrier of the Tokamak
  Structure Distortion control & Dimensional accuracy (~0.3%) in welding across 25-200 mm thick SS304/304L
  Transportation logistics- manufactured in Segments, Assembly in Site-workshop and Tokamak pit assembly
Cryo lines and Cryo distribution
  Cryolines: Low heat load 1.2 W/m @ 4.5 K & 4.5 W/m @ 80K, Multiprocess lines (upto 7 process pipes). 5 km of cryogenic transfer lines
  Cryo Distribution: Minimizing the pulse effect to 75 kW refrigerator, using a 3 kg/s cold circulator – which requires development

## Slide 7: Technology Challenges
In-Wall Shield blocks
  Ensuring ~9000 block assemblies out of 3,50,000 components
  Establishing corrosion data for IWS under simulated operating conditions
Cooling Water System
  System Design, taking into account concurrent client design evolution
  Execution of manufacturing of >20 km hydraulic piping under stringent quality requirements, Procurement management in phase with construction activities

## Slide 8: Technology Challenges
Heating &Current Drive systems
  ICRF sources: Amplifier chain for power level 2.5 MW/CW at VSWR 2:1 in the frequency range 35-65 MHz
  DNB: Large Ion source generating an accelerated ion current of 60A & divergence of <7 mrad – no precedence.
    Establishing precision engineering for angled grid segments
Power Supply Systems
  High Power Converters with very Fast Transient Response
  SIC compliance for building interfaces for transmission lines
  Reliability and Seismic requirements
Diagnostics
  Evacuated transmission line and spectrometer to ensure low absorption in the 70 GHz-1000 GHz range – A first demonstration

## Slide 9: Cryostat – Fabrication by Segments and Sections
Cryostat: The outer vacuum shell of ITER.
~29 m in dia & ht. Fabricated in Three stages:
Cryostat
Pit assembly at France
Main section assembly in
Temporary workshop (France)
BS Tier-1 | 100%
BS Tier-2 | 100%
LC Tier-1 | 90%
LC Tier-2 | 50%
600 segments
(Indian Factory)
Top Lid
Base Section
Upper Cylinder
Lower Cylinder
Challenges:
Weld processes :: 0.3% dimensional tolerance
Flatness control of pedestal ring
Special handling of large pieces ~ 100 Tons each
Mitigation:
Start with stricter Tolerance at segment level
Mockup (full size) for process
Special Fixtures

## Slide 10: Cryostat- Mockup to establish Process
190 thk Butt weld
190thk
105 thk
40o
Segment
Butt welds
Flatness (Target) : 12 mm max
Achieved : 7 mm
Handling Fixture
DOT Balance Welding for better dimensional control
Base section mock-up
Turning Fixture

## Slide 11: Cryostat- Sandwich like Base Section
Maximum Achieved Profile at Factory within 60 mm
Maximum Achieved Profile at Site within 90 mm
100% volumetric test for vacuum joints,100% Helium leak test, out gassing test, emissivity test as per ITER requirement have been performed successfully.

## Slide 12: Cryostat- Fabrication and Logistics
Lower Cylinder packed for Storage
Cryostat Base-section Assembly
Cryostat Sections Loading
Cryostat Sections Convoy

## Slide 13
Cryo-line and Cryo-distribution
Challenges:
Cryo-line:
Multi-process Transfer lines with heat in-leaks of 1.2 W/m for 4.5 K and 4.2 W/m for 80 k lines
Cryo-distribution: Development of Cold circulators with efficiency >70%, 3 kg/s at 4.3 k with pressure heads <0.5 bar
13
ITER Cryogenic System: Cryoplants of capacities 75 kW at 4.5K, 1 MW at 80K & their supply

## Slide 14: R&D and Prototyping-Cryo-lines
Prototype Cryoline – 1 (INOX): Design, Manufacturing, Installation and Test
MANUFACTURING
DESIGN
INSTALLATION
Total length: ~ 5 km, max.
Diameter of outer vacuum jacket: 1000 mm,
Up to 7 process pipe in single cryoline,
Safety requirements
Min. fluid temp. -269° C
Prototype Cryoline – 2 (ALAT): Design, Manufacturing, Installation and Test
Success in Prototyping allowed quick transition to line production

## Slide 15: ITER Cryo-distribution
The ITER Cryo-distribution System have,
Five Auxiliary Cold Boxes (ACBs)
Cryo-plant Termination Cold Box (CTCB), one
Thermal Shield Cooling System (TSCS), one
Warm Panels (WPs)
All with control and instrumentation.
Typical ACB
(4 m dia. and 6 m height)

## Slide 16
R&D on ITER Cold Circulator (2 of 2)
Test Auxiliary Cold Box
Refrigerator (5 kW @ 4.5K)
R&D for Cold Circulator –Risk mitigation
Two versions of cold circulators (IHI/BNI) had been tested in full parameter space (5.0 kW/ 4.5 K) in a Japanese facility.
Successful R&D established the technology, reduced risks

## Slide 17
Cryogenic Manufacturing/ Testing facilities
Testing Facility
Manufacturing Facility

## Slide 18
Prototype Cryo-lines have been tested and qualified for all ITER requirements and production is ongoing
Cold circulator has been qualified and manufacturing is in progress for the main series
Several Lessons learnt from the prototype test and experiments used as inputs to final design of respective systems
Indian industry expertise created in large volume helium cryogenics transfer
Unique test facility has been developed where Cryo-lines can be tested
Cryo-lines and Cryo-distribution: Outcome of R&D

## Slide 19: In-Wall Shielding Blocks
~80 % Volume between the shells of vacuum vessel is filled,
Borated steel (SS304B4, SS304B7) for neutron shielding
Ferromagnetic steel (SS430) to reduce toroidal field ripple
8809 Blocks/ 1733 Tons
Special Proceses:
Powder metallurgy route used to produce SS304B7 by Carpenter Technology for better grain structure and boron distribution
Corrosion study for all IWS materials under simulated operating conditions (200 deg. C, 24 bar pressure, water, 5 weeks)
Magnetic permeability control during component machining (Maximum 1.03)
Vibration test for fastener anti-rotation design validation

## Slide 20
Cooling Water System (CWS) removes the Heat generated by the Tokamak and its auxiliary systems
The ITER CWS is divided into 4-subsystems
  Tokamak Cooling Water System (TCWS)
  Component Cooling Water System (CCWS)
  Chilled Water System (CHWS)
  Heat Rejection System (HRS)
Cooling Water System
20
Primary
Secondary
Tertiary
TCWS
Aux.
CCWS-1
CCWS-2
HRS
Final heat sink. Also stores the excess heat during pulse operation and rejects the same during dwell period
  Provides chilled water at 6oC, specified flow rate and pressure
  Provides cooling water at 31oC, specified flow rate, pressure and water quality
Some Isolation valves of CCWS-1 are Safety Important

## Slide 21: Cooling Water System- Challenges
20 km of piping network (SS & CS), manufactured under PED protocol – involving ~105 inch dia welds & their volumetric examination
Site constraint of buried piping: Specially designed “pipe in pipe design
Cooling Tower (10 cells) | Avg. 510 MW | Highest heat rejection capacity – Peak ~ 1.2 GW
Plate type Heat Exchanger (14 nos.) | 70 MW each | At the highest range of available technology
Air cooled Chiller (6 nos.) | 450 KW each | Seismic qualification for Nuclear site
Intermediate Hot Basin introduced for Pulse Thermal Load management |  | 
Extensive interfaces with buildings, site network and site construction |  | 
2500 spools, Chillers,
Pumps, Cooling tower

## Slide 22: R&D facility: DNB, ICRF, DNB, Diagnostics
R&D intensive Packages:
  Power Sources for Ion Cyclotron Heating System
  Diagnostics Neutral Beam
  Power Source for Electron Cyclotron System
  Diagnostics Systems of Indian in-kind
  Associated Power Supplies

## Slide 23: ICRF Power Source
  High power Radio Frequency (35 -65 MHz) sources, (8+1 spare=) 9 nos.
  2.5 MW at VSWR 2.0/35-65MHz/CW OR
  3.0 MW at VSWR 1.5/40-55MHz/CW
ITER Specification | CPI, USA (Tetrode) | Thales, France (Diacrode)
2.5 MW/VSWR 2:1/ 2000s | ~1.9 MW/VSWR 1:1/300s | 1 MW/VSWR 1:1/1000 hrs.
BW:±1MHz at 1dB | High Q cavity | High Q cavity
  R&D to establish these specifications initiated in 2010.

## Slide 24: ICRF Power Source: R&D
Two parallel three-stage amplifier chains plus a Combiner Circuit on the output side
Tube qualification phase using single chain (R&D)
  1.5 MW / 2000s / 35 - 65 MHz at VSWR 2.0
  Any phase of reflection coefficient
  Both with Diacrode & Tetrode technologies
CAD Model of one Test Set-up
RF input
RF output

## Slide 25: ICRF Power Source: R&D
Test Rig: 3MW Dummy Load + Mismatch Tx-line
Test facility with Transmission lines/ RF test Load/ Controls/ Low Power RF stages/ Cooling Systems

## Slide 26: ICRF Power Source: R&D
Tested for 35MHz, 45 MHz, 55 MHz & 65 MHz on Match Load
1.7MW/3600s/36MHz
HPA3
HPA2
Chart: High Power Test on Match Load
| 22 | 43.4 | 63.4 | 73.3
Test@36MHz | 500 | 1008 | 1501 | 1705
Test@45MHz | 503 | 753 | 1000 | 1502
Test@55MHz | 503 | 761 | 1016 | 1271 | 1500
Test@65MHz | 503 | 748 | 1033 | 1503
Dummy Load
Tx-line
Controls
Aux. PS
Ref. angle (Deg.) | Poutput (kW) |  | 
 | SSPA | HPA2 | HPA3
0 | 1.0 | 28.9 | 1520
45 | 1.1 | 32.3 | 1501
90 | 1.4 | 47.5 | 1505
135 | 1.9 | 72.0 | 1506
180 | 2.2 | 87.7 | 1503
Mismatch load test: VSWR 2:1 at 65 MHz
Even with VSWR condition, forward power could be kept constant to 1.5MW

## Slide 27: ICRF Power Source: R&D
HPA3
Ref. angle (Deg.) | Poutput (kW) |  | 
 | SSPA | HPA2 | HPA3
0 | 2.73 | 41.3 | 1506
45 | 2.89 | 45.4 | 1506
90 | 4.28 | 74.9 | 1515
135 | 4.89 | 90.7 | 1514
180 | 4.85 | 93.6 | 1515
Dummy Load
Tx-line
Mismatch load test: VSWR 2:1 at 55 MHz
Harmonic level < 35dB
Aux. PS
HPA2
Test run conducted at 55 MHz/1.5 MW/ 2000s for five consecutive RF pulses with 25% duty cycle
Even with VSWR condition, forward power could be kept constant to 1.5MW
Overall electrical efficiency : 55% - 65%, RF exposure limit: < 30 W/cm2
Freq. | HPA3 Pf | HPA3 Pr | HPA2 Pf | HPA2 Pr | SSPA Pf | Gain-3
MHz | kW | kW | kW | kW | kW | dB
35 | 1248 | 4.2 | 79.4 | 16.54 | 4.17 | 11.96
36 | 1497 | 3.22 | 67.77 | 0.29 | 4.17 | 13.44
37 | 1234 | 1.54 | 72.18 | 3.16 | 4.17 | 12.33
54 | 1173.4 | 6.74 | 51.7 | 8.10 | 3.58 | 13.45
55 | 1513.0 | 7.78 | 61.6 | 0.06 | 3.58 | 13.90
56 | 1131.0 | 4.38 | 70.6 | 10.56 | 3.58 | 12.19
1dB BW measurement at 36 & 55 MHz at 1.5 MW

## Slide 28: ICRF Power Source: Path Forward
Next step is to achieve the final specs 2.5 MW/CW at VSWR 2:1 in 35-65 MHz range in a prototype – principal challenge is to stabilize the performance of the combiner during mismatch load condition
Bulk production: Based on prototype RF source, lookout for Indian manufacturing of some RF components

## Slide 29: Diagnostic Neutral Beam (DNB)
Physics
  Acceleration of 60A/96kV H- ion beam
  RF ion source (H-) large extraction plane ion source, with
  Current densities of 30-35 mA/cm2
  Beam (17-20A, Neutral) transport over ~21 m length

## Slide 30: DNB: R&D and Technology
Technology
      Manufacturing angled grid segments, 320 precision apertures, with 0.05 mm positioning accuracies
      Effecting reliable dissimilar material transitions through EBW joints
      High accuracy (~ 0.1 mm/m) of drift control in deep drilled heat exchangers
    Mitigation:
      Set up and operate DNB prototype facility (INTF) along with smaller source facilities ROBIN and TWIN
      Pre manufacturing prototypes to establish realizable parameters and the route to product development
Challenges
Calorimeter
Residual Ion Dump
Neutralizer
RF Ion Source + Accelerator

## Slide 31
DNB: R&D with Ion Source (ROBIN)
RF Power: 30-60kW, Source filling pressure: 0.3-0.6 Pa
Grid bias voltage., 18-26 V, EPSS: ≤10kV, APSS: ≤15kV
Extraction area : 146 apertures 73 cm2
Achieved :
H- ion current density
27mA/cm2 @ e/H- ratio 2.65
22 mA/cm2 @ e/H- 0.88
Beam transmission : 70 – 85%

## Slide 32
Indian Test Facility
32
Transport Duct
Second Calorimeter
Cryopumps
Residual Ion Dump
Neutraliser
Ion source and accelerator
100kV hushing
Calorimeter
HV transmission line
Cooling water system

## Slide 33: DNB: Prototyping and Manufacturing
1:1 prototype of 320 aperture angled grid segment , first of its kind, developed successfully and formed the basis of series production.
Important highlights:
Process development to achieve the desired tolerances
Tolerances achieved
  Aperture positioning (<50 microns tolerance)
  Beam group angles (within 0.011 ⁰ tolerance)
Special aperture shapes for beam optics control

## Slide 34: DNB: Manufacturing
Product realization
Identifying the critical process to be established prior to regular production
Raw mat. development (CuCrZr)
Manufacturing Process Like special welding, Deep hole drilling etc.
Trials
Validation acc. to EN/ISO and functional requirements
Implementation of development outcome in bulk production
Validate the product by Functional Test
( Pressure & Leak test)
Trials
Drilling Depth: 1700 mm
Drift control achieved < 500 micron over 1.7m
EB Welding : CuCrZr to CuCrZr and CuCrZr to Ni to SS 316L
EB Welding : CuCrZr to CuCrZr and CuCrZr to Ni to SS 316L
RID Panel
Heat Transfer element
Drilling Depth: 1.7 m
Drift control achieved < 500 micron over 1.7m
EB welding of OF Cu to OF Cu OF Cu to Ni to SS 316L
Neutralizer Panel

## Slide 35: DNB: Material Development (CuCrZr)
According to ITER Requirement (1) restricted chemical compositions (2) without use of metalloid deoxidizer (conventionally used by global manufacturer)
Restricted compositions improves the manufacturability and reliability of component during operation.
Grain Size < 100 micron
Solution Annealed + Aged
Material successfully developed by ITER India under MoU with NFTDC, Hyderabad. Developed material is being used in ITER Beam Line components.
Fatigue test setup

## Slide 36: Power Supplies for ICRF and Neutral Beam
Several Groups of Power Supplies:
  For Diagnostics Neutral Beam system
    High Voltage converters
    High Current converters
    High power RF
    Nuclear installation
  For ICRF (Tetrode/ Diacrode) System
    High Voltage converters
  For Electron Cyclotron (Gyrotron) system
    High Voltage converters

## Slide 37: Power Supplies: Neutral Beam System
7.2MW, 100kV Acceleration Grid Power supplies (AGPSs) viz. for DNB and SPIDER;
IEC standard Compliant,
Site specific compact termination boards & high voltage building feedthroughs

## Slide 38: Power Supplies – ICRF System
For ICRF sources, Dual output High Voltage Power Supply
                Successfully supported RF source operations of 1.5MW (RF power) over 3600s and beyond
                Exceeds ITER specifications of IC High Voltage Power supply
Driver Stage | 8-18 kV
 | Power : 250 kW
End Stage | Voltage : Δ of 1-9 kV above driver stage
 | Maximum Voltage:27 kV
 | Power : 2800 kW
Layout of Dual Output HVPS at ITER-India lab

## Slide 39: Power Supply: HV Transmission Line
Transmission line
TL supports transport of 15MW over 25m @100kV, also accommodates hydraulics, ~800kW RF lines for DNB test.
ITER TL line is ~100m/ have a large penetration into Nuclear building

## Slide 40
Electron Cyclotron RF Source
ITER-India High Power Gyrotron Test Facility Layout
1
2
3
4
6
5
TP Station
Test Gyrotron & Waveguide
Large flow rate Cooling Supply Header and Manifold
Low Power RF Beam test bench
Power Supplies and HV Protection System
R&D on Body PS using HV switch (35kV/100mA/1kHz modulation):
BPS (35kV/100mA/1msec) as Backup
HV Switch experimental test setup with Electrical Equivalent Load
HV Cubicle
~35 kV @ 100Hz (500k || 1700pF)
In-House developments :
Industrial Grade prototype Interlock Module (CIM):
Full scale Signal Conduction Units :
LabVIEW Application:
Fast & reliable data acquisition & control system
R&D Prototype (CIM)

## Slide 41: Diagnostics
3 Diagnostic systems & 1 Port
X-Ray Crystal Spectroscopy (XRCS) : Spectrometers (X-ray crystals, Detectors , Vacuum chamber), Calibration source, I&C
Electron Cyclotron Emission (ECE) : Michelson Interferometers & Radiometers, Polarization splitter unit, Transmission line, Calibration source, I&C
CXRS : Visible Spectrometers, Detectors, Opto-mechanical components like filters, mounts, I&C
Upper Port- 09 (UP#09) : Complex integration with Interspace Support Structure (ISS) & Port Cell Support Structure (PCSS) etc., and customization for XRCS(Edge)
Diagnostic systems are essential to monitor plasma impurities and emission. Ports are needed to house the Diagnostic systems in position and act as shielding from neutrons.
Fixed Anode X-Ray Source
Prototype Calibration Source

## Slide 42: Diagnostics: Challenges and R&D
Challenge:
Establishing measurement techniques for low loss transmission of ultra wide band frequency range of 70 GHz – 1000 GHz
R&D:
Setting up a prototype experiment – transmission and detector (Fourier Transform Spectrometer) in Vacuum to establish attenuation calibration for a 8 m transmission length for the transmission line attenuation
Transmission attenuation of 8 meters waveguide with two miter bends – establishes a calibration

## Slide 43
Broader Perspective of India in ITER
43
Leap-frog Indian Domestic Fusion Research
Complementary Research in areas India is not producing in-kind
  High Heat Flux Systems: Divertor,
  High throughput Cryopumping
  Magnet technologies
  Tritium Breeding System
  Material Irradiation facilities

## Slide 44
Broader Perspective: Tritium Breeding System
Four heats of RAFM steel each having 200 kg with varying tungsten and tantalum content have been produced.
The aim was to optimize the tungsten and tantalum content with respect to strength and toughness.
Similar processing route and heat treatment conditions have been followed as follows during pilot scale production.
44

## Slide 45
Broader Perspective: Divertor System
Tungsten Mono-Block Fabrication Technology For Divertor
  Hot Radial Pressing Technique Developed for joining tungsten mono-block with copper-alloy tube;
  Mono-block target test mock-up with straight as well as curved copper-alloy tube (Radius Of Curvature=500mm) fabricated;
  Mono-block target test mock-up successfully tested for heat flux up to 20MW/m2;
Tungsten Macro-Brush Fabrication Technology for Dome
  Vacuum Brazing Technique Developed for joining tungsten with copper-alloy substrate;
  Tungsten macro-brush test mock-up with copper-alloy heat sink fabricated;
  Macro-brush target test mock-up successfully tested for heat flux up to 10MW/m2;
Slide courtesy:Samir Khirwadkar

## Slide 46
Broader Perspective: Modeling
ITER-India and IPR are involved in a wide range of modeling activities – some directly for ITER, others relevant for ITER
ACTYS - A state of art neutron activation solver, improved numerical treatment, flexible with new data libraries (ENDF-6 format)
  Coupled with Deterministic transport code ATTILA for SDDR calculations
  Yields activity, contact dose, decay heat, gamma spectrum, rad-waste classification

## Slide 47: Broader Perspective: Relevant R&D centres
Under a specially funded program, centers of excellence have been invited to submit projects on areas of mutual benefit
Has helped in addressing important issues in materials, jointing technologies, physics modelling, diagnostics etc.
Has generated a set of trained HR in important areas of fusion R&D

## Slide 48: Summary
Indian deliverables for ITER have progressed from R&D/ Prototype/ Mock-up to Delivery
Domestic R&D and Prototyping as part of strategy
R&D facilities are operational and producing usable results
Significant part of R&D is through Industry partnership
Creating a young pool of Engineers and Scientists in the field
Collaborating to create future pool for Scientific Exploitation of ITER when it is ready for operation
Opportunity for Indian Industry is also open in ITER procurements at international level.

## Slide 49
49
ITER Collaboration
Institutional Collaborations
ITER
Members
Industries
National
Fusion
Program
(NFP)
Students
Domestic
R & D
Other DAE units

## Slide 51: Thank you