## Slide 1: Measurements with Torsion Balance
DHEP Annual Meeting
4th - 6th May, 2022
Simon Pereira

## Slide 2
Introduction
Damping System
Measurements
Outline of the talk:

## Slide 3
Acknowledgements
Dr. N. Krishnan
Mr. A. Vaidyanathan
Mr. B. S. Mallikarjun

## Slide 4
A general method to measure a gravitational force is to observe the amplitude or frequency of a linear harmonic oscillator.
The oscillator must have a relatively high Q, for measuring a very weak force.
Introduction
Experiments on Gravitation are of mechanical nature.
A simple measurement system for force quantification is a suspended test mass.

## Slide 5
The oscillatory motion is
caused by a restoring torque
which is proportional to the
angular displacement θ.
Torsion Balance: Harmonic Oscillator
A torsion balance is a harmonic oscillator far more sensitive detector of mechanical forces.
+θm
-θm
0
Fixed End
Suspension Fiber
IӪ + k Ө = 0
Mirror

## Slide 6
Optical Lever : Monitoring Motion
Light Source
Detector
Mirror
Suspension Fibre
s
The torsion balance motion is monitored by an optical lever.
Light is incident on a mirror attached to the fibre and is reflected onto a suitable detector at a distance.
The smallest linear displacement that can be detected is 0.1nm.
Primary Optical Lever
Resolution: 3 x10-10 radian
Operating range: ±2.5 x10-6 rad.

## Slide 7
Damping System (Mechanical)
Oscillations of very large amplitude are damped down by mechanical technique. (“Sudden Shifting of Potential Wells”)
The Rotary Motion Drive at the top feed-through assembly is used to damp the initial large oscillation amplitude.
The drive parameters for
the stepper motor are:
angle,
direction and
start time of motor
A set of precisely-timed rotary motions of the top feed-through assembly allows the rapid damping of amplitude.

## Slide 8
Angle / Time Measurements
Secondary Optical Lever is used for fine control of torsion balance motion.
D3
D1 D2

## Slide 9
Angle / Time Measurements

## Slide 10
Amplitude & Period
IӪ + ßӨﹾ+ kӨ = 0
Q(Air) = 44
Q(RV) = 88
Q(UHV)= 2180

## Slide 11
Damping Large Amplitudes
The parameters for stepper motor are determined through accurate time measurements of the optical signal of torsion balance motion.
Stack sequencing program technique is used to transfer drive parameters to software controller.

## Slide 12
Magnetic Induction Drive
System (MID) is used to
damp small amplitudes.
Orthogonally oriented
current–carrying coils
are used to generate a
rotating magnetic field.
In effect, the coil then
functions like the stator, and the mass-bob as the rotor of an induction motor.
Damping System (Electrical)
Oscillations of small
amplitudes are damped
by electrical technique.

## Slide 13
Amplitude Measurements: Two schemes
Vertical Detectors Output
Notes: 13

## Slide 14
Comparison of Amplitude Measurements
Notes: 14

## Slide 15
MID Signals Proportional to the Angular Velocity
Notes: 15

## Slide 16
k = 1.8
k = 1.9
k = 2
Performance of the MID: Angular Velocity
Notes: 16

## Slide 17
Measurements

## Slide 18
Modes of Torsion Balance Motion
Notes: 18

## Slide 19
Acquisition Rate
Notes: 19

## Slide 20
Effect of Environment

## Slide 21
Gravitation Lab (AB-84)
Mirror

## Slide 22
0
2
3
4
1
Optics Axis of Optical Lever is Normal to Mirror face 2
Angle
0
1 = 2 +0
2 = -(2 -0)
ΔT1
Time
T/2
ΔT2
t2
t3
t4
t1
2
3
4
1
Measurement of the Drive Parameters
(1 - 2) = 4
(1 +2) = 20
2
3
4
1
0
The parameters for stepper motor are determined through accurate time measurements of the optical signal of torsion balance motion.

## Slide 23: Large Amplitude Measurements

## Slide 24
We can generate torques that can be:
a) Proportional to the angular velocity.
b) Proportional to the angular displacement.
Magnetic Induction Drive (MID) Control System
Optical lever
Torsion balance
MID coils
Power amplifier
PSD circuit
NI DAQ System
Intel PC
Compute Action
Notes: 24

## Slide 25
Lab-VIEW Programs
T~1 msec
T~ 862 sec
T~86400 sec