## Slide 1
Kameswara Rao, S. Mayekar,
R. Thomas, I. Mirza, M. Shelake,
M. Kumar, S.R. Dugad, G.B. Mohanty
HGCAL R&D and Prototyping Activities at TIFR
DHEP Annual Meeting
May 5, 2022

## Slide 2
LHC Upgrade to High Luminosity LHC
Calorimetry
● Replacement of the endcap calorimeter with high-granularity calorimeter (HGCAL)
CE-E (Electromagnetic)
Active: Silicon
Passive: Cu, CuW, Pb absorbers
13 double-sided layers (full silicon)
CE-H (Hadronic)
Active: Silicon + Scintillator /
Silicon-photomultiplier
Passive: Steel absorbers
7 all-Si layers
Radiation tolerant
High granularity
Precise hit/cluster timing
Enhanced capability for particle flow
reconstruction
Operation at -30°C

## Slide 3
Need to improve the jet resolution for the next generation of calorimeters
At high jet energy, correct association between the tracks and calorimeter cluster is very important, so going for calorimeter with very high granularity
Why HGCAL?
To realize a high-granularity calorimeter (HGCAL), we need: low cost/area active material(s), radiation-tolerant on-detector electronics, high-bandwidth data transmission, powerful FPGAs for off-detector electronics
A largely silicon-sensor-based calorimeter

## Slide 4
Planar p-type DC-coupled sensor pads
simplifies production technology
p-type more radiation tolerant than n-type
Hexagonal sensor geometry preferred to square
makes most efficient use of circular sensor wafer
reduces no. of sensors produced & assembled into modules
8” wafers preferred to 6”
reduces no. of sensors produced & assembled into modules
cost per area is cheaper and simplifies the module mechanics
300mm, 200mm and 120mm active sensor thicknesses
match sensor thickness to radiation field for optimal performance
Simple, rugged module design & automated module assembly
provide high volume, high rate, reproducible module production & handling
About 5K siIicon detector modules need to be assembled in India for a total requirement of ~27K modules (~15 modules per day)
Technical Requirements of HGCAL
8” low-density sensor
192 cells with ~1.1 Sq. cm size
300µm & 200µm active thickness
8” high-sensity sensor
432 cells with ~0.5 Sq.cm size
120µm active thickness

## Slide 5
Silicon sensor glued to baseplate and
PCB containing front-end electronics
Wire-bonding from PCB to silicon via holes
Baseplate
Kapton
Silicon
PCB
Module
parts
Gluing
Wire-bonding
Visual inspection
Electrical testing
Encapsulation
Key steps involved:
Components for an HGCAL Module
5

## Slide 6
Wire-bonder
Delvotec 6400 (used for Belle II SVD)
Working area: 150 x 200, 25mm in Z
Suitable for up to 6” wafers
Coordinate Measuring Machine
Mitutoyo Vision Active 202
Working area: 250x200x150mm
Wire Pull Tester
XYZTEC condor sigma lite
Mini Gantry
Fisnar F7300N
Leica M80 microscope
Motic microscope
Mushashi SM-300SX-3A mini gantry
Optical table
Additional 300 Sq ft of clean-room area
On the way:
  Aerotech gantry
Existing Instruments and Infrastructure

## Slide 7
Wire-bonding Studies
Dummy 8” HGCAL PCB
One of the stepped holes
6” HGCAL module
One of the stepped holes
Part
A
Part
B
Small hole size : 4 mm
Big hole size : 6 mm
Step size of 0.6 mm
Bonds at 120° locations
Automatic program has
been developed for this
application

## Slide 8
Baseplate
Measured :
Flatness: 0.173 mm
Thickness : 0.87 mm
Design values :
Length : 166.940mm
Thickness : 1.4mm
Measured :
Flatness : 0.078 mm
Thickness : 1.262 mm
Design values :
Length : 166.640mm Thickness : 1.194mm
PCB
Measured :
Flatness: 0.05 mm
Thickness : 0.330 mm
Design values :
Length : 166.570mm
Thickness : 0.300mm
Sensor
HGCAL Dummy Module Assembly: Components
Edge to Edge distance details
Baseplate and sensor : 0.185 mm
Base plate and PCB : 0.150 mm
Sensor and PCB : 0.035 mm
166.508mm
166.441mm
166.733mm

## Slide 9
Multipurpose jig
Baseplate aligned on multipurpose jig
Sensor jig
Sensor aligned on jig
Sensor jig placed on
multipurpose jig
Sensor on baseplate
Designed and produced:
1) Multipurpose jig
2) Sensor jig
3) PCB pickup jig
Sensor alignment and placing setup
glue pattern on base plate
Glue: Araldite 2011 slow setting glue
Aligners for sensor
Flatness of baseplate + sensor: 0.265 mm
Thickness of baseplate + sensor: 1.261 mm
Glue thickness: 0.06 mm
After gluing the sensor:
Dummy HGCAL Module Assembly

## Slide 10
PCB aligned on multipurpose jig
PCB pickup jig
Placed PCB pickup jig on
Multipurpose jig
PCB picked up
Placed tape to avoid interference with vacuum cups
PCB Pickup Setup

## Slide 11
Baseplate and sensor on
multipurpose jig
PCB pickup jig
Placed the PCB on multipurpose jig
All together
Glue thickness achieved is around 53 microns between sensor and PCB
Glue spread observed on
above red circles
Placing PCB on Sensor
Glue – Araldite 2011
More details on gluing in the poster of Sukant

## Slide 12
Improved version of glue pattern
(Modules 2 and 3)
Flatness of complete assembly = 0.076 mm
Thickness of complete assembly = 2.529 mm
Need to perform wire-bonding
Followed by encapsulation
HGCAL Assembled module
Assembled module
Glue spread seen on
the sensor at some holes
Optimized the parameters to avoid the glue spread
Wire-bonding
Encapsulation

## Slide 13
Developed HGCAL mechanical prototypes
Completed gluing, wire-bonding and encapsulation studies
Need to develop jigs suitable for main gantry – work in progress
Waiting for the main gantry to be delivered at TIFR needed for the large-scale production of modules
Need to work on the module testing and thermal cycling set-ups
Summary

## Slide 14
Thank you

## Slide 15
Main Gantry and HGCAL modules in Cassette
Procuring this Main Gantry
for mass production
HGCAL module
HGCAL module in Cassette
Values for both endcaps
Silicon
600 m2 of silicon
6M channels