## Slide 1: Overview of the Cosmic Muon Veto for the mini-ICAL detector
Mandar Saraf on Behalf of INO Collaboration

## Slide 2: Outline of the Talk
Background
CMVD Specs
Mini-ICAL at IICHEP
Main Components of the CMV
Scintillator Assembly
CMVD Around the mini-ICAL
Di-Counter Making
Tile Making
CMVD Electronics
SiPM Characterisation and Testing
Simulation Studies of the CMVD
Status

## Slide 3: Background
To minimize cosmic muon background, it is necessary to have the ICAL under a km of rock cover on all the sides
The advantage of shallow depth is many more available sites at a low cost
The feasibility of constructing a Cosmic Muon Veto Detector (CMVD) to study rare events at shallow depth, needs to be validated.
As a proof-of-principle, the CMVD is being built around the mini-ICAL detector at the IICHEP lab at Madurai

## Slide 4: CMVD Specifications
Basically, tag every muon passing through CMVD
Efficiency requirement of 99.99%
False trigger rate to be < 10-5

## Slide 5: The mini-ICAL at Madurai
Mini-ICAL is a 1/600th scaled down version of ICAL
Consists of 4m x 4m x 1.1m electromagnet of 11 layers
Magnet interleaved with 20 RPCs, 2 RPCs in each layer
RPC: 1.74m x 1.85m, 61 strips on x-side and 58 on y-side
Main task: tracking of muons

## Slide 6: Main Components
Active Detector: Extruded Plastic Scintillator – Polystyrene + POPOP & PPO Dopants | From Fermilab’s in-house factory
4.5m to 4.7m long scintillators
50 x 20 mm counter
50 x 10 mm counter

## Slide 7: Main Components continued …
Light Collection: Wavelength Shifting (WLS) Fibre | Kuraray Y-11, Round, 1.4 mm diameter, Multi-clad, non-S type, Peak absorption wavelength: 430nm, Peak emission wavelength: 475nm
Readout: Hamamatsu MPPC (SiPM) – S13360-2050VE, 2 mm x 2 mm active area, 1584 pixels
SiPM Mounted on
a Carrier Board
SiPM
Fibre

## Slide 8: Scintillator Assembly (Di-counter)
Cross sectional view of a Di-Counter Assembly
Blown up view of a Di-Counter Assembly

## Slide 9: Components of designed and manufactured locally
Component | Qty | Mfr
Counter Mother Board | 712 | Pvt Mfr
SiPM Mounting Block | 712 | Pvt Mfr
Polyurethane Gasket | 712 | Pvt Mfr
Fiber Guide Bar | 712 | Pvt Mfr
Threaded Sleeve | 1424 | In House
Sleeve Pin | 1424 | In House
SiPM Panel as received from Hamamatsu

## Slide 10: CMVD Around the Mini-ICAL
CMV covers mini-ICAL on 3 sides and top
Each side/top consists of 3/4 layers of staggered plastic scintillator strips
Total 712 scintillator strips of length 4.5 to 4.7m

## Slide 11: Scintillator Staggered Arrangement

## Slide 12: Di-Counter Making
Glue: Fevitite Superstrong

## Slide 13: Tile Making

## Slide 14: Electronics – Counter Mother Board
Counter Mother Board

## Slide 15: Electronics – Devices Studied
Features | CMVD Spec | VMM3a | Petiroc 2a | Triroc 1A | DRS4
Channels | 64 or 32 | 64 | 32 | 64 | 9
Architecture | LG Charge, HG Charge and Timing | Amplifier, shaper, Peak Detector, TAC and ADCs, | Amplifier, LG CR-RC Shaper, SCA/ Peak detector, TAC, ADCs | Amplifier, LG and HG CR-RC Shaper, SCA/ Peak detector, TAC, ADCs | Domino Ring waveform Sampler, 1024 cells, up to 5GHz sampling rate
AMP gain | Reasonable gain | 0.5, 1, 3, 4, 5, 6, 9, 12, 16 mV/fC | Fixed gain 40 | 13mV/p.e positive 16.5mV/p.e negative | NA
Shaper peaking time | Tunable to capture Peak amplitude | Adjustable 25, 50, 100 and 200ns | Adjustable 25, 50, 75 & 100 ns | Adjustable 10ns to 1.28us (10ns res) | NA
ADCs | 10 bit or higher | 10 bit – Peak, 8 bit – TAC, | 10 bit – Peak or SCA 10 bit - TAC | 10 bit – Peak or SCA 10 bit - TAC | None, analog output
Charge Dynamic range & resolution | 50 pC with res of 0.04 pC | 0.1 to 2pC resolution : less than 1fC | 0-480 pC i.e. 3000 pe | HG : 100 pe, LG : 3000 pe, | 0.1pC, 28pC
Timing resolution (With 40 MHz ref clk) | 100ps – 150ps | 97 ps | 100 ps | 88 ps | 1 ns
Multiplexed Analog out | Required if ext ADC needed | PDO, TDO, MO (amp all 64 channels) & more | LG Peak or SCA out | LG (Peak or SCA), HG (Peak or SCA) and TAC | Available
Trigger Out | ToT or ORed Time or charge trigger | Disc out all 64 | Disc out all 32, Charge OR32, Time OR32 | Time trig ch, Charge OR64, Time OR64, | NA
Detecting method | Capturing and digitizing of CMVD signals on RPC stack muon trigger. | L0 mode (refer VMM document) | Local trig using 32 ch Disc out and issue hold signal when RPC trigger and local trigger matches | Issue Hold signal when RPC trigger comes, Note: shapers peaking time to be set close to RPC trigger latency. | Pre-sampling of analog signal, readout through ADC on ext trigger
LG, HG and TAC | At least 32 channel LG charge, HG charge and Timing from one card. | 32 Ch in LG peak and 32 CH in HG peak, TAC only with HG. | 32 Ch LG charge INT ADC, 32 CH TAC INT ADC. | LG 64 ch charge INT ADC , HG 64 Ch TAC INT ADC and MUX HG charge (peak or SCA) EXT ADC | NA

## Slide 16: Electronics – DRS4 Based on DAQ

## Slide 17: SiPM Characterisation
TIA

## Slide 18: Simulation studies of CMVD
Simulation to measure the efficiency of CMVD
  Based on inputs from the experimental results
  Effect of multiple scattering and dead spaces due to electronics and gaps
Generate inputs for designing of front-end electronics

## Slide 19: Status
~3500 SiPMs procured and tested
8 km of WLS fibre procured
All small components, FGBs, SMBs, Threaded Sleeves, Pins Screws, etc. procured or fabricated locally
Counter Mother Boards deigned and pilot production carried out
Main DAQ system design is underway
 | Required | Fabricated | Tested
Di-Counters | 356 | 359 | 267
Tiles | 89 | 64 | 4
CMBs | 712 | 20 | 20
Wall Structures | 4 | 4 | 2
DAQ System | Under Design | NA | 

## Slide 20: Thank You
Q & A …

## Slide 21: Extra

## Slide 24
Di-Counter Assembly Jig