## Slide 1: Trigger electronics technologies for current and future particle physics collider experiments
D.Acosta
University of Florida, USA
Home of the “Gators”

## Slide 2: Outline
Context: Particle physics at the Large Hadron Collider
  Our data source
Trigger systems and current hardware
Future Developments and Outlook
  HL LHC trigger upgrade
  Machine learning (AI) in triggers
  FCC
Summary
Notes: Most of the talk on the future

## Slide 3: The CERN Large Hadron Collider (LHC)
CERN
CMS
A 27km proton-proton collider
and heavy ion collider Operations began late 2009
Collision energy: 14 TeV design
2010-11: 7 TeV
2012: 8 TeV
2015-18: 13 TeV
ATLAS

## Slide 4: Where the Higgs Boson Was Discovered (2012)
Fundamental field and particle from the unified electroweak theory of Weinberg, Salam, and Glashow via the Brout-Englert-Higgs mechanism
  Hγγ HZZ4l

## Slide 5: And now couplings to fermions confirmed in 2018!
Observation of ttH
  Best fit 𝜇ttH = 1.26+0.31-0.26
Observation of Hbb
  Best fit 𝜇Hbb = 1.04+0.20-0.20
Observation of H𝜏 𝜏
  Best fit 𝜇H𝜏𝜏 = 1.24+0.29-0.27
Notes: About 15% precision measurement

## Slide 6: The “Compact” Muon Solenoid (CMS)
+ Trigger and data acquisition systems: 40 MHz beam crossings filtered to 100 kHz at Level-1 and then record 1 kHz after High Level Trigger
3.8T
15m
Notes: Zoom into one endcap for Scale

## Slide 7: CMS Experiment, Opened
3.8T solenoid (2.7 GJ!)
beampipe
Muon detectors
~100M electronic channels.
Big data and big computing needs.
Notes: In a vast cavern 100m down

## Slide 8: Data Acquisition for Particle Physics Experiments
“Data acquisition” is the collection and storage of data recorded by a set of detectors comprising an experiment
Typically needs a “trigger”, a set of conditions (a “menu”) by which to initiate the sequence to digitize data from analog sensors (or read out from local buffers) and record to memory/disk/tape storage
This trigger can be:
  As simple as a single signal pulse indicating the presence of a particle passing or interacting in an experiment
  But nowadays as complicated as partial reconstruction of a proton-proton collision from the detector data, and a long list of criteria to decide whether to store or not

## Slide 9: Triggers for Particle Physics
Why is a trigger needed?
  Too much data to continuously stream to disk for storage and/or computer processing reasons
    For example, an LHC experiment generates ~100 terabytes of data per second!
  Electronics digitizing data may induce “dead time”
    A period of time when further data cannot be recorded and thus the experiment is insensitive to incoming data, wasting collider luminosity.
It is really the first step of a data analysis
  The trigger is an online data filtering system
  But irreversible – can’t go back to data you did not record
    e.g. Throw away 99.998% of all data… (keep ~1000 Hz)
    But, don’t throw out the baby (Higgs boson) with the bath water!

## Slide 10: LHC Cross Sections and Rates
 Total collision rate: 2 GHz
for L =2 x 1034 Hz/cm2
 Higgs boson rate: 1 Hz
arXiv: 1002.0274v2
 b quark rate: 10 MHz
 W boson rate: 4 kHz
Keep
Billions of collisions per sec but at a beam crossing rate of 40 MHz
We cannot keep all physics processes in order to collect enough data on interesting rare processes

## Slide 11: Trigger Systems at Collider Experiments
Typically segmented into multiple levels, with decreasing input rates and longer processing times (latencies)
Level-1:
  Custom electronic designs for maximum throughput (TB/s) and shortest latencies (microseconds). i.e. specialized computing
    Custom chips (ASICs) and programmable logic (FPGAs)
  Processing logic done in a maximally parallel way for shortest latency
  Processing is pipelined, meaning processing is segmented into steps of a certain clock period (beam crossing), and intermediate results are registered after each step
(Possibly) Level-2:
  Combination of custom electronics and commercial computing equipment
Level-3:
  Commercial computing clusters of up to O(10 000) CPUs with up to seconds per event processing time
    i.e. Parallelized with different collision events processed with different CPUs, but mostly sequential within a CPU core

## Slide 12: Example: CMS Trigger Architecture
Only two levels:
  Level-1: custom electronics to reduce the data from a collision rate of 40 MHz to no more than 100 kHz for the detector readout electronics, with only a 4 microseconds latency (buffer depth)
  High Level Trigger (HLT): event filter farm comprised of commercial CPUs running software to further reduce event rate to storage to an average of ~1 kHz (for run 2)
In a nutshell, it is a real-time data processing system
1 kHz
40 MHz
Notes: HLT rate is increase since Run 1, factor 2 increase in lumi, and from sqrt(s)

## Slide 13: Current CMS Level-1 Hardware
Xilinx Virtex-7 FPGAs
Up to 10 Gbit/s optical links
uTCA telecommunications form factor and infrastructure
MTF7

## Slide 14: Reprogrammable Digital Electronics for Level-1
Field Programmable Gate Arrays (FPGAs)
  Off the shelf component, not custom like ASICs
  A silicon “breadboard” of configurable logic gates, memories, transceivers, Digital Signal Processors (DSPs), registers,
Digital logic at a lower level than a CPU because the logic is not pre-specified
  Although you could program an FPGA to become a CPU in principle...
State of the art: Xilinx Ultrascale+, 16 nm technology
  Up to 1.7M Configurable Logic Blocks (CLBs) - 6 bit LUTs
  Up to 12K DSP slices
  Up to 128 transceivers at up to 32 Gbit/s
  Up to ~500Mbit of RAM
Millions of logic gates!
Terabits per second!

## Slide 15: High Level Synthesis
Latest way to develop firmware is through high level languages like Xilinx Vivado HLS and OpenCL
The HLS tool consists of a special type of compiler which allows the designer to implement their designs using a high-level language and then translates the high-level language description into a hardware description language such as VHDL/Verilog
Allows use of mainstream software languages such as C/C++ as the design entry
  Enables developers to reduce development time
  Allows simulation of exact design to run within a C/C++ environment (e.g. the code base of your experiment)

## Slide 16: Example Level-1 Algorithm: Muon “Track-Finding”
  Track-Finder links receive track segments and FPGA builds into distinct tracks through pattern recognition logic in firmware
    2-D tracks for barrel region, 3-D tracks for endcaps
  Performs a momentum measurement using the deflection of muon in the magnetic field (complicated in endcaps)
Use angular deflection in magnetic field to measure momentum
Pt = f(Δφ12, Δφ23 , η )
Notes: Quick is 25 ns

## Slide 17: HLS Usage: Kalman Filter Tracking
Firmware for barrel track-finder uses 25-60% of Virtex-7 FPGA
Tested as default trigger in Run 2 near end of pp program with cosmics and pp collisions, with good results

## Slide 18: Endcap Muon Track-Finder, 2016+
12 μTCA double-module processors
  Xilinx Virtex-7 FPGA and memory
PT calculated from Reduced Latency DRAM
  1 GB  30 bit address space
  +8 address bits (only) over previous CSCTF
Algorithm
  Machine Learning (more later): Boosted Decision Trees (BDTs) used for regression to assign momentum using Δφ bending between 4 detector stations, and Δη, and bend angle in first station
  But note, algorithm is run offline and stored as a look-up table (LUT)

## Slide 19: CMS Data Acquisition & High Level Trigger
System accepts up to 100 kHz event rate (100 GB/s bandwidth) from detector electronics (“FEDs”)
Event builder
  Run 1: Myrinet network switch
  Run 2: Infiniband network switches
High Level Trigger
  ~26 000 CPU cores
  Software-based algorithms
  Output bandwidth ~GB/s
  Average selection rate ~1000 Hz
  ~300 ms/event processing time available for 100 kHz input rate

## Slide 20: The CMS High-Level Triggers
Reduces rate from 100 kHz to ~1 kHz (LHC Run 2)
Starts with a data sample already enriched in physics!
  Level-1 already applied a factor 400 background rejection
The HLT algorithms work with higher precision data than that used by Level-1
  No I/O limitations
  Very close to offline analyses
New detector additions: the precision silicon pixel and strip tracking systems
  Readout is too slow for Level-1 trigger
  Much higher precision on the momentum of charged particles (2% vs. 20% for muons)
  Much better rejection against fake electrons from π0s (with track requirement)
  Better precision of jet energies
More sophisticated algorithms can be run
  Jet algorithms (including jet substructure)
  Lepton isolation
  B jet tagging (from track impact parameter measurements)
  Topology and invariant mass cuts

## Slide 21: Trigger Menus
A trigger “menu” represents a (large) set of selection criteria for the broad physics program of the experiment, e.g.
  Entrée 1: 2 muons of opposite charge, one with PT >17 GeV and one with PT >8 GeV
  Entrée 2: “jets” with a total scalar jet HT > 500 GeV
    These entrées are often referred to as “trigger lines”
Crudely speaking, O(1) trigger per analysis topic
  Some triggers are very general and serve many analyses (preference)
  But often many “backup” triggers are required for the control regions of specific analyses, which increases the total count
Separate L1 and HLT menus
  L1 menu has ~300 items for CMS
  HLT menu has ~600 menu items for CMS.
    Each trigger item has prerequisite L1 “seeds”

## Slide 22: CMS HLT Menu Snippet

## Slide 23: Future of Triggers

## Slide 24: The High Luminosity LHC
L  7.5 x 1034 Hz/cm2
Pileup: 140-200
We are here
LHC energy upgrade to 14 TeV, followed by luminosity upgrade
4X higher luminosity and pileup, accrue 10X larger data sample, add new high granularity detectors to expts.

## Slide 25: CMS HL LHC Detector Upgrades
New detector systems with higher granularity to handle unprecedented pileup and radiation
Endcap calorimeter,
Triggerable silicon tracker,
Timing detector,
more muon coverage,
electronics
TIFR involvement

## Slide 26: HL LHC Trigger Challenge
Cope with higher collision rate and particle densities, yet maintain thresholds in trigger menu similar to LHC in order to retain sensitivity to electroweak scale physics
  Want to benefit from the increased luminosity
  Must improve rate reduction at no cost to efficiency
    Need better trigger algorithms
Add sensitivity to new physics scenarios, such as from long-lived heavy particles
  Displaced “muons” from new particle decays
    Particles displaced from the nominal collision vertex
  Heavy stable charged particles
    Muon-like particles traveling with β < c and highly ionizing

## Slide 27: CMS HL LHC Trigger Requirements
Increase Level-1 Trigger output rate: 0.1 0.75 MHz
  Better sharing of rate reduction between Level-1 and HLT
Increase Level-1 decision latency: 4μs  12.5μs
  More processing time for more complex algorithms
    Both requirements imply changes to detector front-end electronics (deeper data buffers, higher bandwidth)
Adding inner detector tracking (silicon strips) to Level-1
  Better performing Level-1 Trigger
  Recovers capability that Tevatron experiments had a generation ago (albeit with much less data throughput demands)
  Major new change to make silicon detector systems fast enough for trigger purposes, and yet still able to power and cool
Increase DAQ storage rate to disk: 1  7.5 kHz

## Slide 28: HLT @ HL LHC
If we have full tracking at Level-1, what is left for HLT to achieve another factor 100 reduction in rate reduction?
Tracking
  Has access to pixel hits in addition to strips  b jet tagging
  HLT so far has not had the resources to perform global tracking for the entire Level-1 bandwidth
  But with the Track-Trigger, the full collection of tracks can be accessed by HLT for every event and used even if Level-1 did not need to for all triggers to achieve rate reduction
    This is what ATLAS experiment plans with its Fast Tracker (a custom “accelerator” for it computing processors)

## Slide 29: CMS Proposed Level-1 Trigger Architecture
New
New
 Detector improvements
Match tracks with calorimeter clusters and muons
Dataflow

## Slide 30: Track Stub Finding in new CMS Tracker
Stub efficiency vs. PT for various layers and disks 
Barrel
Coincidence of hits in a double layer of silicon helps reduce data bandwidth from detector
Require a coincidence within a pattern, limits PT > 2 GeV
  < 3% of tracks
“Push” design: all found stubs forwarded
  3-4 stubs/module/BX for Barrel layer 1
  ~10K stubs/BX
  O(50) Tbps !

## Slide 31: Silicon Track-Finding
Tracking at Level-1 is a feature that Tevatron experiments had...
For CMS it is a “push” design – all stubs taken every beam crossing, whereas ATLAS experiment has a region of interest seeded design
Latency: ~5 μs allocated for CMS design
Multiple approaches under consideration to find tracks:
  Pattern-based: Track patterns stored in Associative Memory chips
    Target implementation in custom ASICs to store large number of patterns (~1 G overall)
  “Tracklet” approach: Track building from stubs with pair-wise layer extrapolations
  Hough transform: transformation of track patterns to clusters in transformed space
    Target implementation in FPGAs
Generally implemented with time-multiplexing of the input data (round-robin of event data to processors)
All followed by a track-fitting stage to extract track parameters
CMS options
ATLAS design

## Slide 32: Particle Flow in Level-1 Trigger
“Particle Flow” is the optimum combination of tracking momentum and calorimeter energy measurements
  Used successfully in CMS HLT and offline analyses
Full exploitation of tracking at Level-1 for HL LHC proposed
  Requires matching all calorimeter clusters to all tracks, removing clusters not attached to the primary vertex, and replacing cluster energy with track parameters for rest
  Significantly improves the jet and hadronic energy flow measurements at CMS. Also reduces pile-up dependence.

## Slide 33: Technologies for the HL LHC Trigger
Optical data links @ bandwidths up to 28 Gbit/s, and possibly 56 Gbit/s (from 10 Gbit/s currently)
  Much more data to ship around
Ultrascale FPGAs
  O(100) data link receivers and transceivers
  Factor 4 or more logic resources per chip than currently, to tackle more complex algorithms
Large Memory banks (DDR4)
Advanced Telecommunication Computing Architecture (ATCA)
  Standardized shelf technology
    Current CMS trigger uses μTCA, a daughter card of ATCA

## Slide 34: R&D on State of the Art Optical Links
Test of Firefly optical links via PRBS-31 at 14, 26, and 28 Gbps with Xilinx Ultrascale+ FPGA evaluation board XUSP3S
Add transmission through a 15 cm differential line and Impel connectors
Also through a 15 cm Firefly optical fiber.
Through RTM connectors
Through fiber interconnect
Realistic connection schemes on boards

## Slide 35: Optical Link R&D Eye Diagrams
An eye diagram is the envelope of rising and falling signals on a line at the clock transition
  Need open “eyes” so as not have errors when latching signals
  Tested with pseudo-random test vectors (PRBS)
Firefly works at tested 14, 26, and 28 Gbps
  Can be used on RTM or mezzanines
  Can be attached to FPGA via high-speed connectors or cables

## Slide 36: Next Generation Trigger R&D Prototypes
Serenity: Two Xilinx Kintex FPGAs, and 72+72 Tx+RX optical links at 16 Gbit/s;
TIFR developing a VU9P version
Embedded
Linux
Module
(ELM)
Main FPGA
Eth
switch
IPMC mezzanine
Pt LUT
mezzanine
Optical links
Optical links
Optical links
LVDS I/O
Optical links
APx: Xilinx VU9P FPGA, and 100+100 Tx+RX optical links at 28 Gbit/s, 128 GB RAM

## Slide 37: Next Gen Prototype Architecture: APx
Main board + RTM
Large UltraScale+ FPGA
  Typically targeting Xilinx VU9P
Embedded Linux mezzanine for control functions (Xilinx Zynq)
IPMC mezzanine (another Zynq+Linux)
Gigabit Ethernet as main control interface
  Option for 10G or 100G(?) Ethernet
~100 optical links total
  RX+TX each, Up to 28 Gb/s each
  On main board with FPGA for cleanest high-speed signal path and widest airflow
128 GB DDR4 RAM
Embedded
Linux
Module
(ELM)
Main FPGA
Eth
switch
IPMC mezzanine
Pt LUT
mezzanine
Optical links
Optical links
Optical links
LVDS I/O
Optical links
Main board screenshot from T. Gorski

## Slide 38: AI in Trigger Systems
Machine learning algorithms (aka Artificial Intelligence) have been used in particle physics analyses for decades
  First in a limited capacity, but now extensively!
  Most Higgs boson measurements make extensive use of machine learning to extract the signal over large backgrounds
Starting to be incorporated into the Level-1 Trigger
  For example, a Boosted Decision Tree algorithm was used to train the muon momentum regression in the CMS endcap muon Level-1 trigger and the results were encoded into a large memory
  But with current technology, neural networks (and BDTs) are possible to implement directly into the FPGA logic fabric, opening many powerful possibilities!
  Unique use of AI is for very fast inference, < 1 microsecond
Let’s discuss both approaches

## Slide 39: Machine Learning for Regression
Our trigger application is somewhere between a classification problem and a regression
  We want to know the particle momentum above or below a specific threshold, but for multiple thresholds (just not an infinite set)
For our BDT approach we use a transformation + loss function to focus on low momentum events (whose mismeasurement to high momentum drives the rate)
  Target= 1/pT makes differences in low pT count more in loss
  Loss = |1/pT,meas – 1/pT,true|2 , but studied other loss functions
    Focus on low pT more  lower rate (good), lower effic. (bad)
    Focus on low pT less  higher rate (bad), higher effic. (good)
With redundant measurements (4 detector stations), ML can identify outliers (e.g. high momentum muon showering) and reject them to keep efficiency high
  We used to have to introduce ad hoc “human” algorithms to recover effic.

## Slide 40: Calculation by Memory Look-up
A brute force approach to do a calculation quickly is to use a memory look-up table (LUT)
  A “cheat”. Don’t really calculate it online at all (no CPU involved real-time)
  Instead, pre-calculate offline your quantity from inputs using whatever algorithm you want and with as much computing resources you have!
    But you must do this for every possible address input to the memory
    Memory must accommodate fast random addressing, not just quick block reads, to satisfy Level-1 Trigger timing (25 ns clocking)
The challenge:
  You must squeeze all the data for your track fit into the memory address
    N bits of of data requires a memory of 2N addresses
Pt LUT
(RAM)
PT
Δφ12
Δφ23
η
Track type
 Address 
 Data 
N bits
2N words

## Slide 41: The LUT Hardware
  Current generation CMS trigger
    1 GB of Reduced Latency DRAM
      30 bit address space
    50 ns random address look-up
  R&D for next generation
    128 GB of DDR4 memory
      37 bit address space
    Result in 54 ns

## Slide 42: Encoding and Training the Result
First pack (compress!) your input data in an optimal way
  This is a data science in itself!
  Here are muon track variables for the CMS trigger, for example:
Train the AI algorithm
  For this example, used a Boosted Decision Tree for a regression on the momentum of the track
    TMVA package of root.cern.ch
  Trained on simulated track trajectories in the experiment
  Care taken on choice of a loss function (penalty) so that performance is optimized for application (efficiency, rate)
Apply trained algo to all 230 input combinations and store in file
ACAT2017 proc.
Many variables, but few bits each

## Slide 43: How did it do for the current CMS trigger?
Trigger rate versus regions of the detector:
Endcap regions significantly improved with AI algorithm

## Slide 44: Next Gen: Neural Network Machine Learning
Loosely inspired by how neurons work in the brain
  Neurons fire signals to other connected neurons, amplifying the signal to some degree in the process
In a neural network, the inputs are multiplied by a set of weights, and the product is sent to a nonlinear activation function
  e.g. tanh, sigmoid, relu, etc
A Deep Neural Network has many hidden layers
  e.g. Convolutional neural nets for image recognition
inputs
Hidden layers
outputs

## Slide 45: Neural Network Machine Learning
The Neural Network must be trained with large sample of examples of desired classification (just as with the BDT algorithm)
  Cat vs. not a cat; Higgs boson vs. not a Higgs boson; momentum =10 vs. momentum =100
  Weights are determined from back propagation and using a specific loss function (penalty)
The application of trained network is known as inference
  And Level-1 needs it very fast!

## Slide 46: Neural Networks in FPGAs
The
  Implementation of fast neural network inferences into FPGAs:
    arXiv:1804.06913v2
  Converts results of a trained NN into Xilinx Vivado HLS firmware
  The Xilinx DSP slice offers a 27 x 18 bit multiplier
  Some Xilinx devices 
  HLS4ML optimizes use of DSP slices
    #bits, sequential re-use of slice, etc.
Basic DSP slice

## Slide 47: Neural Networks for Momentum Regression
The Level-1 trigger needs fast inferences
A neural network implemented within an FPGA alleviates the bottleneck of the memory look-up table approach
  No loss of input variable precision
  Can achieve better performance, and still fit into target FPGA
Prototyped one for CMS muon trigger for HL LHC
  3 hidden layers, not too deep
  Momentum regression output
  and a signal/pileup background classifier (01, where 0=bkgnd and 1=signal)
Output:
pT, PU discr.
64 nodes
~40 inputs
32 nodes
16 nodes
Notes: Feed forward

## Slide 48: How did we do with performance?
NN algorithm, in combination with new muon detectors for upgrade, achieves better performance
  4X rate reduction
  Higher efficiency
LUT
NN
75% rate reduction
Work in progress

## Slide 49: HLS4ML FPGA Implementation
Take results from trained NN and use HLS4ML to generate firmware
  Use 18 bit precision for inputs & output (mantissa and exponent)
  Xilinx Virtex-7 690T target FPGA
  Clock of 250 MHz
Fits within FPGA resources, and latency ~160ns
Tested in hardware, results agree with expectation

## Slide 50: Test Patterns

## Slide 51: Back to AI: Other Tasks/Signatures amenable to NNs
Current application applies to reconstructing track momenta
  Mostly a regression task
But there are also pattern recognition tasks with unique signatures in the detectors from proton collisions:
  Possible new particles and their decays beyond what we know or expect from our theories
    Signatures where the particle appears not to come from the collision point
    Or decays rich in a certain type of particle (muons)
Could imagine training AI to identify these types of signatures from the input data
  A sort of particle decay “face” recognition!

## Slide 52: Neutrino Experiment example
  Convolutional Neural Net to determine what type of neutrino interaction
arXiv:1604.01444v3
From software to firmware?
Notes: Software based

## Slide 53: Heterogeneous Computing Platforms
Acceleration from GPUs helps CPUs in some compute-intensive tasks
  For example: the most computationally heavy step for AI is the training.
Now FPGAs are also available as accelerators
  With particular interest for machine-learning
  For example:
    Microsoft Azure cloud computing
    Amazon Web Services (AWS) cloud – F1 instance
Could blend the functionality between some fast tasks for particle physics data processing, like Level-1 trigger systems for selecting data for storage, and traditional computing platforms for software-based data analysis
  One node for multiple trigger levels?
  In-situ AI training based on data vs. simulation?

## Slide 54: Trigger-Less?
Replace all front-end electronics to be able to send all data to software-based High Level Trigger
  Current LHCb upgrade
  Would be much more challenging for a large “4pi” experiment like ATLAS or CMS

## Slide 55: Future Circular Collider (Hadron)
Goals:
  Higher energy: ~100 TeV
    Explore high energy frontier
  Higher luminosity: 5-30 x 1034 Hz/cm2
    High precision, e.g. Higgs boson couplings
Trigger Challenges:
  Pileup: O(1000) pp collisions per beam crossing (20X more than LHC)
  Higher detector channel count from increased granularity
  Radiation levels in tracking volume
Requires new ideas and new technologies to tackle next order of magnitude!
  And a new generation of physicists and engineers!

## Slide 56: Summary & Outlook
Showed how AI algorithms can be embedded into electronic processor designs for fast applications such as the CMS Trigger
  Memory look-up for storing results, or
  Direct implementation of neural networks into FPGAs
Our unique AI requirement is sub-microsecond inference
Some of our hardware R&D embedding this were shown
Some concerns we have for NN applications to a real-time system is what happens when the network is presented with data not seen in training sample?
  Working on ensuring that training is robust, so results are predictable
Next big challenge is how to utilize FPGAs as accelerators for training in addition to inference

## Slide 57: Thank You
Canoeing in the Mangroves of the Florida Everglades

## Slide 58: Backup

## Slide 59: Example: Cathode Strip Chamber
Part of the muon detection system
  A muon is a heavier version of the electron
540 wire chambers on 15m disks at each end of experiment
About 2500 front-end electronics boards
About 1M readout channels

## Slide 60: HLT Tracking
HLT uses regional tracking of strip and pixel hits in an iterative approach for different track categories
In order to mitigate effects from pile-up, the CPU processing time has been reduced:
  Optimization of code
  Primary vertex constraint in all iterations
  Optimization of region pT cuts
  Removal of last two tracking iterations (of 5) except for displaced track triggers
Overall a factor ~4 reduction in CPU time per event from LHC Run 1
Notes: Iter 0: prompt high pt tracks; Iter 1: prompt low pt tracks; Iter 2: recover prompt high pt tracks

## Slide 61: Optimized Measurements: “Particle Flow”
The precision of charged particle tracking measurements of momentum exceeds that of calorimeter energy measurements at lower momenta
  Therefore, combine in an optimal way
Requires mapping all charged tracks to energy clusters in the calorimeter to produce “particle flow” objects
  ECAL only depots  electrons
  ECAL+HCAL  charged hadrons
  ECAL only, no track  photons
  ECAL+HCAL, no track  neutral hadrons
This is at HLT for CMS as well as for offline analyses
  Improves jet energy resolution, and missing transverse energy resolution

## Slide 62: More Recent ASICs: Associative Memory
Associative Memory ASICs (VLSI)
Content Addressable Memory
  Think of it as a very, very large address space memory, but only addresses corresponding to interesting patterns (e.g. physical) deliver data out (so very sparse)
Used in HEP to store a large number of possible patterns from tracks propagating through silicon tracking system
  CDF Silicon Vertex Detector
  ATLAS Fast TracKing (FTK) system
NIM A 518 (2004) 532
CERN-LHCC-2013-007

## Slide 63: AM ASICs
ATLAS FTK AM chip
3D stacked silicon technology also in R&D
CERN-LHCC-2013-007
Proposed vertically integrated pattern recognition AM
- Higher speed, density
Particle trajectory
T. Liu et al 2015 JINST 10 C02029

## Slide 64: Boosted Decision Trees
A decision tree repeatedly splits a dataset into smaller subregions based on features in that dataset
  Similar to what particle physicists were doing already by hand (“cuts” on the data set)
The Boosting takes an ensemble of decision trees, where each subsequent tree tries to improve upon the error from the previous one
  Each tree gets a weight, and the ensemble gets the weighted sum

## Slide 65: Abstract
  Trigger systems for experiments at particle physics colliders must analyze and select from an enormous amount of raw data generated from billions of collisions per second only a tiny fraction for storage, all within a processing time of just microseconds per collision event. A two-level processing system based on field programmable gate arrays in the first level and CPUs for the second level must implement algorithms to identify and measure particles coming from the collisions with high precision, and retain only those collisions most interesting to the physics program of the experiment. This talk will review the challenges and electronic solutions for such trigger systems, including the use of state-of-the-art technologies and machine-learning artificial intelligence algorithms to extract the best performance. The outlook toward future upgrades and experiments also will be presented.
Notes: 50 min + 10min questions