## Slide 1: DEVELOPING TECHNOLOGIES FOR INDIA'S DELIVERABLES TO ITER
Aparajita Mukherjee
On behalf of the ITER-India Team

## Slide 2
Areal view of ITER site, France
ITER Machine

## Slide 3: ITER-MACHINE IS BEING BUILT MOSTLY BY IN-KIND CONTRIBUTIONS FROM SEVEN PARTNERS
45.46% from EU
9.09% each from China, India, S. Korea, Japan, Russia & US
Each component of the machine will be delivered either by
Single ITER partner
OR
More than one partner
The ITER machine (peep inside)

## Slide 4
ITER IN-KIND CONTRIBUTION PACKAGES:
Mainly Two Types
Design responsibility is ITER’s
First of its kind
Any of the partner supports ITER to reach on a final design
ITER owns the responsibility of performance
Post manufacturing any modifications required are ITER’s responsibility in terms of cost and schedule
Design responsibility is with the partner responsible for delivery
Functional requirements and boundaries defined by ITER
Partner responsible has to engineer, fabricate and demonstrate the system as per the requirements
Any modifications and the resultant impact on schedule and cost is partner’s responsibility
Build to Print (BTP)
Functional Specification (FS)

## Slide 5
The partner, for either of the design approaches mentioned, is responsible for the successful manufacturing and delivery of the package to ITER
Challenges :
Many of the components are the first or largest of their kind;
In addition; Stringent quality requirements
Nuclear site requirements in line with French safety rules and regulations
Components have to survive the life time of ITER as maintenance is only possible to a certain extent and with remote handling tools
Manufacturing of most of the components underway

## Slide 6
INDIA’S IN-KIND CONTRIBUTION TO ITER
9 packages with multi-dimensional technology development |  |  | 
Heavy & precision engineering – material and manufacturing intensive | 1 | Cryostat (BTP) | Machine jacket to ensure vacuum environment for SC magnet
 | 2 | In Wall Shields (BTP) | Neutron shielding
R&D oriented and technology intensive | 3 | RF sources: Ion Cyclotron Frequency (FS) | Plasma heating, current drive, wall conditioning
 | 4 | RF sources: Electron Cyclotron Frequency (FS) | Startup, heating, current drive, instability control
 | 5 | Diagnostic Neutral Beam (BTP ) | Energetic neutral beam in plasma to detect He ash
 | 6 | Power supplies (FS) | Power ITER heating and beam systems
 | 7 | Diagnostics (FS + BTP) | Diagnosing ITER plasma
Technologically challenging & Integration intensive | 8 | Cryolines and Cryodistribution (FS) | Cooling some ITER components to sub zero temperatures
Interface & integration intensive | 9 | Cooling water systems (FS) | Removal of heat load from ITER components

## Slide 7
INVOLVEMENT IN ENGINEERING & MANUFACTURING OF ITER COMPONENTS
GOAL: Successful development & on time delivery with desired quality
Most of the components of ITER are first of their kind
Sizes are massive, weights enormous, tolerances tight, quality requirement stringent, performance ultimate
To address to all these prototyping is extremely essential
ITER-India adopted a two-step approach :
STEP - I: Prototype
STEP - II: Bulk Production
- as per ITER-specific standards and then subjecting them all to critical evaluation

## Slide 8
CRYOSTAT
30 m
30 m
Vacuum : 10-6 Torr
3500 tonnes of steel
Largest stainless steel vacuum vessel to be built in the world : 16000 m3 volume
Material used: SS 304, SS 304L dual; Co content <0.1%
JINDAL steel, Industeel (France) & L&T Forging (Hazira)
to limit radiation dose due to neutron and gamma induced radioactivity, (Compliance with nuclear safety requirements)
FUNCTION: JACKET TO ENSURE VACUUM ENVIRONMENT FOR SC MAGNETS

## Slide 9
Challenges:
Welding Tolerance control : 0.3% of the dimension post joining of pieces
Strict flatness control
Special handling of large pieces ~ 100 tons
Special welding techniques
Special jigs and fixtures (to hold the piece while welding and handling) made
Upper Cylinder
Base Section
Lower Cylinder
Top Lid
12 Segments
13 segments including central Lid
12 Segments
13 Segments
CRYOSTAT
Segmented approach

## Slide 10
190mm to 80mm weld joint
Prototypes to ensure ITER requirement
Fixture for major weld
Arrangement to manage distortion at free edges
Top lid mock-up (30 deg.)
Base Section (40 deg.)
CRYOSTAT
Welding across a thickness range of 20–200 mm
Control of weld distortion
Construction heavily dependent on

## Slide 11
An example of full piece assembled from segments
Status
Fabrication Completed
Ongoing Top-lid fabrication
Manufacturing at factory
100% volumetric test for vacuum joints,
100% Helium leak test,
Out gassing test and emissivity test as per ITER requirement performed successfully
Workshop at ITER site
CRYOSTAT

## Slide 12
Lower cylindercompleted in February 2019
Base section complèted in July 2019
Ongoing Upper cylinder sub-assembly
At Workshop
Base Section & Lower Cylinder handed over to IO
CRYOSTAT

## Slide 13: IN WALL SHIELDS
FUNCTION:
Neutron shielding for components situated outside of vacuum vessel (such as magnets) as well as for environmental safety &
Reduce toroidal field ripple
Occupy 55 % of the space between the double walls of the vacuum vessel
Modular structure 9000 blocks made of 72000 borated (1-2% boron) or ferritic steel plates (each 40mm thick)
Reduces toroidal magnetic field ripple as it has high Saturation Magnetization
Provides high neutron shielding due to its high Neutron Capture Cross Section
IWS Blocks
Support Rib + Lower Bracket Assembly
SS316L(N)-IG
9000 blocks are to be assembled for 9 sectors of vacuum vessel & the field joints
These block assemblies use ~ 5,10,000 brackets, spacers, bolts and washers

## Slide 14
Constraints of IWS
Not accessible for maintenance/repair after fabrication of Vacuum Vessel (VV)
These blocks remain immersed in water-passing through double wall of VV
Hence, IWS materials should have high corrosion resistance
Use of powder metallurgy route used to produce SS304B7 by Carpenter Technology for better grain structure and boron distribution
Corrosion study for all IWS materials under simulated operating conditions (200 deg. C, 24 bar pressure, water, 5 weeks)
Magnetic permeability control during component machining (Maximum 1.03)
Vibration test for fastener anti-rotation design validation
Development includes:
IN WALL SHIELDS

## Slide 15
PRESENT STATUS
Expected completion of manufacturing: Mid 2020
IN WALL SHIELDS

## Slide 16: RF Sources: Ion Cyclotron Resonance Frequency
Indian contribution: 9 nos. of RF Source
(8 for plasma operation + 1 spare)
2.5 MW/VSWR 2:1/35-65 MHz/2000s
3.0 MW/VSWR 1.5:1/40-55 MHz/3600s
3MW test loads
Transmission Lines (8)
RF Sources (8+1)
TL to Hot Cell Facility
Movable matching
system
Pre-matching units (2)
Matching units (2)
Antennas (2)
HVPS
(PPTF)
&
Functionality:
Heating
Current drive
Wall conditioning
This kind of RF source is unique in terms of its stringent specifications
ITER require total 20 MW ICRF power to the plasma

## Slide 17: RF Sources: Ion Cyclotron Resonance Frequency
To address major technical issues:
Single chain (R&D) experimentation at 1.5 MW / 2000s / 35 - 65 MHz at VSWR 2:1 launched using Diacrode & Tetrode technologies
No unique amplifier chain able to meet the output power requirement
ITER-India proposed a layout consists of two parallel three-stage amplifier chains + a combiner circuit on the output side

## Slide 18: RF Sources: Ion Cyclotron Resonance Frequency
Phase-I: R&D
Phase-II: Prototype
Phase-III: Bulk Production
  - Stability of combined system during mismatched conditions
  - Identification of final stage tube & critical components
  - Tackling major Interfaces
(single chain experimentation)
(2 chain of amplifiers + Combiner)
Execution plan

## Slide 19: RF Sources: Ion Cyclotron Resonance Frequency
RF input
RF output
Test Rig
Developed dedicated test facility comprises of Low power RF section, SSPA, Controls, High Voltage & Auxiliary Power Supplies,Tx-line system, Test Rig, Cooling etc.
Test Rig: 3MW Dummy Load + Mismatch Tx-line
Tetrode based system
Diacrode based system
RF input
RF output

## Slide 20: RF Sources: Ion Cyclotron Resonance Frequency
Chart: High Power Test on Match Load
| 22 | 43.4 | 63.4 | 73.3
Test@36MHz | 500 | 1008 | 1501 | 1705
Test@45MHz | 503 | 753 | 1000 | 1502
Test@55MHz | 503 | 761 | 1016 | 1271 | 1500
Test@65MHz | 503 | 748 | 1033 | 1503

## Slide 21
3MW ICRF Source is to be tested as per ITER specification at ITER-India lab
2 nos. of 1.5MW amplifier chains combine to achieve the desired power 2.5MW to 3 MW
MW level power combiner developed & tested successfully at ITER-India lab
RF Sources: Ion Cyclotron Resonance Frequency

## Slide 22: RF Sources: Electron Cyclotron Resonance Frequency
Gyrotron Sources
Transmission Lines
Launchers
24x1MW@170GHz
24 corrugated waveguide lines (D:50 mm; L~150m)
1 + 4
Functionality:
To assist plasma start up
Heating
Current drive
Plasma instability control
Requirement: total 20 MW of EC power to ITER plasma
Gyrotron: 24 Nos.
Japan - 8
Russia - 8
Europe - 6
India - 2
Indian contribution to ITER ECRF sources:
2 Gyrotron source sets + Auxiliary Power Supplies & Controls
Nominal RF Frequency | 170 GHz
RF Power | 1 MW
Pulse (Max) | 3600 s
Efficiency |  50 %
Reliability | ≥ 95%
Main Specifications

## Slide 23: Execution Plan
Phase-I
Phase-II
Gyrotron Test Facility Development
to support ITER deliverables
Final Design Review
Procurements for ITER Deliverables
Acceptance Tests, Delivery & Commissioning at ITER site
Establish System Integration & Integrated System Performance
Domestic Preparatory Activity
Activity towards ITER Deliveries
Test Gyrotron + WG components close to ITER specs
IIGTF Layout
Test Gyrotron Setup
Prototype Auxiliaries close to ITER Specs
RF Sources: Electron Cyclotron Resonance Frequency

## Slide 24: RF Sources: Electron Cyclotron Resonance Frequency
High Power Gyrotron Test Facility Layout
Gyrotron RF Beam Diagnostics
Auxiliary Power Supplies
HV (-70kV) Crowbar protection
Fast & reliable data acquisition and control system
Large flow rate Cooling distribution Manifold
~16 m x 16 m
Clear Height > 7.5 m
Test Gyrotron and Waveguide Setup (under procurement)
  Measured Amplitude profiles @ different radial planes
  Re-constructed Amplitude profiles
  Retrieved Amplitude & Phase profiles at the waveguide aperture

## Slide 25
Diagnostics Neutral Beam (DNB)
Challenges
DNB Injector
HNB Injectors (EU – JA procurement)
ITER Tokamak
100 keV, 60 A beam of H-
100 keV, 20 A beam of H0
8 driver based RF negative ion source
~ 60%
To deflect out un-neutralized part
Beam transport ~20.7m from the ion source
Intense physics R&D
Beam source of the largest size,
High precision manufacturing + heavy engineering
Function: measures He ash

## Slide 26
Development of beam technology
Source development:
RF based negative ion source optimization & operation
Material & engineering aspects
Development of material
Similar & dissimilar metal joining
Several precision machining techniques
Source development : Optimizing source & H- beams
Achieved current density ~ 27 mA/cm2, against required 35 mA/cm2
Diagnostics Neutral Beam (DNB)

## Slide 27
Test facility for neutral beam production & transportation at ITER-India lab
Diagnostic neutral beam line: 100 keV, 60 A beam of H-
SS 304 (UHV class)
Top lid openable
Sealing using double O ring seals
Vacuum vessel
(10 m long, 4.5 m dia)
Heavy engineering
Diagnostics Neutral Beam (DNB)

## Slide 28
Aperture zoomed view
Aperture position accuracy: 50 microns
Flatness of the plane 40 microns
Angle accuracy 0.01o
100 KeV 60 A H- ion source for DNB
Four segmented grid – 1280 apertures
Precision Engineering
3 grid beam extractor & accelerator system of ion source need to focus beam at 21 m without much beam loss
Diagnostics Neutral Beam (DNB)

## Slide 29
OFCu – OFCu EBW
OFCu – SS through Ni interface EBW
High heat flux facing components need to maintain strength at elevated temp.
ITER Grade CuCrZr material developed (NFTDC)
Cr : 0.6 – 0.8%; Zr : 0.07% to 0.15% ; Cd : 0.01%; Co : 0.05% ; total impurities not to exceed 0.1%.
Calorimeter
Beam Dump
Materials joining technique
  From similar materials
  Dis-similar materials
Diagnostics Neutral Beam (DNB)

## Slide 30: Power Supplies
Diagnostic Neutral beam
Beam power supply :
10 kV, 140 A (1.4 MW) Extraction PS
90 kV, 70 A (6.3 MW) Acceleration PS
RF generators for ion source
1 MHz, 200 kW each (4 nos.)
8 kV 60 A power supply for the electrostatic RID
RF Systems :
ICRH:
27kV/190A Dual power supply
Driver Stage : 8-18 kV / 20A,
End stage : 27 kV / 170A
ECRH :
55 kV, 110 A
Multi MW power supplies for Diagnostics Neutral Beam and RF systems

## Slide 31: Power Supplies
Several multi-MW power supplies developed to support operations of the RF based plasma heating systems in ITER and the Diagnostic neutral beam system
100 kV, 7.2 MW acceleration system power supplies for ion source manufactured in India and working in Padua Italy on ion source dev. Test bed
Power supplies for DNB system
HVPS for ICRF system
Developed successfully, tested &
operated with ICRF source as per ITER need

## Slide 32
High Power Transmission lines for DNB
Power Supplies

## Slide 33: Diagnostics
The diagnostic package includes India’s participation in
X-Ray Crystal Spectroscopy (XRCS) - Survey & Edge: Real-time monitoring of impurity content in ITER core & edge plasma
Set of spectrometers (X-ray crystals, Detectors, Vacuum chamber), Calibration source, Instrumentation & Control (I&C)
Electron Cyclotron Emission (ECE): measures radiated power in EC frequency range and provides electron temperature profile & temperature fluctuations
Set of Michelson Interferometers & Radiometers, Polarization splitter unit, Transmission line, Calibration source, I&C
Charge eXchange Recombination Spectroscopy (CXRS): measures plasma Ion temperature, Velocity and Impurity density
Optical Fibers, Detectors, Visible Spectrometers, Opto-mechanical components like filters, mounts, I&C
Upper Port- 09 (UP#09): Complex integration with Interspace Support Structure (ISS) & Port Cell Support Structure (PCSS) etc., and customization for CXRS(Edge)

## Slide 34: Diagnostics
Challenge:
Establishing measurement techniques for low loss transmission in ultra wide band frequency range of 70 GHz – 1000 GHz
Mitigation:
Setting up a prototype experiment – transmission and detector (Fourier Transform Spectrometer) in Vacuum to establish attenuation calibration for 8 m long transmission line
Attenuation of 8 m of smooth walled waveguide with two miter bends – establishes the calibration
Chart: Frequency(GHz)

## Slide 35: Cryolines and Cryodistribution System
Used to cool
ITER superconducting magnets; supercritical He @ 4K
Cryostat and thermal shields; forced flow of He @ 80K
Cryosorption pumps; supercritical He @ 4K shielded by He gas @ 80K at different pumping locations
Indian scope: to and fro transport of cryogens to desired locations
5 km long cryolines
5.5 km long warm lines
7 cryodistribution boxes (local storage houses)
Cryoplant
Cryolines + Cryodistribution
Clients
75 kW @ 4.5K LHe; (IO)
1.2 MW @ 80K LN2 (EU)
ITER Cryogenic System:
CRYOLINES
CRYODISTRIBUTION SYSTEM
CRYOPLANT

## Slide 36: Cryolines
Validation of structural and mechanical integrity
Measurement of heat load at 80K and 4.5K
Helium leak tightness tests
Test Objectives
Test Results
All test objectives were fulfilled
All stringent technical & quality requirements were met by both industrial partners
Prototype cryoline 1 (INOX)
Prototype cryoline 2 (ALAT)
DESIGN MANUFACTURING
INSTALLATION
Benefits of prototyping activities (multiple sources and designs) :
Risk mitigated
Performance testing and comparison
Develop industry
State of the art facilities developed in Indian industry
Multi-process Transfer lines with heat in-leaks of
1.2 W/m for 4.5 K and
4.2 W/m for 80 k lines
Prototype: Most complex line with straight, Tee, Elbow & Z sections

## Slide 37: Cryodistribution
Efficiency requirement ≥ 70%
Stringent mass flow rate: ~ 2.7 kg/s at 4.3k with pressure heads <0.5 bar
Reliable, robust design
Should sustain abnormal modes of operation & pulsed heat loads of the ITER machine
Existing cold circulators and ITER requirement
Key Challenges for ITER Cold circulator
Cold circulator
Critical component of Cryodistribution, provides forced flow cooling (SHe) to all cryogenic users
The ITER Cryodistribution System comprises of:
• Five Auxiliary Cold Boxes (ACBs)
• One Cryoplant Termination Cold Box (CTCB)
• One Thermal Shield Cooling System (TSCS) including the respective Warm Panels (WPs)

## Slide 38: Cryodistribution
Resolution
Cold Circulating Pump-1 (IHI)
Performance Qualification Test at Japan Atomic Energy Agency, Japan
Cold Circulating Pump - 1 Results
Cold Circulating Pump-2 (BNI)
Two cold circulators (one from IHI and one from BNI) have been developed & installed in Test Auxiliary Cold Box (TACB)
Integration of TACB system with the 5.0 kW at 4.5 K class cryogenic test facility at Japan
Tested and risk mitigated

## Slide 39: Installation of Cryoline and Cyodistribution System at ITER
Cryo facility at ITER site
Installation of cryolines at ITER site
Cryolines and Warmlines ready for dispatch
CTCB Cold Box internal movement in factory
Cryoplant building
Gas He & LN2 storage tanks
LHe storage tank

## Slide 40: Cryolines installed inside Cryoplant

## Slide 41: Water Cooling System
Water used to remove heat
from the vacuum vessel & its components, and
to cool auxiliary systems such as RF and beam heating & current drive systems, the cryogenic system, the power supply and distribution system etc.
The cooling water system incorporates
multiple closed heat transfer loops (CCWS & CHWS) + an open-loop heat rejection system (HRS).
Heat generated during operation will be transferred through the tokamak cooling water system (TCWS) to the intermediate component cooling water system (CCWS), and to the HRS, which will reject the heat to the environment.
ITER machine is equipped with cooling water system to manage the heat generated during operation of the tokamak

## Slide 42: Water Cooling System
Indian scope includes the following subsystems:
Component Cooling Water System (CCWS) : Provides cooling water at 31oC, specified flow rate, pressure and water quality
Chilled Water System (CHWS) : Provides chilled water at 6oC, specified flow rate and pressure
Heat Rejection System (HRS): Final heat sink. Also stores excess heat during pulse operation and rejects the same during dwell period
Delivery include ~4500 pipe spools upto 2m diameter, in varying lengths and piping geometries,
~ 18 km of piping and ~ 105 inch diameter of welding
The scope of supply includes
10 cells of Cooling Tower: Avg. 510 MW; Peak~1.2 GW
14 Plate type Heat Exchanger: 70 MW each: Possibly at the highest range of design
4MW Chiller: Highest capacity manufactured in India
40 Pumps: different capacity (Max 1.4MW motor capacity)
Extremely high flow rates (>20000 m3/hr) & meeting requirements of low conductivity
Highly interface intensive configuration
Design - Procurement (vendor availability) - Manufacturing - Quality – logistic
Challenges:

## Slide 43: Water Cooling System
Several important components of the cooling water system developed
4MW chiller with requirement of seismic qualification for nuclear site ever manufactured indigenously
Innovative Pipe-in-pipe concept developed to allow thermal expansion in buried network
1.4 MW Motor with strict noise level limit
Flow Splitter to smoothen the flow to vertical pump
Mock-up of basin & pumping arrangement at Kirloskar factory

## Slide 44: Water Cooling System
18 km of piping network manufactured under PED protocol, involves ~ 105 inch diameter of welding & their examination to ensure their correctness
~ 4200 spools delivered, all major components like pumps, chiller, heat exchanger, cooling tower etc. delivered (95% delivery completed)

## Slide 45: Water Cooling System
Pumps delivered by ITER-India being installed at ITER site
Site service building in ITER France houses the chiller systems, pumps, electrical panels and interconnecting piping network delivered by ITER India
Cooling Tower components delivered by ITER-India under assembly at site
Delivered by ITER-India, erected by ITER Organization

## Slide 46
India’s activity on site
Cryostat Workshop
Heat Rejection system
Cryogenic lines
In-Wall Shielding
Diagnostic Neutral Beam
Heating and Current Drive
Slide courtesy : Mr. Laban Coblentz, IO, France

## Slide 47
SUMMARY :
Many components are first of their kind
Technologies involved are complex
Complexity increases manifold by the size, shape, safety and quality requirements
In this journey of development a lot of materials, machining, jointing, electrical, RF, hydraulic and cryogenic areas of engineering have been addressed
Several prototypes have been developed
A lot of facilities in industry have come up and are coming up to become self reliant
Thanks for your kind attention !