## Slide 1
Coordinadora: GI “ASANUM CIENCIA DEL SUELO, ARQUEOMETRIA Y NUEVOS MATERIALES”
Msc. María Luisa Cerón L.
Facultad de Ciencia Físicas
Universidad Nacional Mayor de San Marcos
Laboratorio de Análisis de Suelos y Arqueometría, Facultad de Ciencias Físicas, Universidad Nacional Mayor de San Marcos (UNMSM), Calle Germán Amézaga N° 375, Lima, Perú.

## Slide 2: Mineralogical Characterization of the Serra Pelada Meteorite by Energy Dispersive X Ray Fluorescence and X Ray Diffractometry
Cerón Loayza, María L., Bravo Cabrejos, Jorge A., Montoya Burga, Jenny A., Mori Escobar Fanny E., Tesillo Quispe Mabel E.
Laboratorio de Análisis de Suelo, Facultad de Ciencias Físicas, Universidad Nacional Mayor de San Marcos Ap. Postal 14-0149, Lima 14, Perú.

## Slide 3: I. Abstract
We report the preliminary results about the elemental composition and structural phases of a Serra Pelada meteorite. The Serra Pelada meteorite fell on June 29, 2017 that impacted at Serra Pelada Village (a famous gold mining location) (5º 57.135’S, 49º 39.238’W), located in the State of Pará, northern Brazil. Serra Pelada is a monomict basaltic eucritic breccia and is a normal member of the howardite-eucrite-diogenite (HED) are from the crust asteroid 4 Vesta [1]. We show result by X Ray Fluorescence Energy Dispersive (EDXRF) and X Ray Difractometry (XRD). this was performed with a portable EDXRF AMPTEK instrument.

## Slide 4: II. Methodology
1. The sample was ground in an Agate mortar to be able to analyze it by the technique of Energy Dispersive Ray Fluorescence and X-Ray Difractometry
45m

## Slide 5
III. Techniques Physics Applied
Detector
Fuente de alto voltaje para el tubo de rayos X
Analizador
multicanal
Fuente de poder y
amplificador de pulsos
Muestra
Tubo de RX
It includes the following components:
1. The sample holder with the sample to be irradiated.
2. Continuous and characteristic X-ray source with its respective high voltage source, or a low energy gamma ray source.
3. X-ray detector with its respective power source and a pulse amplifier; each detected X-ray gives rise to an electronic pulse.
4. A multichannel analyzer that records these pulses according to their amplitude, which is linearly related to the energy of the X-ray.
5. A PC with the program that controls the recording of the FRX spectrum.
3.1 X Ray Fluorescence Energy Dispersive (EDXRF)
The equipment used is manufactured by the firm AMPTEK, which is specialized in developing solid state detectors using the Peltier effect to cool the silicon crystal.

## Slide 6
3.2 X Ray Difractometry (XRD)
After data collection, we proceed to the structural identification of the compounds present in the samples, using a Crystallographica-Search Match (CSM) database. Search CSM Macht 1.1, Team LND. Version 2, which is a search program with the PDF databases of the International Center for Diffraction Data (CIDD).
III. Techniques Physics Applied
For the structural analysis of the minerals present in the sample, the XRD technique was applied using a BRUKER diffractometer, model D8-Focus, using CuKα (1.5406 Å) radiation (40 kV, 40 mA) with a vertical goniometer, the scanned angle interval was 4º < 2 < 70º and the 2 advance was 0.02°/step with a time interval of 3 s per step.

## Slide 7
Meteorite Serra Pelada
IV. Result and disscusion
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
Q
T
T
An
An
An
An
An
An
An
Q
An
An
An
An
An
An
An
An
An
An
An
An
An
An
An
An
An
An
An
Au
Au
Au
Au
Au
Au
Au
Au
An
Au
Au
Au
An
Py
Py
Py
Py
Py
Py
Py
Py
Py
Py
Py
Py
Py
O
O
O
O
O
O
Orp
Orp
Orp
Orp
Py
He
He
He
Intensity (a.u.)
2 Theta (°)
We present preliminary result about the characterization of meteorite Serra Pelada .The results pertaining the structural phases found by XRD include mainly anorthite (An), pyroxene (Py), Quartz (Q), Olivine (O), Troilite (T), Orthopyroxene (Orp), Augite (Au) and Hematite (He).

## Slide 8
IV. Result and disscusion
The results obtained through these techniques allow us to find information about a large extraterrestrial impact. The elemental composition analysis shows Si (28%), S (1.2%), Ca (15.8%), Ti (1.7%), Cr (0.8%), Mn (1.7%), Fe (48%), Cu (0.8%), Zn (0.05%), Ga (0.08%), Ge (0.06%), and Au (0.8%).
We observe the presence of the element gold (Au); Au was probably produced by supernova nucleosynthesis or colliding neutron stars, and has been present as dust as other materials merged and differentiated to form the asteroid Vesta.
Meteorite Serra Pelada

## Slide 9
Añay!!