## Slide 1: LIGO India – opportunities for industries
Amit K Srivastava, IPR
On behalf of LIGO India Project team
(IPR, DCSEM, RRCAT, IUCAA)
amit@ipr.res.in
Vigyan Samagam 4-5 Nov 2019

## Slide 2: Introduction
LIGO-India project: Collaborative work between LIGO-US/NSF and DAE/DST.
Objective:
  Setting up a 4 km arm-length Michelson interferometer with Fabry-Perot enhancement to detect gravitational waves – similar to the LIGO design
  function as LIO (like other LIGO observatories LHO, LLO)
To be developed by
  DCSEM: land, civil and infrastructure
  IPR: vacuum system, control and data systems
  RRCAT: optics, lasers, mirrors, suspension, other detector components and related electronics
  IUCAA: data centre for storage and computing, data for science

## Slide 3
Advanced LIGO Detector

## Slide 4: Contents
About the site & schematic representation; civil and infrastructure work
Vacuum system – overview and industrial work requirements
Detector: Laser and Optics
Control and Data System activities
Data Storage and Data Computing
Conclusions

## Slide 5: Contents
About the site & schematic representation; civil and infrastructure work
Vacuum system – overview and industry participation
Detector: Laser and Optics
Control and Data System activities
Data Storage
Conclusions

## Slide 6: Project Site: General Description
The terrain is not flat and requires a levelling at 440 m above MSL.
This requires CUTTING – 1504 x 103 m3; FILLING – 867 x 103 m3
As laser light travels in a straight line, corrections to the earth’s curvature needed
Building vibration due to wind and other external sources to be minimum
Low maintenance building and civil construction
Restriction on use of many chemicals (organic)

## Slide 7: Civil Construction
Corner Station – Laser & Vacuum Equipment Area (LVEA)
End Station – Vacuum Equipment Area (VEA)

## Slide 8: Civil Construction……..

## Slide 9: Infrastructure Development
Beside building construction, other required infrastructure development work:
Electric Power Distribution for building and scientific requirements
Water Supply
Site Communication Equipment and General Computer Networking
Road structure for connectivity
Security and Safety

## Slide 10: Contents
About the site & schematic representation; proposed civil work
Vacuum System – Overview and Industrial Work Requirements
Detector: Laser and Optics
Control and Data System activities
Data Storage and Data Computing
Conclusions

## Slide 11: Vacuum System Overview
BSC | 05 Nos
HAM | 06 Nos.
Cryopump | 04 Nos.
MC Tube | 04 Nos.
Spools and adapters | 85 m
Beam tube | 8 kms
Big Ion pump | 06 Nos
Big Gate valve | 12 Nos.
TMP, Gauges | Several

## Slide 12: Surface area exposed to vacuum
Sl. No. | Vacuum Components | Quantity | Total surface area exposed to vacuum
1 | HAM chamber | 6 | ~35 m2 x 6
2 | BSC chamber | 5 | ~60 m2 x 5
3 | Spool and Adapter |  | ~400 m2 (Corner) ~25 m2 (End)
4 | Mode Cleaner tube | 4 | ~180 m2 x 4
5 | Beam tube | 2 | ~16000 m2 x 2
6 | Baffles |  | ~225 m2
 | TOTAL |  | 34000 m2
    The surface area of steel exposed to vacuum is a source of contamination
    The ultimate vacuum in the detector will be primarily decided by the outgassing rate of constituent species present in the vacuum chamber
    Hydrogen is intrinsic during stainless steel manufacture, hydrogen partial pressure requires continuous monitoring and control
  To attain detector sensitivity, stringent effort to control contamination is required
  LIGO prescribed material for mechanical structure fabrication – SS304L (low hydrogen)

## Slide 13: BSC parts and dimensions
Upper part
Lower part
Parameters | Values (mm )
Inner Diameter | 2654
Upper Part | 
Height | 1994
No. of Nozzles / OD Size | 02 / 356
Lower Part | 
Height | 2823
Connecting flange ID | 2654
End cover ID | 1536
No. of Nozzles /OD Size | 10 / 356 06 / 254 12 / 203
Height : 5.21 m
Inner diameter : 2.65 m
Wall thickness (upper) : 6.35 mm
Wall thickness (lower) : 12.7 mm
Wall thickness (head) : 9.5/6.35 mm
Surface area : 60 m2
Volume : 35 m3
Chamber weight: ≈ 7050Kg
Support weight: ≈ 1000Kg (Carbon steel)
SS304L

## Slide 14: HAM parts and dimensions
2140mm ID Shell
1537mm ID port
Parameters | Values (mm)
Cylindrical Part | 
Inner Diameter | 2140
Length | 1854
No. of Nozzles / OD Size | 01 / 356 04 / 305 06 / 254 10 / 203
Two big Cylindrical Ports | 
Inner Diameter | 1537
No. of Nozzles / OD Size | 02/254
Height : 2.92 m
Inner diameter : 2.14 m
Wall thickness : 12.7 mm
Wall thickness (head) : 9.5/6.35 mm
Surface area : 35 m2
Volume : 10 m3
Chamber weight: ≈ 4500Kg
Support weight: ≈ 600Kg (Carbon steel)
SS304L

## Slide 15: Beam Tube
Length of beam tube : 4 km in each arm
Total length: 8 km
Internal diameter : 1.24 m
Thickness: 3.2 mm (available higher)
Beam tube (each) section length: ≈20 m
Bellows at every 40 m
Prototype development of two 20 m sections joined by a bellow and with cryopump at end is being planned

## Slide 16: Pump and Gauge location
 | Roughing pump | TMP+ scroll pump | Ion pump | Gauges
HAM-1 | 1 (100 m3/hr) | 1 (500 l/s)+1 | 1 (500 l/s) | 1 (pirani, ion)
HAM-6 | 1 (100 m3/hr) | 1 (500 l/s)+1 | 1 (500 l/s) | 1 (pirani, ion)
Annulus pumping of HAM-1 & HAM-6 |  |  | 1 (55 l/s) | 
HAM-2 to long cryopump | 1 (100 m3/hr) | 2 (2000 l/s)+1 | 2 (2500 l/s) | 
HAM-5 to long cryopump | 1 (100 m3/hr) | 2 (2000 l/s)+1 | 2 (2500 l/s) | 
Annulus pumping of HAM-2,3,4,5 & BSC-1,2,3 spools and adapters |  |  | 7+ (55 l/s) | 
80 K cryopump |  |  | 2 (500 l/s) (for initial pumping) | 2 (pirani, ion)
Gate valve annulus at LVEA |  |  | 6 (55 l/s) | 
Pumps at VEA | 2 (X-arm + Y-arm) (100 m3/hr) | 2 (X-arm + Y-arm) (2000 l/s)+1 | 2 (X-arm + Y-arm) (1500 l/s) | 2 (X-arm + Y-arm) (pirani, ion)
Annulus pumping at VEA |  |  | 8 (55 l/s) | 
Beam tube | Roots pump of LVEA will be used for pumping and then shifted to LVEA | 4 (X-arm + Y-arm) (2500 l/s) 16 cryosorption pumps (X-arm+Y-arm) (4000 l/s) | 4 (X-arm +Y-arm at 2 km interval) (2500 l/s) | 16 (X-arm + Y-arm) (pirani, ion)

## Slide 17: QA during manufacturing: Some key issues
LIGO India will be built ~ 6 years
Some activities will be at site – requires QA (trained personnel at site – civil, beam tube, overall installation and commissioning)
Some activities are off site – more reliance on external QA (steel making, bought out items, fabrication)
TPI: Highly trained persons

## Slide 18: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Detector: Laser and Optics
Control and Data System activities
Data Storage and Data Computing
Conclusions

## Slide 19
Test Masses:
40 kg
38 cm in diameter
Polishing: 0.15 nm rms
Coating absorption: 0.5 ppm
LIGO Detector Optics

## Slide 20
Quad Suspension
Design : 4 stage pendulum
Final stage: Monolithic
Mechanical Q : 103
Isolation: factor of 1012
Actuation: electro-magnetic
electrostatic (4th stage)
LIGO Detector Subsystem

## Slide 21
Quad Assembly
The assembly of the four-stage vibration isolation suspension of the core-optics of the detector needs to be developed in India

## Slide 22
Detector 3rd Generation R&D
2 micron laser source development
Silicon optics development
Crystalline coating development at 2 micron
Squeezed light source at 2 micron
At wavelength metrology for Si Optics & coatings
FPGA based digital filters for control loops

## Slide 23: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Detector: Laser and Optics
Control and Data System activities
Data Storage and Data Computing
Conclusions

## Slide 24
Control and Data System

## Slide 25
CDS Functional requirements
Monitoring and Control:
Monitor all detector subsystems
Feedback control of detector system
Physical Environment Monitoring
Vacuum equipment interface and control
Global Control of distributed feedback loops
Data Acquisition for all subsystems:
AI/AO Hardware with supporting software
Timing distribution system
Computing/data processing and networking
Data visualization and analysis tools
Control and Data System (CDS) Infrastructure

## Slide 26
CDS Hardware Overview

## Slide 27
Subsystem-wise Fast Channels: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Per-channel | Channels at that rate |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Per-channel | Total rate
Rate(Hz) | PSL | SUS | ISI | HPI | ALS | ASC |  |  |  | IMC | LSC | OAF | OMC | CAL | TCS | PEM | ODC | TOTAL | Rate (KB/Sec) | (MB/Sec)
65536 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 262.14 | 0
32768 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 131.07 | 0
16384 | 14 | 23 |  |  | 2 |  |  |  |  | 2 | 13 | 2 | 9 | 13 |  | 31 | 4 | 109 | 65.54 | 7.14
8192 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 33 |  | 33 | 32.77 | 1.08
4096 |  |  | 25 |  |  |  |  |  |  |  |  |  |  | 4 |  | 15 |  | 44 | 16.38 | 0.72
2048 |  | 158 | 150 | 22 | 2 | 76 |  |  |  | 47 | 16 |  | 9 |  | 5 | 63 |  | 548 | 8.19 | 4.49
1024 |  | 386 |  | 88 |  |  |  |  |  |  |  |  |  |  |  | 12 |  | 486 | 4.1 | 1.99
512 |  | 277 | 195 | 176 |  | 32 |  |  |  |  |  |  | 2 |  |  |  |  | 682 | 2.05 | 1.4
256 |  | 682 | 2 |  |  |  |  |  |  |  | 4 |  |  | 1 |  | 40 |  | 729 | 1.02 | 0.75
128 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0.51 | 0
Chan/Sys | 14 | 1526 | 372 | 286 | 4 | 108 |  |  |  | 49 | 33 | 2 | 20 | 18 | 5 | 194 | 4 | 2631 |  | 
Rate (MB/sec) | 0.92 | 5.65 | 2.04 | 0.9 | 0.15 | 0.69 |  |  |  | 0.52 | 0.99 | 0.13 | 0.67 | 0.92 | 0.04 | 3.96 | 0.26 | 17.57 |  | 17.57
Overall Channels |  |  |  |  |  |  |  |  | No. of Channels in LLO |  |  | No. of Channels in LHO
Fast channels-IFO stored in DAQ-Science frame |  |  |  |  |  |  |  |  | 2600 |  |  | 2631
Fast channels-IFO stored in DAQ commissioning frame(include science frame) |  |  |  |  |  |  |  |  | 5200 (approx) |  |  | 5400 (approx)
Monitoring channels-IFO including science and commissioning frame-(FEC channels) |  |  |  |  |  |  |  |  | 180154 |  |  | 191201
Monitoring channels-non IFO |  |  |  |  |  |  |  |  | 24568 |  |  | 32587
LIGO Controls Channels: Tentative

## Slide 28
Special Requirements for Controls
Round the clock Continuous operation
Large number of data acquisition and control channels
Distributed supervisory control
Networking and Remote access
System performance and reliability for continuous operation
Ultra High Vacuum Interface
Real-time application development
Component testing and integrated hardware testing
Software development and integration
Data formatting and mass storage

## Slide 29: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Detector: Laser and Optics
Control and Data System activities
Data Storage and Data Computing
Conclusions

## Slide 30
Acquiring, long-term storage, serving to other centres
Data conditioning/ Processing: Calibration, category vetos, cleaning, ..
Data analysis: Production and exploration
Several services (sites, wikis, logbooks, issue tracker, ..)
Numerical Relativity Simulations
Data Management

## Slide 31
Time series data sampled at 16Hz - 16kHz
~ 200k monitoring channels
Expected raw data volume:
~700TB/year/detector
  ~ 3-4 Peta Byte/year from five interferometers
      (LHO, LLO, Virgo, KAGRA, LIGO-India)
“Science channels”: ~ 1% of total data
Data Volume

## Slide 32
153 nodes, 4056 CPU cores
  about 225TF peak performance
  RAM: 5-10GB/core
  storage: 250TB
  10G interconnect
Scope for prototyping GPU based codes: 10 NVIDIA K40 cards
Authentication method: GSI enabled OpenSSH
Building can accommodate infrastructure needed for LIGO-India
LIGO Data Analysis System @ IUCAA

## Slide 33
Tier-1 Data Centre
Ramp up computing infrastructure in stages
  Computing power to more than 1 Peta Flops
  Storage to at least 5 Peta Bytes
  Need may increase by manifold
  But new technology may come to rescue
Also collaborate with other computing facilities
Plans @ IUCAA

## Slide 34
- Will store one copy of the RAW data
  - Will also act as a Disaster Recovery (DR) site
- Provide in-place computing power
  Necessary for calibration and low latency searches
  - Computing power more than 300 Tera Flops
  - Storage more than ~5 Peta Bytes
Plans @ LI Site

## Slide 35
Backbone by National Knowledge Network (NKN)
Data Communication Network

## Slide 36: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Detector: Laser and Optics
Control and Data System activities
Data Storage and Data Computing
Conclusions

## Slide 37: Conclusions
Making a project like LIGO successful - requires
  enormous collaborative R&D
  Strong and effective project management to ensure
    In time delivery
    Within budget
Industry have to be effective partners in this activity
Major Scientific Challenges
  Noise suppression
  Contamination control
  Perfect functioning of support systems
  Operating with a high duty-cycle of the observatory

## Slide 38: Conclusions…..
Industry contribution in different form:
  Development work as routine job
  One time development as specific job that requires prototyping and R&D
  Supply of material: One time and at regular interval
  Maintenance contract work
Major Technical Challenges for industry
  High precision and accuracy
  QA/QC
  Skilled Manpower and advanced manufacturing tools

## Slide 39
Special thanks to all LI project coordinators for sharing information for the presentation.
LIGO Pictures Courtesy: : LIGO-US