## Slide 1
FEM Study of Normal Modes of Gauribidanur Equivalence Principle Apparatus
B S Mallikarjuna
Gravitation Laboratory
Gauribidanur
Annual Meeting - 2018
A Survey of Older Results
+
Some Newer Work

## Slide 2
A few FEM Application areas:
Elasticity problems
Flow of heat
Fluid flows
Magnetic flux problems
FEM is a numerical technique for obtaining approximate solutions to a wide variety of engineering problems.
It is also an efficient design tool.
WHAT IS FINITE ELEMENT METHOD?
Phases of FEM
Pre-Processing
Solution
Post Processing

## Slide 3
The Underlying Mathematical Concept in FEM:
The Physical System being modelled has a Governing Partial Differential Equation (PDE), and this has to be solved subject to specific Boundary Conditions and/or Initial Conditions.
The FEM converts the governing PDE into a set of Algebraic Equations, which are then solved numerically.
A few FEM Advantages:
Accurate representation of complex Geometry
AND complex Boundary Conditions
Ability to include dis-similar material properties
Capture of local effects
Visually powerful tool that helps zero-in on “problem areas”
(e.g., Dynamically Visualize “Mode Shapes” in Studies of Elastic Systems)

## Slide 4: Why are WE interested in FEM?
We have two main sub systems in the UGL:
i) UHV chamber (with Torsion Balance inside it)
ii) Optical lever (rad/Hz sensitivity)
Concern: Of Utmost Importance to minimize noise disturbances.
Approach: EITHER a) ISOLATE Our System from the ambient
OR b) REDUCE THE RESPONSE of our system to the noise impacting it from the ambient
ISOLATE?  e.g. Use A Vibration Isolation Platform
REDUCE THE RESPONSE?  e.g. Stiffen The Apparatus (displacement response ~ 1/ k ~1/ f2 )
UGL means Underground laboratory; UHV means Ultra High Vacuum

## Slide 5
BUILDING A SOLID MODEL
-- This is the very FIRST stage of the Pre-Processing

## Slide 6
Photograph of the UHV Chamber
“Solid model” of the UHV Chamber

## Slide 7
Front view
Top View
Side View
Autocollimator Support Structure with UHV Chamber
Note: Different scales for different Views

## Slide 8
Front View
Top View
Side View
Autocollimator Support Structure
Note: Different Scales for different Views

## Slide 9
In my seminar last year, I had brought out many matters of principle that one has to be careful with in the use of the FEM.
For shortage of time, I will not enter into all of these at this time. However, I have a detailed poster on display, and would be happy to discuss these aspects with anybody who is interested..
For this talk, I will restrict myself to one issue of principle, which is
The CRITICAL IMPORTANCE of imposing the “Correct” Boundary Conditions while solving such problems.

## Slide 10
Zoomed view of Base Connection
“EFFECT OF BOUNDARY CONDITIONS ON OUTPUT RESULTS”
“Table Mount”

## Slide 11
Freq. of Lowest Mode : 11.1 Hz
Note the Mode Shape!
BOUNDARY CONDITION 1

## Slide 12: BOUNDARY CONDITION 2
Freq. of Lowest Mode: 26.1 Hz
Note the Mode Shape!

## Slide 13
So: by way of exploring this question about “Boundary Conditions”, a small experiment that we did in the recent past. 

## Slide 14
FREQUENCY MEASUREMENTS ON A CANTILEVER BEAM WITH DIFFERENT BOUNDARY CONDITIONS
National Instruments cDAQ Unit,
with 16-bit ADCs
Coil
Magnet
Magnet and Coil-Pickup Scheme

## Slide 15
Cantilever Beam: 34.75x1.5x400mm
Magnet
Coil
Zoomed view of the Actual setup
FREQUENCY MEASUREMENTS ON A CANTILEVER BEAM WITH DIFFERENT BOUNDARY CONDITIONS (Cont….)
Chart: MEASURED Natural Frequency of Our Cantilever (Steel Ruler) as the parameter “n” is varied
| 0 | 25 | 50 | 75 | 100 | 125 | 150
Curve Fit results | 6.815 | 7.23 | 7.81 | 8.875 | 9.86 | 11.3 | 13.03
Line diagram of the setup
Note: “L” = 400 mm always

## Slide 16
Some Results from the Detailed Study of Actual Systems in use in the Gauribidanur Experiment 

## Slide 17
Numerical Study 1 -
“Autocollimator Frame”
(This is the Frame on which the Autocollimator is mounted.
It has to be very rigid because a very high precision instrument is mounted on it – Angular Sensitivity 3 x 10-10 radian.)

## Slide 18
Autocollimator Frame
Mode No. | Frequency in Hz
1 | 12.66
2 | 22.32
3 | 23.68
4 | 24.82
Results:
Numerical Study -1

## Slide 19
Mode-1@ 12.66 Hz Mode-2@ 22.32 Hz
Mode-3@ 23.68 Hz Mode-4@ 24.82 Hz
Mode Shapes are an Important Diagnostic!

## Slide 20
Mode No. | Frequency in Hz
1 | 33.93
2 | 34.96
3 | 48.48
4 | 54.54
Results:
Autocollimator Frame (after stiffening)
Mode No. | Frequency in Hz
1 | 12.66
2 | 22.32
3 | 23.68
4 | 24.82
Results:
Mode No. | Frequency in Hz
1 | 33.93
2 | 34.96
3 | 48.48
4 | 54.54
Results:
Before Stiffening
After Stiffening

## Slide 21
Mode-1 @33.93 Hz Mode-2 @34.96 Hz
Mode-3 @48.48 Hz Mode-4 @54.54 Hz
Mode Shapes after Stiffening

## Slide 22
Numerical Study 2 -
“Table Mount”
(This is a Structure that Elevates the Base Height of the UHV Chamber.
If it lacks Rigidity, the entire UHV Chamber with its internal contents is sitting on a “weak” or “floppy” base.)
Table Mount

## Slide 23: Table Mount
Mode No. | Frequency in Hz
1 | 26.13
2 | 26.13
3 | 42.50
4 | 81.70
Results:
Numerical Study -2
Mode No. | Frequency in Hz
1 | 42.48
2 | 43.18
3 | 60.66
4 | 63.23
Results:
Table Mount AFTER Stiffening

## Slide 24
Numerical Study 3 – “UHV Chamber”
This is the chamber where “Torsion Balance” sits inside.
This UHV Chamber has to be rigid because it is holding a Torsion Balance which has period of about 30min (This shows the delicacy of the system).

## Slide 25
UHV Chamber
Mode No. | Frequency in Hz
1 | 4.39
2 | 4.45
3 | 10.25
4 | 10.39
5 | 11.14
FEM packages demand a LOT of Computational Resource!!
Numerical Study -3
Results from ANSYS Workbench
Computation time taken by
i7 processor machine with 8 core and 32 GB RAM - 6 1/2 hrs
e.g. Autocollimator Frame under
SolidWorks – 1.6 xlements

## Slide 26
Dynamic view of the Mode Shape:

## Slide 27
UHV Chamber
Mode No. | Frequency in Hz
1 | 9.08
2 | 9.19
3 | 12.78
4 | 13.77
5 | 14.09
Results
UHV Chamber after addition of ONE more Boundary Condition
Mode No. | Frequency in Hz
1 | 4.39
2 | 4.45
3 | 10.25
4 | 10.39
5 | 11.14
Results:
Mode No. | Frequency in Hz
1 | 9.08
2 | 9.19
3 | 12.78
4 | 13.77
5 | 14.09
Results:
Before Modification
After Modification
Additional Constraint: All Degrees of Freedom here are “frozen”

## Slide 28
Dynamic View of the Mode Shape AFTER Freezing All DOF at the Top End:

## Slide 29: Immediate Future Plans:
Putting together a more sophisticated computing platform:
Intel Xeon Processor E5-2650 v4 with Intel Server Board S2600CW2R
NVIDIA QUADRO P1000 GPU
Seagate SATA Solid State Drive
DDR4 2400 MHz ECC RAM Modules etc.
ii) Refining the Magnet-Coil pickup system
iii) Working on a Strain-gauge Amplifier System – scalable, compact, and easily deployable

## Slide 30
My work so far  one specific area of application of the FEM: “Elastic Studies of Mechanical Structures”.
General Closing Remarks
However, remember that the Finite Element Method is generally applicable wherever there are Differential Equations to be solved with Complex Boundary or Initial Conditions.
Some other areas where the FEM can be applied:
Astronomy (design of Telescope Structures)
Design of MEMs and NEMs structures (heat design; mechanical properties)
Low Temperature Physics (heat design; vibration isolation..)
Electromagnetic Design (e.g., within INO, for the ICAL..)
Cavity Design for Accelerators
We are now in an era where the FEM will find even wider applicability.
It is almost an inevitable tool for the design and optimization of future experiments!
The Differential Equation to be solved may change but the general principles of solving them with the FEM will remain the same!!
The FEM is already in use in some of these areas within TIFR!!

## Slide 31
Thank you