## Slide 1: LIGO India – opportunities for industries
S Mukherjee - on behalf of LIGO India Project team
(DCSEM, IPR, IUCAA, RRCAT)
Head – LIGO Div, IPR; head.ligodiv@ipr.res.in
Vigyan Samagam – 8-9 May 2019

## Slide 2: Introduction
Guideline – MoU between DAE, DST and NSF of 2016
Objective –
  Setting up a 4 km arm-length Michelson interferometer with Fabry-Perot enhancement to detect gravitational waves – similar to the LIGO design
  function as LIO (similar to LHO, LLO)
To be developed by
  DCSEM – land & civil
  IPR – vacuum & control and data systems
  RRCAT – optics, lasers, mirrors, suspension, detector
  IUCAA – data centre, data for science
Presentation covers the activities under the development phase

## Slide 3: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Control and Data System activities
Data Management
QA during manufacturing; some key issues
Conclusions

## Slide 4: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Control and Data System activities
Data Management
QA during manufacturing; some key issues
Conclusions

## Slide 5: General site description
The terrain is not flat and requires a levelling at 440 m above MSL.
This requires CUTTING – 1504 x 103 m3; FILLING – 867 x 103 m3
As laser light travels in a straight line, corrections to the earth’s curvature needed
Building vibration due to wind and other external sources to be minimum
Low maintenance building, and civil construction
Restriction on use of many chemicals (organic)

## Slide 6: General description
Corner Station – Laser & Vacuum Equipment Area (LVEA)
End Station – Vacuum Equipment Area (VEA)

## Slide 7: General Description

## Slide 8: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Control and Data System activities
Data Management
QA during manufacturing; some key issues
Conclusions

## Slide 9: Vacuum System Overview
BSC | 05 Nos
HAM | 06 Nos.
Cryopump | 04 Nos.
MC Tube | 04 Nos.
Spools and adapters | 85 m
Beam tube | 8 kms
Big Ion pump | 06 Nos
Big Gate valve | 12 Nos.
TMP, Gauges | many

## Slide 10: Total surface area exposed to vacuum
Sl. No. | Vacuum Components | Quantity | Total surface area exposed to vacuum
1 | HAM chamber | 6 | ~35 m2 x 6
2 | BSC chamber | 5 | ~60 m2 x 5
3 | Spool and Adapter |  | ~400 m2 (Corner) ~25 m2 (End)
4 | Mode Cleaner tube | 4 | ~180 m2 x 4
5 | Beam tube | 2 | ~16000 m2 x 2
6 | Baffles |  | ~225 m2
 | TOTAL |  | 34000 m2
    The surface area of steel exposed to vacuum is a source of contamination
    The ultimate vacuum in the detector will be primarily decided by the outgassing rate of constituent species present in the vacuum chamber
    Hydrogen is intrinsic during stainless steel manufacture, hydrogen partial pressure requires continuous monitoring and control
  To attain detector sensitivity, stringent effort to control contamination is required
  LIGO prescribed material – SS304L (low hydrogen)

## Slide 11: BSC parts and dimension details
Upper part
Lower part
Parameters | Values (mm )
Inner Diameter | 2654
Upper Part | 
Height | 1994
No. of Nozzles / OD Size | 02 / 356
Lower Part | 
Height | 2823
Connecting flange ID | 2654
End cover ID | 1536
No. of Nozzles /OD Size | 10 / 356 06 / 254 12 / 203
Height : 5.21 m
Inner diameter : 2.65 m
Wall thickness (upper) : 6.35 mm
Wall thickness (lower) : 12.7 mm
Wall thickness (head) : 9.5/6.35 mm
Surface area : 60 m2
Volume : 35 m3
Chamber weight: ≈ 7050Kg
Support weight: ≈ 1000Kg (Carbon steel)
SS304L

## Slide 12: HAM parts and dimension details
2140mm ID Shell
1537mm ID port
Parameters | Values (mm)
Cylindrical Part | 
Inner Diameter | 2140
Length | 1854
No. of Nozzles / OD Size | 01 / 356 04 / 305 06 / 254 10 / 203
Two big Cylindrical Ports | 
Inner Diameter | 1537
No. of Nozzles / OD Size | 02/254
Height : 2.92 m
Inner diameter : 2.14 m
Wall thickness : 12.7 mm
Wall thickness (head) : 9.5/6.35 mm
Surface area : 35 m2
Volume : 10 m3
Chamber weight: ≈ 4500Kg
Support weight: ≈ 600Kg (Carbon steel)
SS304L

## Slide 13: LIGO detector vacuum components
Length of beam tube : 4 km in each arm
Total length: 8 km
Internal diameter : 1.24 m
Thickness: 3.2 mm (available higher)
Beam tube (each) section length: ≈20 m
Bellows at every 40 m
Prototype development of two 20 m sections joined by a bellow and with cryopump at end is being planned

## Slide 14: Pump and Gauge location
 | Roughing pump | TMP+ scroll pump | Ion pump | Gauges
HAM-1 | 1 (100 m3/hr) | 1 (500 l/s)+1 | 1 (500 l/s) | 1 (pirani, ion)
HAM-6 | 1 (100 m3/hr) | 1 (500 l/s)+1 | 1 (500 l/s) | 1 (pirani, ion)
Annulus pumping of HAM-1 & HAM-6 |  |  | 1 (55 l/s) | 
HAM-2 to long cryopump | 1 (100 m3/hr) | 2 (2000 l/s)+1 | 2 (2500 l/s) | 
HAM-5 to long cryopump | 1 (100 m3/hr) | 2 (2000 l/s)+1 | 2 (2500 l/s) | 
Annulus pumping of HAM-2,3,4,5 & BSC-1,2,3 spools and adapters |  |  | 7+ (55 l/s) | 
80 K cryopump |  |  | 2 (500 l/s) (for initial pumping) | 2 (pirani, ion)
Gate valve annulus at LVEA |  |  | 6 (55 l/s) | 
Pumps at VEA | 2 (X-arm + Y-arm) (100 m3/hr) | 2 (X-arm + Y-arm) (2000 l/s)+1 | 2 (X-arm + Y-arm) (1500 l/s) | 2 (X-arm + Y-arm) (pirani, ion)
Annulus pumping at VEA |  |  | 8 (55 l/s) | 
Beam tube | Roots pump of LVEA will be used for pumping and then shifted to LVEA | 4 (X-arm + Y-arm) (2500 l/s) 16 cryosorption pumps (X-arm+Y-arm) (4000 l/s) | 4 (X-arm +Y-arm at 2 km interval) (2500 l/s) | 16 (X-arm + Y-arm) (pirani, ion)

## Slide 15: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Control and Data System activities
Data Management
QA during manufacturing; some key issues
Conclusions

## Slide 16
LIGO Control Systems

## Slide 17
LIGO DAC Functional requirements
Monitoring and Control:
Monitor all detector subsystems
Feedback control of detector system
Physical Environment Monitoring
Vacuum equipment interface and control
Global Control of distributed feedback loops
Data Acquisition for all subsystems:
AI/AO Hardware with supporting software
Timing distribution system
Computing/data processing and networking
Data visualization and analysis tools
Control and Data System (CDS) Infrastructure

## Slide 18
CDS Hardware Overview

## Slide 19
Subsystem-wise Fast Channels: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Per-channel | Channels at that rate |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Per-channel | Total rate
Rate(Hz) | PSL | SUS | ISI | HPI | ALS | ASC |  |  |  | IMC | LSC | OAF | OMC | CAL | TCS | PEM | ODC | TOTAL | Rate (KB/Sec) | (MB/Sec)
65536 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 262.14 | 0
32768 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 131.07 | 0
16384 | 14 | 23 |  |  | 2 |  |  |  |  | 2 | 13 | 2 | 9 | 13 |  | 31 | 4 | 109 | 65.54 | 7.14
8192 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 33 |  | 33 | 32.77 | 1.08
4096 |  |  | 25 |  |  |  |  |  |  |  |  |  |  | 4 |  | 15 |  | 44 | 16.38 | 0.72
2048 |  | 158 | 150 | 22 | 2 | 76 |  |  |  | 47 | 16 |  | 9 |  | 5 | 63 |  | 548 | 8.19 | 4.49
1024 |  | 386 |  | 88 |  |  |  |  |  |  |  |  |  |  |  | 12 |  | 486 | 4.1 | 1.99
512 |  | 277 | 195 | 176 |  | 32 |  |  |  |  |  |  | 2 |  |  |  |  | 682 | 2.05 | 1.4
256 |  | 682 | 2 |  |  |  |  |  |  |  | 4 |  |  | 1 |  | 40 |  | 729 | 1.02 | 0.75
128 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0.51 | 0
Chan/Sys | 14 | 1526 | 372 | 286 | 4 | 108 |  |  |  | 49 | 33 | 2 | 20 | 18 | 5 | 194 | 4 | 2631 |  | 
Rate (MB/sec) | 0.92 | 5.65 | 2.04 | 0.9 | 0.15 | 0.69 |  |  |  | 0.52 | 0.99 | 0.13 | 0.67 | 0.92 | 0.04 | 3.96 | 0.26 | 17.57 |  | 17.57
Overall Channels |  |  |  |  |  |  |  |  | No. of Channels in LLO |  |  | No. of Channels in LHO
Fast channels-IFO stored in DAQ-Science frame |  |  |  |  |  |  |  |  | 2600 |  |  | 2631
Fast channels-IFO stored in DAQ commissioning frame(include science frame) |  |  |  |  |  |  |  |  | 5200 (approx) |  |  | 5400 (approx)
Monitoring channels-IFO including science and commissioning frame-(FEC channels) |  |  |  |  |  |  |  |  | 180154 |  |  | 191201
Monitoring channels-non IFO |  |  |  |  |  |  |  |  | 24568 |  |  | 32587
LIGO Controls Channels: Tentative

## Slide 20: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Control and Data System activities
Data Management
QA during manufacturing; some key issues
Conclusions

## Slide 21
Data Management
- Primary Purposes
Data management
  Acquiring, storage, archival, serving to other centres
Data conditioning
  Calibration, category vetos, cleaning, ..
Data analysis: Production and exploration
Several services (sites, wikis, logbooks, issue tracker, ..)
Numerical Relativity Simulations

## Slide 22
Data Volume
Time series data sampled at 16Hz - 16kHz
  ~200k monitoring channels
Expected raw data volume: ~700TB/year/detector
  ~3-4 PetaByte/year from five interferometers
      LHO, LLO, Virgo, KAGRA, LIGO-India
“Science channels”: ~1% of total data

## Slide 23
LDAS @ IUCAA
LDAS = LIGO Data Analysis System
153 nodes, 4056 CPU cores
  about 225TF peak performance
  RAM: 5-10GB/core (total: 25TB)
  storage: 250TB
  10G interconnect
Scope for prototyping GPU based codes: 10 NVIDIA K40 cards
Authentication method: GSI enabled OpenSSH
Building can accommodate infrastructure needed for LIGO-India

## Slide 24
Plans: At IUCAA
Tier-1 Data Centre
Ramp up computing infrastructure in stages
Plans till first year of LIGO-India operation (~2025)
  Computing power to more than 1 PetaFlops
  Storage to at least 5 PetaBytes
  Need may increase by manifold
  But new technology may come to rescue
Also collaborate with other computing facilities

## Slide 25
Plans: At LIGO-India Site
Will store one copy of the RAW data
  Will also act as a Disaster Recovery (DR) site
Provide in place computing power
  Provision has been made in civil design
  Necessary for calibration and low latency searches
Plans till first year of LIGO-India operation (~2025)
  Computing power more than 300 TeraFlops
  Storage more than ~5 PetaBytes

## Slide 26
Plans: Network Schematic
Backbone by National Knowledge Network (NKN)

## Slide 27: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Control and Data System activities
Data Management
QA during manufacturing; some key issues
Conclusions

## Slide 28: QA during manufacturing; some key issues
LIGO India will be built ~ 6 years
Some activities will be at site – requires QA (trained personnel at site – civil, beam tube, overall installation and commissioning)
Some activities are off site – more reliance on external QA (steel making, bought out items, fabrication)
Highly trained TPI needed

## Slide 29: Contents
About the site & schematic representation; proposed civil work
Vacuum system – overview and industry participation
Control and Data System activities
Data Management
QA during manufacturing; some key issues
Conclusions

## Slide 30: Conclusions
Making a project like LIGO successful - requires
  enormous collaborative R&D
  Strong and effective project management to ensure
    In time delivery
    Within budget
Industry have to be effective partners in this activity
Major Technical Challenges
  noise suppression
  contamination control
  perfect functioning of support systems
  Operating with a high duty-cycle of the observatory
Thank you for your attention head.ligodiv@ipr.res.in