## Slide 1: Challenging Technology Horizons for Expanding Discovery Space
A. N. Ramaprakash
Associate Programme Director, India TMT
(On behalf of ARIES, IIA, IUCAA & others)

## Slide 2: Mega-Optical and IR Facilities
Three international projects approached Indian communities in 2006-2007
Evaluation process lasted over a year
  Need for participation
  Selection of the most suitable project
  Level of participation and human resources
Community chose TMT for 10% level participation
  Guaranteed in-kind contribution
  Based on segmented technology with Keck heritage
  Smaller group – larger say
  Synergy with existing facilities in the Northern hemisphere
24.5-m GMT
30-m TMT
39-m E-ELT

## Slide 3: India’s Participation
Led by India-TMT consortium
  Aryabhatta Research Institute for Observational Sciences (ARIES), Nainital
  Indian Institute of Astrophysics (IIA), Bengaluru
  Inter-University Center for Astronomy and Astrophysics (IUCAA), Pune
India-TMT Coordination Centre (ITCC) at IIA campus
Funded by DST and DAE
  Mega-Facilities for Basic Science Programme
Other institutes and centres
  CDAC, TIFR, IIST, IISERs, Universities

## Slide 4: India’s Participation Status and Future
2007-2014
  Development of consensus among the scientific community
  Proposal development
  Technology demonstration and Prototype development
  Fund approval by the Union Cabinet – 24th Sept. 2014
  Agreements signed by Union Cabinet Minister for S&T on 2nd Dec. 2014
2015-2019
  Execution of partner work packages
  Civil construction stalled
2019 – 2029/30
  Resume On-site Construction of TMT International Observatory
  Execution of our share of work packages
  Development of human resources and readiness to use the facility
2030 – 2080
  Science Operations

## Slide 5: TMT Collaboration
Delhi 12250 km
Beijing 8470 km
Tokyo 6470 km
Washington, DC 7670 km
Ottawa 7650 km
Mauna Kea
Calif. 4030 km

## Slide 6: Summit of Mauna Kea ~ 4200m above MSL

## Slide 7: Thirty Metre Telescope Project
Highly segmented (492) primary mirror
Three mirror approach
  Flat tertiary mirror allows quick steering of light into a suit of instruments mounted on two Nasmyth focii
Built-in post focal adaptive optics system on one of the Nasmyth platforms
  Exploit diffraction limited resolution
  Enhance sensitivity to 50-60 times of current largest telescopes

## Slide 8: Indian Role
Cash contribution to the project capped at 30%
  To a common pool for common fund, infrastructure etc.
Up to 70% of all partner contributions will be made in in-kind
  Subsystems (h/w and s/w)
  Human resources (b/w)
  Services

## Slide 9: TMT Observatory: Partners Work Share
China: tertiary mirror(M3)
Na GS laser launching
Segments, instruments
Canada: Calotte type dome, AO systems, instruments
Japan:Telescope Structure,
Segment Blanks, segments
instruments
USA: Segments, Polishing, Civil Works,
Integration,instruments
India : M1 Control system, Software, segments
Instruments

## Slide 10: Indian Role

## Slide 11: Edge Sensors
Prototype developed at GOAL, Puducherry
  Precision machined glass blocks, lithography, etching

## Slide 12: Actuators
Prototypes made at Avasarala Technologies Ltd., Bengaluru

## Slide 13: Segment Support Assembly
Prototypes made at Avasarala Technologies, Bengaluru and Godrej & Boyce, Mumbai

## Slide 14: Other work in progress
Hardware
  Primary Mirror Control System
    Industry exploration in progress
  M1, M2 and M3 Coating plant
    Design work to be initiated
Software
  Honeywell, Persistent Systems, Thoughtworks
  Observatory Control System
    Common Software development started – Thoughtworks, Pune
    Initial work with CDAC
  Telescope Control System
    Preliminary design work initiated – Honeywell, Pune

## Slide 15: Primary Mirror Segment Polishing
574 segments of 82 different types
  492 + 82 spares
  1.44 m across corners, 45mm thick
  Aspheric, Off-axis
    Curvature changes from centre to edge
  f/1 near paraboloid primary
Radius of curvature should match to very high precision and good accuracy
Surface roughness <2nm rms with no sub-surface damage
Tight specification on surface figure
India TMT is setting up an optics facility at IIA’s Hosekote campus near Bengaluru

## Slide 16: First Light Instruments

## Slide 17: TMT Global Participants
HIA, Victoria
(IRIS OIWFS)
UH IfA, Hawaii
(MOBIE detector readout electronics)
USTC, Beijing
(MOBIE AGWFS)
NIAOT, Nanjing (MOBIE AGWFS)
DI, Toronto
(IRIS Science, NSCU)
NAOJ/Canon, Tokyo
(IRIS imager, MOBIE cameras)
UCLA/CIT
(IRIS, IRMS)
UCSC, Santa Cruz
(MOBIE)
IIA, Bangalore (IR-GSC)
IUCAA, Pune (IR readout electronics)
CSEM, Neuchatel (IRMS CSU)
TIPC, Beijing
(Cooling)

## Slide 18: Challenges
Globally distributed construction of such a complex and precision equipment
Heterogenous work force
  levels of expertise and exposure
  work cultures
  industry standards
  language (spoken and written)
  time zones
Laws and Regulations
  taxes, duties
  labour
  environment
  health and safety
  intellectual property
  dispute resolution
  ownership
  liabilities

## Slide 19: Challenges
Logistics
  Import, Export Processes
  Packaging
  Shipping
  Insurance
Long duration
  Retention of knowhow and key personnel
  Motivation of workforce
  Changes in technology
  Changes in scientific aspirations and landscape
  Changes in funding support

## Slide 20: TMT Discovery Space – the known unknowns

## Slide 21: Our Universe

## Slide 22: Astonishing future, Fundamental questions
How and when did the universe come into being?
How did galaxies take birth and evolve into what we see today?
What is the large scale structure of this universe?
Is there life anywhere else in this universe?
Is there stuff we can’t see? If so how much?
How do massive blackholes form and evolve?

## Slide 23: Beyond Imagination

## Slide 24: Imagining the knowns
Thank You
Imagining the knowns and discovering the unknowns