## Slide 1: MICRO/NANOELECTRONICS AND ADVANCES: IMPACT ON 21st CENTURY COMMUNICATIONS
Technology Day Special ASET Colloquium, 10th May 2019
Prof. B. S. Sonde

## Slide 2: Micro/Nano electronics
A route to miniaturization in electronics with device feature sizes going down from µm to nm:
Major sector of modern electronics technology
Large share in electronics industry: ~25%
Silicon technology exploited→ Information Age
Delivering products and services of high quality
Keeping productivity engine buzzing for decades
Many new branches initiated: Digital/Optical/RF /IT/Sensors/MEMS, all benefitting society
New industries launched: Design, Technology, Packaging, Testing, Assembly, Applications

## Slide 3: Early developments
Based on silicon- preferred for BJT, MOS, CMOS:
Monolithic ICs using photolithography, oxidation diffusion, epitaxial, metallization &etching steps
IC variety: Analog, Mixed signal, Digital, ASIC/SIC -SSI, MSI, LSI, VLSI (Microchip)
VLSI-A generic term in ICs: Device feature size =<1 µm →few nm, Device density >= 1M → 1B
Moore’s law followed: Microchip device density doubling/year(~1965), but now slowing down
Moore’s law continues to be a predictor for VLSI progress for some more years in the future also!

## Slide 4: VLSI trends in recent decades (1)
MOS/CMOS technology related, driven by Moore’s law from the beginning:
Chip-level density: >1 M, doubling ~ annually
Device size: < 1 µm, decreasing steadily
Device power dissipation: < 1µw → few nw
Chip area: >10 mil2, increasing with functions
Package size: Steadily increasing with complexity
Chip-carrier and packaging, now major issues

## Slide 5: VLSI trends in recent decades (2)
Performance related, year by year:
Operating speed:>100 Mb/s, increasing
I/O connections: Complexity-based, increasing
Flexibility: Increasing, through ASIC route
Testability: Increasing, due to innovative design
Reliability: Increasing, being of monolithic type
Cost/function: Steadily declining
Limits: Microchip power dissipation, cost rising! Also, more I/O connections leading to EMI, delays!

## Slide 6: Some examples of VLSI
Major:
System on Chip (SOC)
Memory: DRAM. SRAM, ROM, EEPROM, NVRAM (Flash)
Logic: µ-processor/controller, DSP, ASIC
Minor:
Analog: Analog Array, RF
Mixed Signal: ADC, DAC, Codec, MEMS, Sensors
Power: Control, HV
Mostly CMOS designs!

## Slide 7: Further miniaturization in VLSI
Three factors observed to be useful for this:
Scaling down of device dimensions/design rule by using lithography
Design innovation at device, circuit, function, algorithm, power dissipation, process levels
Increase in µchip size to include more devices
Typically. in a 3-year period, as observed:
Lithography reduction by X2
Design innovation by X 2
Chip size increase by X 2
Leading to chip density increase by 4 (X4)!

## Slide 8: Lithographic power of shorter wavelengths
Illumination Deep UV(nm) Extreme UV(nm) Wavelength(λ) 248 193 157 13.4
Numerical 0.75 0.25 Aperture(NA)
Process Constant 0.50 0.50
(K1)
Min. Feature 165 128 105 27.0
Size (nm)
[Lithographic resolution= K1.λ /NA]

## Slide 9: Evolution of lithography systems
Illumination Optical Source Resist Wavelength(λ)
248 nm Hg lamp/ Chemically
Excimer laser(Kr F) amplified
193 nm Excimer laser(Ar F) ,, ,,
157 nm Excimer laser (F2) ,, ,,
13.4nm Laser plasma/Synchrotron Improved
Further miniaturization by photolithography and end of Moore’s law?

## Slide 10: VLSI performance-limiting factors
Mainly by four factors listed below:
Fundamental: Minimum energy required to perform the on-chip switching function
Material: Rate of removal of heat generated by power dissipation at the chip level
Technological: Photolithography limitations and inadequacies of Al on-chip interconnects
Economic: Increasing costs for going to e-beam/ X-ray lithography and Cu on-chip interconnects
Finally, replacing silicon by other materials?

## Slide 11: Future of Micro/Nano electronics
Silicon to dominate microchips for at least two more decades, with SOI as supplement
Increase in on-chip density/speed & decrease in power dissipation to continue by CMOS & SOC
Microchips reaching cutting edge of technology with highest chip densities >> system needs
Result: Design gap widening & low density high performance VLSI becoming more attractive
ASICs already pace setters for VLSI progress and this trend expected to continue for many years
On-chip/Off-chip interconnections already at the limits, placing high demands on R&D

## Slide 12
Area | Microchip-based Products/Services
Communications | Digital Transmission, Switching, Networking; Cordless/Mobile Phones; Value Added Services; LOS Micro/mm-wave /Satellite &Optical Communication; Convergence with computers (C&C).
Computers | PCs-Desk top, Lap top, Note book types; Work Stations, Multimedia PCs, Home PCs, PDA, GPS, Internet, IOT.
Consumer | AM/FM/Digital Radio, Digital Audio, CD/Cassette Players; Broadcast/Cable/Satellite TV, ED/HD TV, Digital Camera, Camera phone, Clock, Wrist Watch.
Control & Instrumentation | Robotics, Industrial Control, FMS, Test/ Measuring/ Biomedical / Programmable/Automotive Instrumentation.
Military & Space Systems | Avionics, Military/Space Strategic Products, Command, Control and Communication Systems, Information Displays.
Some applications of VLSI

## Slide 13: Examples of VLSI applications
Both directions cited as examples in good use:
High-end products earlier, leading to low-end:
Satellite-based CCD Camera (1970s) leading to Digital Camera(‘90s), Camera Phone (2000s)
Large Computers & ARPANET (1960s) leading to Home PC, Laptop, Internet(2000s)& IOT(‘10s)
b) Low-end products earlier, leading to high-end:
Electronic Clocks/Watches (1960s) leading to Time/Frequency standards for space use(‘90s)
Bulky TV Colour Picture tubes (1960s) leading to LCD/LED-Flat Panel Colour TV displays (2000s)

## Slide 14: Communications in everyday life
For exchanging information:
Different modes: Person-Person, Person- Machine, Machine-Person, Machine-Machine
Different services: Voice/Non-voice types, Fixed (at home/work), Mobile (on the move)
Different types: Audio/video conferencing, Radio/TV broadcasting, Inter/Intra net, IOT
Different methods: Wire-line, Coax, Wave-guide, Wireless: Terrestrial, Space-based Optical/Photonic: Fiber-optic, Free-space
Used in: Business, industry, education, training, healthcare, library services, entertainment, other, with products & services impacted by microchips!

## Slide 15
To achieve:
Reduced distance between peoples
Better understanding among societies
The world becoming a Global Village
Based on:
Microelectronics as key driving force
Digital, wireless, C&C as main approaches
Photonics as supplement to electronics
Implications:
Microchips used everywhere in 21st century
Humans interacting with microchips more than with other humans every day!
Communications-major gains

## Slide 16
Period | Microelectronics Era | Voice Transmission Developments | Voice Switching Developments | Non-Voice Communication Developments
1950s | Discrete Devices & Circuits | Analog | Electro-Mechanical | 
1960s | Early Integrated Circuits (ICs) | Early Digital | Early Space Division (Electronic) | Low Speed Data
1970s | Large Scale Integration (LSI) | High Speed Digital | Space Division (Electronic) | High Speed Data
1980s | Very LSI (VLSI) | Digital Networking | Time Division (Electronic) | Facsimile, Internet
1990s | Advanced VLSI | Integrated Transmission Networking | Integrated Switching System | Low Definition Image, Broad- band Internet
2000s | Advanced VLSI | Modern Communication | Modern Communication | High Definition Image, Advanced Internet , IOT
Progress in communications

## Slide 17
1
4
16
32
64
128
512
1
2
8
32
KILOBITS PER SECOND
MEGABITS PER SECOND
SECURE
VOICE
IMAGE
PHONE
SLIDE
SHOW
VOICE MAIL
HIGH RESLOUTION
FACSIMILE
CELLULAR
RADIO
VIDEO CONFERENCE
NETWORK
TELEPHONY
MOVIES ON
COMPACT DISC
AUDIO
CONFERENCE
DIGITAL
TELEVISION
MUSIC
PREVIEW
AND
BROADCAST
HDTV
Signal compression in communications

## Slide 18
Information
storage
and Retrieval
Information
Processing /
Conversion
Human intellectual activities
Information Creation
Human intellectual activities
Information Memory
Broadcasting, Transmission , Switching and Networking
Information Generation
Information Storage
Information Transfer
Scope of modern communications
Scope of conventional communications
Information handling functions in C&C

## Slide 19
Electronics versus photonics
in communications
Electrons: Strong Coulomb interaction
Material confines and directs electron flow
Control electronic potential by interfacial charge storage
Switching by electron-electron interaction superior
Photons: No interaction between photons directly;
Interaction via electron-photon in materials
Excellent for transmission
Result:
Electronics better for switching in communications
Photonics better for transmission in communications

## Slide 20: Some questions on further miniaturization >2020
What could be the smallest device size in a silicon microchip?
What could be the min. feature size beyond which X-ray/e-beam lithography attractive?
What is the highest power density that can be sustained in a silicon microchip?
What is the minimum energy required for a logic operation in a microchip?
Answers to these would help understand many major issues on future Micro/Nano electronics