## Slide 1
Performance of prototype ICAL detector module
Neha & Apoorva Bhatt
India-based Neutrino Observatory

## Slide 2
1934 Fermi postulated a theory explaining beta decay as a three body decay (neutrino)
1962 Lederman, Schwartz and Steinberg discovered νµ in an accelerator based experiment
Neutrinos
1914 Chadwick observed continuous energy spectrum
in nuclear beta decay
1930 Pauli proposed a particle to save the principle of energy conservation in beta decays
1956 F. Reines and C. Cowan for the first time experimentally detected e from nuclear reactor
1965 first reported of atmospheric νµ at Kolar Gold Fields in India

## Slide 3
The MNR Experiments, Miyake, Narasimham and Ramanamurthy
KGF Cosmic Ray muon experiments
B V Sreekantan et al Proc Ind Acad Sci 43 (1956) 113
1956 : First experiment by Sreekantan group at depth upto 270m
Geiger counter based telescope measures Cosmic muons intensities at various depth and its angular distributions
1961 : New Series of Cosmic muon Experiments started by TIFR in KGF depths from 270m to 2760m
The MNR group measure flux around 6 different depths and found at 2760m muon flux is attenuated
This led to the observation neutrino at deep underground
S Miyake, V S Narasimham, P V Ramana Murthy Nuovo Cim 32 (1963) 1505; 32 (1963) 1524

## Slide 4: KGF neutrino and proton decay experiments
Collaboration: INDIA , UK and Japan
Proton Decay Experiment
S Miyake, V S Narasimham, P V Ramana Murthy Nuovo Cim 32 (1963) 1505; 32 (1963) 1524
140 ton
Absorber : Iron
Detector : Proportional counter
Neon Flash Tubes
2.5 Lead

## Slide 5
1965 Ray Davis measured solar neutrino flux and found deficit of flux (=> solar neutrino puzzle) This led to the birth of Neutrino oscillations
The neutrino flavour state can be represented as a super-position of mass eigenstate ν1, ν2 and ν3 with mass m1, m2 and m3
Oscillation probability is related to the differences in the mass squared m2ij (m2i - m2j ), L and E.
Various experiments have been conducted using atmospheric, solar, reactor and accelerator neutrinos to measure ∆m212 and ∆m213
However, the sign of ∆m213 is not yet known.
Neutrino Oscillations & Mass Hierarchy

## Slide 6
The independent analysis of the T2K and NOνA data shows a preference towards normal hierarchy.
Additional knowledge can also be gained by studying the atmospheric neutrinos as they offer wide range
of energies and baselines.
Therefore, magnetized Iron CALorimeter was proposed to identify mass hierarchy using atmospheric 
ICAL only
M.M. Devi et al, JHEP 1410, 189 (2014)
ICAL + T2K + NovA
S. Agarwalla et al.
Mass hierarchy of neutrinos – sensitivity of ICAL
40% improvement by hadron
energy information

## Slide 7
1270m
India-based Neutrino Observatory
Underground complex
Study Atmospheric neutrinos
51 kton ICAL
Largest electromagnet
30000 glass RPCs
151 layers of 5.6 cm Fe
ICAL
15 m

## Slide 8
102
106
T. Enqvist et al. NIMA 554 (2005) 286–290
Pyhasalmi underground laboratory
Shallow depth Iron CALorimeter (SICAL)
Can we make the ICAL detector at a shallow depth (100m) i.e SICAL?
Requirements:
A cosmic muon veto detector with an efficiency of 99.99% if placed at a 100 m depth
Challenges:
Achieving the required veto efficiency
Muon induced neutral background
Advantages:
Possibility of a larger size detector
Sufficient cosmic muons for monitoring the RPC detectors
Use the cosmic muons to estimate the magnetic field using muSR

## Slide 9
Small CMV Detector set-up at TIFR
Hut Area ~ 1 m x 1 m
Top: 3 layers of scintillator
Side: 1 layer of scintillator
Trigger setup : 4 layer of scintillator
Proof of Principle experiment

## Slide 10
Results
No. of layers at top in HUT | Veto Efficiency (%) 100 ns prompt gates
One | 99.909 ± 0.004
Two | 99.970 ± 0.003
Three | 99.978 ± 0.002
N. Panchal et al. Journal of Instrumentation 12 (2017) T11002
CMVD for mini-ICAL
A bigger Veto detector is already planned for mICAL.
3 layers of PSs.
5 cm wide extruded PS tiles as detector
SiPM as readout.

## Slide 11
µ-induced neutral background for SICAL
Rock
ICAL
VETO
µ
N. Panchal et al. Journal of Instrumentation 14 (2019) P02032
Experiment for SICAL
The experimental verification of the results is required
E-ICAL is planned to be placed at a shallow depth (~30m)
Simulated ~135 days of muon flux in GEANT4
2 false positive events
µ crosses CMV undetected
Neutral particle event mimicking ν events in ICAL
Gives false positive
0.015/day with an upper bound of 0.05/day at 95% C.L.

## Slide 12
Performance of magnet and measurement of magnetic field (using pickup coils and Hall probes) vs 3D simulation.
Performance of RPC including DC-DC supply, FE electronics in fringe B-field, EMI, closed loop gas system.
Feasibility of (μSR) for information about B-field complementary to sense loop and hall probe data.
Measure Φ (μ+ ), Φ (μ− ) for ∼ 0.5 GeV < E < 1.3 GeV at Madurai (near equator) and compare with simulation.
Proof of principle test of cosmic muon veto detector.
Requirement of a magnet prototype of ICAL

## Slide 13
Iron plate lifting using gantry
Iron plate placing on Pedestal
Water cooled Induction brazing machine
Induction brazing in progress
mICAL magnet assembly
Description | Size
Size of magnet | 4m x 4m x 1.1m
Weight of the magnet | ~ 85 tons
No of Iron detector layers | 11
No of RPC detector layers | 10
No coils | 2
Placement of ‘U’ coils
Gap of 12 mm
‘C’ and ‘U’ section Coils
2 coils, 18 turns each
X-sec 30 X 30 mm2 and 17 mm bore
In-situ brazing of upper “C” and lower “U”
Resistance test < 5uohm
Coil Hydrostatic Pressure test
Holding pressure = 12 bars (1Hr)

## Slide 14
Front End DAQ Module
Trigger System
Low Conductivity Water Cooling system
Magnet Field Measurement
Search Coils
Hall Probes
Closed loop Gas system
HV Power Supply
Run Control Backend and Data Storage
Mini ICAL sub-Systems
1.5kW power unit & mainframe
FPGA
100ps TDC
Ethernet
Side board
Power board
DFE and AFE power Supply
LV Power Supply
12 Channel HV distribution
Compressor
DM water tank
Pump
Purifier
Chiller
Pump
Magnet Power Supply
30V , 1500A
Danfysik
Manual & auto
mode
CAM Software
Power Supply
Trigger logic board
CAU
SRB
8 to 10 µS/cm

## Slide 15
IRON PLATES
GAP 3mm
HALL PROBE STRIP
SEARCH COIL
4m
4m
Magnet Base Raft
COPPER COIL
Magnetic measurement system
(1st ,6th , 11th layer)
Hall probe PCB in the gap
Hall probe PCB strip
Field map from simulation
Field Measurement Systems
Shim for hall probe insertion
At 900 A, 90% of the sensors has 1.3 T
Hall probe varies from 6% to 30% from simulation result

## Slide 16
Search coils for flux measurement
Plate | Average field from simulation (T) | Field measured using search coil (T)
B | 1.23 | 0.96
B1 | 1.31 | 1.4
A | 1.23 | 1.3
D | 1.6 | 1.5
Search coil varies from 4.6% to 28% from the simulation result
Teflon coated copper wires
Analog signal from search coils were amplified & integrated over a period of time to get the field
2 sets of coil were put per layer for redundancy

## Slide 17
17
A journey through RPC road
10 cm  30 cm
30 cm  30 cm
1 m  1 m
2 m  2 m
Now with 200 cm × 200 cm Glass RPC in Avalanche mode

## Slide 18
Resistive materials like glass or bakelite for electrodes
Special paint mixture (developed locally) for semi-resistive coating
Plastic honey-comb laminations used as readout panel
Special plastic films for insulating the readout panels from high voltages
Two modes of operation: Avalanche (R134a:Isobutane:SF6 ::95.2:4.5:0.3) and Streamer (R134a:Isobutane:Ar::56:7:37)
Schematic of an assembled gas volume
Edge spacer
Gas nozzle
Glass spacer
Schematic of RPC

## Slide 19
Close loop gas recirculation
and purification system
RPC Detectors
Storage Tank
Gas 1
Gas 2
Gas 3
Receiver
Tank
Gas Purification

## Slide 20
Front End DAQ Electronics
RPC DAQ
HV Module
NINO
ANUSPARSH
2m X 2m RPC with tray

## Slide 21
DAQ
Electronics
Flow
Diagram

## Slide 22: Installing RPC tray
Insert RPC tray one by one

## Slide 23
Noise rate in presence of magnetic field
Almost no change in noise rate with magnetic field
  RPC and onboard electronics found to work well in the fringe field
Time
900A0A
In three hour current reduces from 900A to 0A

## Slide 24
Noise rate RPC
Noise rate is within the expected limit (<~200Hz) for strips

## Slide 25
Few clean muon trajectories
Bending in X-side due to magnetic field in Y-direction.

## Slide 26
Trigger condition :
At least one strip in Layers -6, 7, 8 & 9 has signal more than Vth
Strip Distribution for RPCs
Expected to be uniform distribution
In practice edge strips have fewer events than those in the middle due to in-situ trigger condition.
Noisy strip, inefficient strips and dead strips can be identified.

## Slide 27
Strip multiplicity in all events
Strip multiplicities is about 1.5
Multiplicity 0 : inefficiency
Multiplicities : 1- ~4, Avalanche signal in RPC
Multiplicities : ~5 - ~20, Streamer mode + Shower signal in RPC
Multiplicities : >20, mainly due to correlated electronic noise
Trigger condition : At least one strip in Layers -6, 7, 8 & 9 has signal more than Vth

## Slide 28
Basic principle to analyse muon data
Fit X-Z/Y-Z trajectory of a muon excluding the layer under study (Lxy)
Extrapolate muon trajectory in the layer Lxy
Calculate extrapolated point in strip co-ordinate (-0.5 to 0.5)
Look for multiplicities as a function of this co-ordinate
Expected single strip hit for trajectory passing through the center (all induced charge in one strip)
Same region, double strip hit, which passed through the boundary; also inefficiency
 |  |  |  |  |  |  |  |  |  |  |  | x |  | 
x | x | x | x | x | x | x | x | x | x | x | x | x | x | x
x |  |  |  |  |  |  |  |  | x | x |  |  |  | 
 |  |  |  |  |  |  |  | x | x |  |  |  |  | 
 |  |  |  |  |  |  | x | x |  |  |  |  |  | 
 |  |  |  |  |  | x |  |  |  |  |  |  |  | x
 |  |  |  |  | x |  |  |  |  |  |  |  |  | 
 |  |  |  | x |  |  |  |  |  |  |  |  |  | 
0.5 0 0.5

## Slide 29
Strip multiplicity (within a strip)
Ensure our alignment correction is working properly
ZERO multiplicity : Inefficiency
0.5 0 0.5
Single strip : while muon passed through the centre of the strip
Double strip : while passed though the boundary of two strip

## Slide 30
Efficiency in different layers
Button spacers are clearly visible
Inefficiency band is due to electronics associated with strip(s)
Inefficiency areas are due to improper graphite coating and/or larger gap

## Slide 31
Position resolution for multiplicity 1, 2, 3 & 4
Almost independent of multiplicity upto 2, beyond three the resolution is too large due to streamer pulse
Tail is mainly due to large RPC signals (streamer) and inefficient strips/electronics

## Slide 32
Time resolution (in ns) for multiplicity 1, 2, 3 & 4
Almost independent of multiplicity because the time is determined by the avalanche signals.
Asymmetry (particularly in single multiplicity) is due to lower gain. Tail in lower side is due to large signal near button spacers

## Slide 33
First result of cosmic muon spectrum
Measured momentum spectrum of cosmic ray muons is distorted, mainly due to;
finite resolution,
limited trigger acceptance
systematic effects
Using the unfolding technique, the muon momentum spectrum is observed and the results are compared with the CORSIKA model.

## Slide 34
S. Pethuraj et.al JCAP 09 (2017) 021, S. Pethuraj et.al axXiv:1905.00739

## Slide 35
Muon lifetime towards magnetic field measurement
Though estimated lifetime is matched with world average.
µ-
µ+

## Slide 36
mini-ICAL detector with veto scintillator

## Slide 37
Scintillator for muon veto detector
Work by Mamta Jangra, INO Student

## Slide 38
Summary
Magnet design, performance and peripheral systems are validated.
Performance of RPCs, DAQ electronics, gas systems, etc found to be satisfactory (in the fringe field)
Momentum spectrum of the cosmic ray muons is measured
Work in progress for placing 2 RPCs/layer in miniICAL magnet.
Studies of extruded plastic scintillators for cosmic muon veto detectors for mini-ICAL going on.
Plans to build Engineering module at shallow depth.

## Slide 39
Mini-ICAL team members:
BARC: Sourabh Pathak, Sandip Patel, S. Ajith, N.S. Dalal, S.P. Prabhakar, T.S. Sreenivasan, D.N. Badodkar (DRHR), S.P. Srivastava, K.N. Karn, P.I. Hadagali, P.K. Biswas, Alok Tripathi, Sachin Dolas, Prabhat Singh, Vinay Sharma, Sanjay Patil, Suresh Jaiswar (CDM) , R. Rengan, K. Srinivas (CED), S. Achrekar, N. Ayyagiri, A. Behere, V.B. Chandratre, D. Das, A. Jain, N. Kamble, T. Kasbekar, H. Kolla, A.Manna, S. Mohanan, S. Moitra, P.M. Nair, S. Padmini, M. Punna, S.M. Raut, S. Prafulla, S. Sikder, M. Sukhwani (ED), P.S. Shetty,
B. Sivaramakrishna, Mathew Dominic, Shashank Padwal (TSD)
SINP: N.K.Mondal
TIFR: B.S. Acharya, Vishal Asgolkar, Rajkumar Bharathi, Apoorva Bhatt*, Santosh Chavan, S. Dasgupta, V.M. Datar, Upendra Gokhale, Darshana Gonji, S.R. Joshi, Suresh Kalmani, Puneet Kaur, A. Lokapure, G. Majumder, Suryanarayan Mondal*, P. Nagaraj, Neha*, Pathaleswar, S. Pethuraj*, K.C. Ravindran, Mandar Saraf, B. Satyanarayana, Ravindra Shinde, Dipankar Sil, Thoi Salam Singh, N. Sivaramakrishnan, Pavan V., L. Umesh, Suresh Upadhya, Piyush Verma, E. Yuvaraj, Mamta Jangra, Jim John.
VECC: S.K. Thakur, A. Bera, A. Ghosh, Noor Mohamed
Mini-ICAL Design Safety Review Committee of BARC Safety Council for their suggestions
Essar Steel (steel plates), Green & Green (assembly), St. Gobain (RPC gaps), Ferrite India (Pune), BEC (Bhilai), Entech (B’luru) ….
* INO Graduate students
Acknowledgements

## Slide 40: Back Up

## Slide 41
Receiver tank inlet
Storage Tank Outlet
1
2
3
4
Low pressure regulator
Feeder valve
Mass flow controllers
MFC 1,2,3,4
MFC 6
MFC 5
Exhaust
Exhaust
N2 input
Radical Remover
Hygrometer
Molecular Sieves
PT 4
PT 5
PT 6
PT 1
PT 3
Pneumatic Cylinders
PT 2
Gas purifiers
Molecular Sieves
Bypass
Close loop gas recirculation and purification system
Gas Mixing (On-line)
Gas Recirculation
Gas Purification system
Control System (PLC)
RPC stack (this part is outside the gas unit cabinet)
High pressure
Low pressure
Non-return valve

## Slide 42
1 per RPC
20 RPCs
RPCs
1 set per RPC
Front-End (Amplifiers and Discriminators)
1 SRB per 20 RPCs
Signal Router Block
1 GTM
Trigger System
1 per GTM
CAU
A Few Servers
DAQ Servers
1 Switch for all RPCs
Tier-1 N/W Switch
(Not used in this setup)
Tier-2 N/W Switch
From Other Tier-1 Switches
From Other RPCs
From Other SRBs
Pulse Shapers
Rate Scalars
Network Interface
Trigger Primitives
Strip Hit Latch
Multi-hit TDC
Soft-core Processor
Ambient Monitor
From Other RPCs
RPC-DAQ
Trigger
System
Data
Network
Front-End
Back-End
Real Time Clock
Global Signals
RTC
DAQ Electronics Flow Diagram